## Slide 1: 10a. Assembly Language
6.004x Computation Structures
Part 2 – Computer Architecture
Copyright © 2015 MIT EECS

## Slide 2: Beta ISA Summary
Storage:
  Processor: 32 registers (r31 hardwired to 0) and PC
  Main memory: Up to 4 GB, 32-bit words, 32-bit byte addresses, 4-byte-aligned accesses
Instruction formats:
Instruction classes:
  ALU: Two input registers, or register and constant
  Loads and stores: access memory
  Branches, Jumps: change program counter
OPCODE
rc
ra
rb
unused
OPCODE
rc
ra
16-bit signed constant
32 bits

## Slide 3: Programming Languages
Means, to the BETA, Reg[4]  Reg[2] + Reg[3]
opcode
rb
ra
1
0
(unused)
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
1
rc
0
0
0
0
0
0
0
0
0
0
0
32-bit (4-byte) ADD instruction:
We’d rather write in assembly language:
ADD(R2, R3, R4)
a = b + c;
or better yet a high-level language:
0
Today
Coming up

## Slide 4: Assembly Language
Abstracts bit-level representation of instructions and addresses
We’ll learn UASM (“microassembler”), built into BSim
Main elements:
  Values
  Symbols
  Labels (symbols for addresses)
  Macros
Assembler
01101101
11000110
00101111
10110001
.....
Source
text file
Binary
machine
language
Array of bytes
to be loaded
into memory
Symbolic representation of stream of bytes
Notes: CASE CONVENTION:
  uCode instrs: LOWER case
  Beta instrs: UPPER case

## Slide 5: Example UASM Source File
Comments after //, ignored by assembler (also /*…*/)
Symbols are symbolic representations of a constant value (they are NOT variables!)
Labels are symbols for addresses
Macros expand into sequences of bytes
  Most frequently, macros are instructions
  We can use them for other purposes
N = 12 // loop index initial value
ADDC(r31, N, r1) // r1 = loop index
ADDC(r31, 1, r0) // r0 = accumulated product
loop: MUL(r0, r1, r0) // r0 = r0 * r1
SUBC(r1, 1, r1) /* r1 = r1 – 1 */
BNE(r1, loop, r31) // if r1 != 0, NextPC=loop

## Slide 6: How Does It Get Assembled?
Load predefined symbols into a symbol table
Read input line by line
  Add symbols to symbol table as they are defined
  Expand macros, translating symbols to values first
Text input
N = 12
ADDC(r31, N, r1)
ADDC(r31, 1, r0)
loop: MUL(r0, r1, r0)
SUBC(r1, 1, r1)
BNE(r1, loop, r31)
Binary output
Symbol | Value
r0 | 0
r1 | 1
r31 | 31
Symbol table
N
12
110000 00001 11111 00000000 00001100 [0x00]
110000 00000 11111 00000000 00000001 [0x04]
100010 00000 00000 00001 00000000000 [0x08]
loop
8
…
…

## Slide 7: Registers are Predefined Symbols
r0 = 0, …, r31 = 31
Treated like normal symbols:
No “type checking” if you use the wrong opcode…
ADDC(r31, N, r1)
ADDC(31, 12, 1)
110000 00001 11111 00000000 00001100
Substitute symbols with their values
Expand macro
ADDC(r31, r12, r1)
ADDC(31, 12, 1)
Reg[1]  Reg[31] + 12
ADD(r31, N, r1)
ADD(31, 12, 1)
Reg[1]  Reg[31] + Reg[12]

## Slide 8: Labels and Offsets
Label value is the address of a memory location
BEQ/BNE macros compute offset automatically
Labels hide addresses!
Input file
N = 12
ADDC(r31, N, r1)
ADDC(r31, 1, r0)
loop: MUL(r0, r1, r0)
SUBC(r1, 1, r1)
BNE(r1, loop, r31)
Symbol | Value
r0 | 0
r1 | 1
r31 | 31
Symbol table
110000 00001 11111 00000000 00001100 [0x00]
110000 00000 11111 00000000 00000001 [0x04]
100010 00000 00001 00000 00000000000 [0x08]
110001 00001 00001 00000000 00000001 [0x0C]
011101 11111 00001 11111111 11111101 [0x10]
N
12
loop
8
Output file
offset = (label - <addr of BNE/BEQ>)/4 – 1
= (8 – 16)/4 – 1 = -3
…

## Slide 9: Mighty Macroinstructions
// Macro to generate 4 consecutive bytes: .macro consec(n) n n+1 n+2 n+3
// Invocation of above macro: consec(37)
Macros are parameterized abbreviations, or shorthand
⇒ 37 37+1 37+2 37+3 ⇒ 37 38 39 40
Is expanded to
// Assemble into bytes, little-endian:
.macro WORD(x) x%256 (x/256)%256
.macro LONG(x) WORD(x) WORD(x >> 16)
Here are macros for breaking multi-byte data types into byte-sized chunks
Has same effect as:
0xef 0xbe 0xad 0xde
Mem: 0x100 0x101 0x102 0x103
. = 0x100
LONG(0xdeadbeef)
Boy, that’s hard to read. Maybe, those big-endian types do have a point.

## Slide 10: Assembly of Instructions
// Assemble Beta op instructions
.macro betaop(OP,RA,RB,RC) {
.align 4
LONG((OP<<26)+((RC%32)<<21)+((RA%32)<<16)+((RB%32)<<11))
}
OPCODE
RC
RA
RB
UNUSED
OPCODE
RC
RA
16-BIT SIGNED CONSTANT
110000
ADDC = 0x30 =
1000000000000000
-32768 =
01111
15 =
00000
0 =
1000000000000000
00000
01111
110000
“.align 4” ensures instructions will begin on word boundary (i.e., address = 0 mod 4)
For example:
.macro ADDC(RA,C,RC) betaopc(0x30,RA,C,RC)
ADDC(R15, -32768, R0) --> betaopc(0x30,15,-32768,0)
// Assemble Beta opc instructions
.macro betaopc(OP,RA,CC,RC) {
.align 4
LONG((OP<<26)+((RC%32)<<21)+((RA%32)<<16)+(CC % 0x10000))
}
// Assemble Beta branch instructions
.macro betabr(OP,RA,RC,LABEL) betaopc(OP,RA,((LABEL-(.+4))>>2),RC)

## Slide 11: Example Assembly
ADDC(R3,1234,R17)
betaopc(0x30,R3,1234,R17)
expand ADDC macro with RA=R3, C=1234, RC=R17
.align 4
LONG((0x30<<26)+((R17%32)<<21)+((R3%32)<<16)+(1234 % 0x10000))
expand betaopc macro with OP=0x30, RA=R3, CC=1234, RC=R17
WORD(0xC22304D2) WORD(0xC22304D2 >> 16)
expand LONG macro with X=0xC22304D2
0xC22304D2%256 (0xC22304D2/256)%256 WORD(0xC223)
expand first WORD macro with X=0xC22304D2
0xD2 0x04 0xC223%256 (0xC223/256)%256
evaluate expressions, expand second WORD macro with X=0xC223
0xD2 0x04 0x23 0xC2
evaluate expressions

## Slide 12: UASM Macros for Beta Instructions
| BETA Instructions:
.macro ADD(RA,RB,RC) betaop(0x20,RA,RB,RC)
.macro ADDC(RA,C,RC) betaopc(0x30,RA,C,RC)
.macro AND(RA,RB,RC) betaop(0x28,RA,RB,RC)
.macro ANDC(RA,C,RC) betaopc(0x38,RA,C,RC)
.macro MUL(RA,RB,RC) betaop(0x22,RA,RB,RC)
.macro MULC(RA,C,RC) betaopc(0x32,RA,C,RC) • • •
.macro LD(RA,CC,RC) betaopc(0x18,RA,CC,RC)
.macro LD(CC,RC) betaopc(0x18,R31,CC,RC)
.macro ST(RC,CC,RA) betaopc(0x19,RA,CC,RC)
.macro ST(RC,CC) betaopc(0x19,R31,CC,RC) • • •
.macro BEQ(RA,LABEL,RC) betabr(0x1C,RA,RC,LABEL)
.macro BEQ(RA,LABEL) betabr(0x1C,RA,r31,LABEL)
.macro BNE(RA,LABEL,RC) betabr(0x1D,RA,RC,LABEL)
.macro BNE(RA,LABEL) betabr(0x1D,RA,r31,LABEL)
Convenience macros so we don’t have to specify R31…
(defined in beta.uasm)

## Slide 13: Pseudoinstructions
Convenience macros that expand to one or more real instructions
Extend set of operations without adding instructions to the ISA
// Convenience macros so we don’t have to use R31
.macro LD(CC,RC) LD(R31,CC,RC)
.macro ST(RA,CC) ST(RA,CC,R31)
.macro BEQ(RA,LABEL) BEQ(RA,LABEL,R31)
.macro BNE(RA,LABEL) BNE(RA,LABEL,R31)
.macro MOVE(RA,RC) ADD(RA,R31,RC) // Reg[RC] <- Reg[RA]
.macro CMOVE(CC,RC) ADDC(R31,C,RC) // Reg[RC] <- C
.macro COM(RA,RC) XORC(RA,-1,RC) // Reg[RC] <- ~Reg[RA]
.macro NEG(RB,RC) SUB(R31,RB,RC) // Reg[RC] <- -Reg[RB]
.macro NOP() ADD(R31,R31,R31) // do nothing
.macro BR(LABEL) BEQ(R31,LABEL) // always branch
.macro BR(LABEL,RC) BEQ(R31,LABEL,RC) // always branch
.macro CALL(LABEL) BEQ(R31,LABEL,LP) // call subroutine
.macro BF(RA,LABEL,RC) BEQ(RA,LABEL,RC) // 0 is false
.macro BF(RA,LABEL) BEQ(RA,LABEL)
.macro BT(RA,LABEL,RC) BNE(RA,LABEL,RC) // 1 is true
.macro BT(RA,LABEL) BNE(RA,LABEL)
// Multi-instruction sequences
.macro PUSH(RA) ADDC(SP,4,SP) ST(RA,-4,SP)
.macro POP(RA) LD(SP,-4,RA) ADDC(SP,-4,SP)

## Slide 14: Factorial with Pseudoinstructions
N = 12
ADDC(r31, N, r1)
ADDC(r31, 1, r0)
loop: MUL(r0, r1, r0)
SUBC(r1, 1, r1)
BNE(r1, loop, r31)
N = 12
CMOVE(N, r1)
CMOVE(1, r0)
loop: MUL(r0, r1, r0)
SUBC(r1, 1, r1)
BNE(r1, loop)
Before
After

## Slide 15: Raw Data
LONG assembles a 32-bit value
  Variables
  Constants > 16 bits
N: LONG(12)
factN: LONG(0xdeadbeef)
…
Start:
LD(N, r1)
CMOVE(1, r0)
loop: MUL(r0, r1, r0)
SUBC(r1, 1, r1)
BT(r1, loop)
ST(r0, factN)
Symbol | Value
N | 0
factN | 4
Symbol table
…
LD(r31, N, r1)
LD(31, 0, 1)
Reg[1]  Mem[Reg[31] + 0]
 Mem[0]
 12

## Slide 16: UASM Expressions and Layout
Values can be written as expressions
  Assembler evaluates expressions, they are not translated to instructions to compute the value!
The “.” (period) symbol means the next byte address to be filled
  Can read or write to it
  Useful to control data layout or leave empty space (e.g., for arrays)
. = 0x100 // Assemble into 0x100
LONG(0xdeadbeef)
k = . // Symbol “k” has value 0x104
LONG(0x00dec0de)
. = .+16 // Skip 16 bytes
LONG(0xc0ffeeee)
A = 7 + 3 * 0x0cc41
B = A - 3

## Slide 17: Summary: Assembly Language
Low-level language, symbolic representation of sequence of bytes. Abstracts:
  Bit-level representation of instructions
  Addresses
Elements: Values, symbols, labels, macros
Values can be constants or expressions
Symbols are symbolic representations of values
Labels are symbols for addresses
Macros are expanded to byte sequences:
  Instructions
  Pseudoinstructions (translate to 1+ real instructions)
  Raw data
Can control where to assemble with “.” symbol

## Slide 18: Assembly of Instructions
// Assemble Beta op instructions
.macro betaop(OP,RA,RB,RC) {
.align 4
LONG((OP<<26)+((RC%32)<<21)+((RA%32)<<16)+((RB%32)<<11))
}
OPCODE
RC
RA
RB
UNUSED
OPCODE
RC
RA
16-BIT SIGNED CONSTANT
1000000000000000
00000
01111
110000
“.align 4” ensures instructions will begin on word boundary (i.e., address = 0 mod 4)
For example:
.macro ADDC(RA,C,RC) betaopc(0x30,RA,C,RC)
ADDC(R15, -32768, R0) --> betaopc(0x30,15,-32768,0)
// Assemble Beta opc instructions
.macro betaopc(OP,RA,CC,RC) {
.align 4
LONG((OP<<26)+((RC%32)<<21)+((RA%32)<<16)+(CC % 0x10000))
}
// Assemble Beta branch instructions
.macro betabr(OP,RA,RC,LABEL) betaopc(OP,RA,((LABEL-(.+4))>>2),RC)