## Slide 1: 14. Caches & The Memory Hierarchy
6.004x Computation Structures
Part 2 – Computer Architecture
Copyright © 2016 MIT EECS

## Slide 2: Our “Computing Machine”
(PC+4)+4*SXT(C)
ASEL
0
1
Data
Memory
RD
WD
Adr
WE
W
D
S
E
L
0
1
2
WA
Rc: ID[25:21]
0
1
XP
PC
JT
+4
Instruction
Memory
A
D
Rb: ID[15:11]
Ra: ID[20:16]
RA2SEL
Rc: ID[25:21]
+
Register
File
RA1
RA2
RD1
RD2
BSEL
0
1
C: SXT(ID[15:0])
Z
ALU
A
B
JT
WA
WD
WE
ALUFN
Control Logic
Z
ASEL
BSEL
PCSEL
RA2SEL
WDSEL
ALUFN
PC+4
0
1
MWR
0
1
2
3
4
XAdr
ILL
OP
WASEL
WASEL
IRQ
W
E
R
F
WERF
00
PCSEL
OE
MOE
MOE
MWR
ID[31:0]
ID[31:26]
0
1
Reset
RESET
Memory
We need to fetch one instruction each cycle
Ultimately data is loaded from and results stored to memory

## Slide 3: Memory Technologies
Technologies have vastly different tradeoffs between capacity, access latency, bandwidth, energy, and cost
  … and logically, different applications
 | Capacity | Latency | Cost/GB
Register | 1000s of bits | 20 ps | $$$$
SRAM | ~10 KB-10 MB | 1-10 ns | ~$1000
DRAM | ~10 GB | 80 ns | ~$10
Flash* | ~100 GB | 100 us | ~$1
Hard disk* | ~1 TB | 10 ms | ~$0.10
I/O subsystem
Memory Hierarchy
Processor Datapath
* non-volatile (retains contents when powered off)

## Slide 4: Static RAM (SRAM)
Drivers
Sense amplifiers
Address decoder
SRAM cell
Wordlines
(horizontal)
Bitlines
(vertical, two per cell)
8x6 SRAM array
Address
3
Data in
6
Data out
6

## Slide 5: SRAM Cell
6-MOSFET (6T) cell:
  Two CMOS inverters (4 MOSFETs) forming a bistable element
  Two access transistors
6T SRAM Cell
Wordline N
access FETs
bitline
bitline
Vdd
GND
GND
Vdd
Bistable element
(two stable states) stores a single bit
“1”
“0”

## Slide 6: SRAM Read
Drivers precharge all bitlines to Vdd (1), and leave them floating
Address decoder activates one wordline
Each cell in the activated word slowly pulls down one of the bitlines to GND (0)
Sense amplifiers sense change in bitline voltages, producing output data
6T SRAM Cell
wordline
access FETs
bitline
bitline
1
2
3
4
OFFON
1
0
GNDVdd
2
2
t
V(t)
t
V(t)
3
Vdd
Vdd
1

## Slide 7: SRAM Write
Drivers set and hold bitlines to desired values (Vdd and GND for 1, GND and Vdd for 0)
Address decoder activates one wordline
Each cell in word is overpowered by the drivers, stores value
wordline
access FETs
bitline
bitline
1
2
3
OFFON
Vdd
GNDVdd
2
2
Vdd
GND
1
1
3
GND
GND
Vdd
All transistors are carefully sized so that bitline GND overpowers cell Vdd, but bitline Vdd does not overpower cell GND (why?)

## Slide 8: Multiported SRAMs
SRAM so far can do either one read or one write/cycle
  We can do multiple reads and writes with multiple ports by adding one set of wordlines and bitlines per port
Cost/bit? For N ports…
  Wordlines: _____
  Bitlines: _____
  Access FETs: _____
Wires often dominate area  O(N2) area!
2*N
2*N
N

## Slide 9: Summary: SRAMs
Array of k*b cells (k words, b cells per word)
Cell is a bistable element + access transistors
  Analog circuit with carefully sized transistors to allow reads and writes
Read: Precharge bitlines, activate wordline, sense
Write: Drive bitlines, activate wordline, overpower cells
6 MOSFETs/cell… can we do better?
  What’s the minimum number of MOSFETs needed to store a single bit?

## Slide 10: 1T Dynamic RAM (DRAM) Cell
word line
bitline
access FET
C in storage capacitor determined by:
C =
e A
d
more area
better dielectric
thinner film
1T DRAM Cell
VREF
Storage capacitor
Trench capacitors take little area
~20x smaller area than SRAM cell  Denser and cheaper!
Problem: Capacitor leaks charge, must be refreshed periodically (~milliseconds)
Cyferz (CC BY 2.5)
Notes: http://upload.wikimedia.org/wikipedia/en/b/be/DRAM_trench_structure_configuration1_1.svg

## Slide 11: DRAM Writes and Reads
Writes: Drive bitline to Vdd or GND, activate wordline, charge or discharge capacitor
Reads:
  Precharge bitline to Vdd/2
  Activate wordline
  Capacitor and bitline share charge
    If capacitor was discharged, bitline voltage decreases slightly
    If capacitor was charged, bitline voltage increases slightly
  Sense bitline to determine if 0 or 1
  Issue: Reads are destructive! (charge is gone!)
  So, data must be rewritten to cell at end of read
word line
bitline
access FET
1T DRAM Cell
VREF
Storage capacitor

## Slide 12: Summary: DRAM
1T DRAM cell: transistor + capacitor
Smaller than SRAM cell, but destructive reads and capacitors leak charge
DRAM arrays include circuitry to:
  Write word again after every read (to avoid losing data)
  Refresh (read+write) every word periodically
DRAM vs SRAM:
  ~20x denser than SRAM
  ~2-10x slower than SRAM

## Slide 13: Non-Volatile Storage: Flash
Flash Memory: Use “floating gate” transistors to store charge
  Very dense: Multiple bits/transistor, read and written in blocks
  Slow (especially on writes), 10-100 us
  Limited number of writes: charging/discharging the floating gate (writes) requires large voltages that damage transistor
Cyferz (CC BY 2.5)
Electrons here diminish strength of field from control gate ⇒ no inversion ⇒ NFET stays off even when word line is high.
Notes: http://en.wikipedia.org/wiki/File:Flash_cell_structure.svg

## Slide 14: Non-Volatile Storage: Hard Disk
Hard Disk: Rotating magnetic platters + read/write head
  Extremely slow (~10ms): Mechanically move head to position, wait for data to pass underneath head
    ~100MB/s for sequential read/writes
    ~100KB/s for random read/writes
  Cheap
Surachit (CC BY 2.5)
Circular track divided into sectors
Disk head
Notes: http://commons.wikimedia.org/wiki/File:Hard_drive-en.svg

## Slide 15: Summary: Memory Technologies
Different technologies have vastly different tradeoffs
Size is a fundamental limit, even setting cost aside:
  Small + low latency, high bandwidth, low energy, or
  Large + high-latency, low bandwidth, high energy
Can we get the best of both worlds? (large, fast, cheap)
 | Capacity | Latency | Cost/GB
Register | 1000s of bits | 20 ps | $$$$
SRAM | ~10 KB-10 MB | 1-10 ns | ~$1000
DRAM | ~10 GB | 80 ns | ~$10
Flash | ~100 GB | 100 us | ~$1
Hard disk | ~1 TB | 10 ms | ~$0.10

## Slide 16: The Memory Hierarchy
Want large, fast, and cheap memory, but…
  Large memories are slow (even if built with fast components)
  Fast memories are expensive
Idea: Can we use a hierarchal system of memories with different tradeoffs to emulate a large, fast, cheap memory?
FLASH
CPU
SRAM
DRAM
Speed:
Capacity:
Cost:
Fastest
Smallest
Highest
Slowest
Largest
Lowest
Mem
Fast
Large
Cheap
≈
?

## Slide 17: Memory Hierarchy Interface
Approach 1: Expose Hierarchy
  Registers, SRAM, DRAM, Flash, Hard Disk each available as storage alternatives
  Tell programmers: “Use them cleverly”
Approach 2: Hide Hierarchy
  Programming model: Single memory, single address space
  Machine transparently stores data in fast or slow memory, depending on usage patterns
10 GB DRAM
CPU
10 KB SRAM
10 MB SRAM
1 TB Flash/HDD
10 GB DRAM
CPU
100 KB SRAM
1 TB HDD/SSD
L1Cache
Main memory
Swap space
X?

## Slide 18: The Locality Principle
  Keep the most often-used data in a small, fast SRAM (often local to CPU chip)
  Refer to Main Memory only rarely, for remaining data.
Locality of Reference:
Access to address X at time t implies that access to address X+ΔX at time t+Δt becomes more probable as ΔX and Δt approach zero.
  The reason this strategy works: LOCALITY

## Slide 19: Memory Reference Patterns
Dt
time
address
data
stack
code
|S|
D
t
S is the set of locations accessed during Δt.
Working set: a set S which changes slowly wrt access time.
Working set size, |S|

## Slide 20: Caches
Cache: A small, interim storage component that transparently retains (caches) data from recently accessed locations
  Very fast access if data is cached, otherwise accesses slower, larger cache or memory
  Exploits the locality principle
Computer systems often use multiple levels of caches
Caching widely applied beyond hardware (e.g., web caches)

## Slide 21: A Typical Memory Hierarchy
Everything is a cache for something else…
Registers
Level 1 Cache
Level 2 Cache
Level 3 Cache
Main Memory
Flash Drive
Hard Disk
On chip
Other chips
Mechanical devices
On the datapath
Access time | Capacity | Managed By
1 cycle | 1 KB | Software/Compiler
2-4 cycles | 32 KB | Hardware
10 cycles | 256 KB | Hardware
40 cycles | 10 MB | Hardware
200 cycles | 10 GB | Software/OS
10-100us | 100 GB | Software/OS
10ms | 1 TB | Software/OS

## Slide 22: Cache Access
Processor sends address to cache
Two options:
  Cache hit: Data for this address in cache, returned quickly
  Cache miss: Data not in cache
    Fetch data from memory, send it back to processor
    Retain this data in the cache (replacing some other data)
  Processor must deal with variable memory access time
Processor
Cache
Main Memory
0x6004
LD 0x6004
LD 0x6034
DATA
0x6034
DATA
0x6034
DATA

## Slide 23: Cache Metrics
Hit Ratio:
Miss Ratio:
Average Memory Access Time (AMAT):
  Goal of caching is to improve AMAT
  Formula can be applied recursively in multi-level hierarchies:
AMAT = HitTime + MissRatio × MissPenalty

## Slide 24: Example: How High of a Hit Ratio?
What hit ratio do we need to break even? (Main memory only: AMAT = 100)
Processor
Cache
Main Memory
4 cycles
100 cycles
What hit ratio do we need to achieve AMAT = 5 cycles?
100 = 4 + (1 − HR) × 100 ⇒ HR = 4%
5 = 4 + (1 − HR) × 100 ⇒ HR = 99%

## Slide 25: Basic Cache Algorithm
MAIN
MEMORY
CPU
(1-HR)
Tag
Data
A
B
Mem[A]
Mem[B]
Q: How do we “search” the cache?
ON REFERENCE TO Mem[X]:
Look for X among cache tags...
HIT: X = TAG(i) , for some cache line i
  READ: return DATA(i)
  WRITE: change DATA(i); Start Write to Mem(X)
MISS: X not found in TAG of any cache line
  REPLACEMENT SELECTION:
    Select some line k to hold Mem[X] (Allocation)
  READ: Read Mem[X]
      Set TAG(k)=X, DATA(k)=Mem[X]
  WRITE: Start Write to Mem(X)
      Set TAG(k)=X, DATA(k)= new Mem[X]

## Slide 26: Direct-Mapped Caches
00000000000000000000000011101000
Each word in memory maps into a single cache line
Access (for cache with 2W lines):
  Index into cache with W address bits (the index bits)
  Read out valid bit, tag, and data
  If valid bit == 1 and tag matches upper address bits, HIT
Tag (27 bits)
Valid bit
Data (32 bits)
32-bit BYTE address
Index
bits
Tag
bits
Offset bits
=?
HIT
Example: 8-location DM cache (W=3)
0
1
2
3
4
5
6
7

## Slide 27: Example: Direct-Mapped Caches
64-line direct-mapped cache  64 indexes  6 index bits
1
1
0
1
1
1
0x000058
0x000058
0x000058
0x000040
0x000007
0x000058
0xDEADBEEF
0x00000000
0x00000007
0x42424242
0x6FBA2381
0xF7324A32
Tag (24 bits)
Valid bit
Data (32 bits)
0
1
2
3
4
63
…
…
…
Read Mem[0x400C]
HIT, DATA 0x42424242
Part of the address (index bits) is encoded in the location!
Tag + Index bits unambiguously identify the data’s address
0100 0000 0000 1100
TAG: 0x40
INDEX: 0x3
OFFSET: 0x0
Would 0x4008 hit?
INDEX: 0x2 → tag mismatch → miss
What are the addresses of data in indexes 0, 1, and 2?
TAG: 0x58 → 0101 1000 iiii ii00 (substitute line # for iiiiii) → 0x5800, 0x5804, 0x5808

## Slide 28: Block Size
Take advantage of locality: increase block size
  Another advantage: Reduces size of tag memory!
  Potential disadvantage: Fewer blocks in the cache
Tag (26 bits)
Valid bit
Data (4 words, 16 bytes)
Example: 4-block, 16-word DM cache
Index bits: 2 (4 indexes)
Tag bits: 26 (=32-4-2)
Block offset bits: 4 (16 bytes/block)
32-bit BYTE address
0 1 2 3

## Slide 29: Block Size Tradeoffs
Larger block sizes…
  Take advantage of spatial locality
  Incur larger miss penalty since it takes longer to transfer the block into the cache
  Can increase the average hit time and miss rate
Average Access Time (AMAT) = HitTime + MissPenalty*MR
Block Size
Miss Penalty
AMAT
Block Size
Increased miss penalty and miss rate
Miss Ratio
Block Size
Exploits spatial locality
Fewer blocks, compromises locality
~64 bytes

## Slide 30: Direct-Mapped Cache Problem: Conflict Misses
Loop A:
Pgm at 1024, data at 37:
Assume:
1024-line DM cache
Block size = 1 word
Consider looping code, in steady state
Assume WORD, not BYTE, addressing
Word
Address
1024
37
1025
38
1026
39
1024
37
…
Cache
Line index
0
37
1
38
2
39
0
37
Hit/
Miss
HIT
HIT
HIT
HIT
HIT
HIT
HIT
HIT
Inflexible mapping (each address can only be in one cache location)  Conflict misses!
Loop B:
Pgm at 1024, data at 2048:
1024
2048
1025
2049
1026
2050
1024
2048
...
0
0
1
1
2
2
0
0
MISS
MISS
MISS
MISS
MISS
MISS
MISS
MISS

## Slide 31: Fully-Associative Cache
Opposite extreme: Any address can be in any location
  No cache index!
  Flexible (no conflict misses)
  Expensive: Must compare tags of all entries in parallel to find matching one (can do this in hardware, this is called a CAM)
32-bit BYTE address
=?
=?
=?
=?
Tag bits
Offset bits
Tag
Valid bit
Data
…
…
…
…
…
…
0 1 2 3

## Slide 32: N-way Set-Associative Cache
Compromise between direct-mapped and fully associative
  Nomenclature:
    # Rows = # Sets
    # Columns = # Ways
    Set size = #ways = “set associativity” (e.g., 4-way  4 entries/set)
  compare all tags from all ways in parallel
An N-way cache can be seen as:
  N direct-mapped caches in parallel
Direct-mapped and fully-associative are just special cases of N-way set-associative
Tag
Data
Tag
Data
Tag
Data
8 sets
4 ways
Tag
Data
=?
=?
=?
=?

## Slide 33: N-way Set-Associative Cache
k
HIT
DATA TO CPU
INCOMING ADDRESS
=?
=?
=?
i
0
MEM DATA
SET
WAY
Example: 3-way 8-set cache
Tag
Tag
Tag
Data
Data
Data

## Slide 34: “Let me count the ways.”
Dt
time
address
data
stack
code
Potential cache line conflicts during interval Δt
Elizabeth Barrett Browning

## Slide 35: Associativity Tradeoffs
More ways…
  Reduce conflict misses
  Increase hit time
Miss ratio (%)
Cache size (bytes)
Associativity
[H&P: Fig 5.9]
Little additional benefits beyond 4 to 8 ways
Hit Time
Ways
AMAT
Ways
Higher hit time
Lower conflict misses

## Slide 36: Associativity Implies Choices
Issue: Replacement Policy
address
Fully associative
Compare addr with each tag simultaneously
Location A can be stored in any cache line
address
Direct-mapped
Compare addr with only one tag
Location A can be stored in exactly one cache line
N
address
N-way set-associative
Compare addr with N tags simultaneously
Location A can be stored in exactly one set, but in any of the N cache lines belonging to that set

## Slide 37: Replacement Policies
Optimal policy (Belady’s MIN): Replace the block that is accessed furthest in the future
  Requires knowing the future…
Idea: Predict the future from looking at the past
  If a block has not been used recently, it’s often less likely to be accessed in the near future (a locality argument)
Least Recently Used (LRU): Replace the block that was accessed furthest in the past
  Works well in practice
  Need to keep ordered list of N items → N! orderings → O(log2N!) = O(N log2N) “LRU bits” + complex logic
  Caches often implement cheaper approximations of LRU
Other policies:
  First-In, First-Out (least recently replaced)
  Random: Choose a candidate at random
    Not very good, but does not have adversarial access patterns

## Slide 38: Write Policy
Write-through: CPU writes are cached, but also written to main memory immediately (stalling the CPU until write is completed). Memory always holds current contents
  Simple, slow, wastes bandwidth
Write-behind: CPU writes are cached; writes to main memory may be buffered. CPU keeps executing while writes are completed in the background
  Faster, still uses lots of bandwidth
Write-back: CPU writes are cached, but not written to main memory until we replace the block. Memory contents can be “stale”
  Fastest, low bandwidth, more complex
  Commonly implemented in current systems
Notes: dsm: Slide used to say 90% of cache ops are reads. Nope. On systems with wback caches, ~10% of the LLC or mem traffic is typically writes. But that doesn’t mean stores are rare!

## Slide 39: Write-Back
ON REFERENCE TO Mem[X]: Look for X among tags...
HIT: TAG(X) == Tag[i] , for some cache block i
  READ: return Data[i]
  WRITE: change Data[i]; Start Write to Mem[X]
MISS: TAG(X) not found in tag of any cache block that X can map to
  REPLACEMENT SELECTION:
    Select some line k to hold Mem[X]
    Write Back: Write Data[k] to Mem[Address from Tag[k]]
  READ: Read Mem[X]
      Set Tag[k] = TAG(X), Data[k] = Mem[X]
  WRITE: Start Write to Mem[X]
      Set Tag[k] = TAG(X), Data[k] = new Mem[X]

## Slide 40: Write-Back with “Dirty” Bits
ON REFERENCE TO Mem[X]: Look for TAG(X) among tags...
HIT: TAG(X) == Tag[i] , for some cache block i
  READ: return Data[i]
  WRITE: change Data[i] Start Write to Mem[X] D[i]=1
MISS: TAG(X) not found in tag of any cache block that X can map to
  REPLACEMENT SELECTION:
    Select some block k to hold Mem[X]
    If D[k] == 1 (Writeback) Write Data[k] to Mem[Address of Tag[k]]
  READ: Read Mem[X]; Set Tag[k] = TAG(X), Data[k] = Mem[X], D[k]=0
  WRITE: Start Write to Mem[X] D[k]=1
      Set Tag[k] = TAG(X), Data[k] = new Mem[X]
MAIN
MEMORY
CPU
TAG(A)
Mem[A]
TAG(B)
Mem[B]
TAG
DATA
V
1
1
0
0
0
0
0
D
1
0
Add 1 bit per block to record whether block has been written to. Only write back dirty blocks.

## Slide 41: Summary: Cache Tradeoffs
Larger cache size: Lower miss rate, higher hit time
Larger block size: Trade off spatial for temporal locality, higher miss penalty
More associativity (ways): Lower miss rate, higher hit time
More intelligent replacement: Lower miss rate, higher cost
Write policy: Lower bandwidth, more complexity
How to navigate all these dimensions? Simulate different cache organizations on real programs
AMAT = HitTime + MissRatio × MissPenalty