## Slide 1: 1. Basics of Information
6.004x Computation Structures
Part 1 – Digital Circuits
Copyright © 2015 MIT EECS

## Slide 2: What is “Information”?
Information, n. Data communicated or received that resolves uncertainty about a particular fact or circumstance.
The card is a heart
The card is not the Ace of spades
The card is a face card (J, Q, K)
The card is the “suicide king”
Example: you receive some data about a card drawn at random from a 52-card deck. Which of the following data conveys the most information? The least?
# of possibilities remaining
13
51
12
1
Notes: http://commons.wikimedia.org/wiki/File:Poker-sm-222-Kh.png

## Slide 3: Quantifying Information (Claude Shannon, 1948)
Given discrete random variable X
N possible values:
Associated probabilities:
1/pi is proportional to the uncertainty of choice xi.
Information is measured in bits (binary digits) = number of 0/1’s required to encode choice(s)
Information received when learning that choice was xi:
x1, x2, …, xN
p1, p2, …, pN

## Slide 4: Information Conveyed by Data
Common case: Suppose you’re faced with N equally probable choices, and you receive data that narrows it down to M choices. The probability that data would be sent is M∙(1/N) so the amount of information you have received is
Even when data doesn’t resolve all the uncertainty

## Slide 5: Example: Information Content
Examples:
information in one coin flip: N= M= Info content=
card drawn from fresh deck is a heart: N= M= Info content=
roll of 2 dice: N= M= Info content=
.17 bits ???
2
1
log2(2/1) = 1 bit
52
13
log2(52/13) = 2 bits
36
1
log2(36/1) = 5.17

## Slide 6: Probability & Information Content
data | pdata | log2(1/pdata)
a heart |  | 
not the Ace of spades |  | 
a face card (J, Q, K) |  | 
the “suicide king” |  | 
Information content
Shannon’s definition for information content lines up nicely with my intuition: I get more information when the data resolves more uncertainty about the randomly selected card.
13/52
2 bits
51/52
0.028 bits
12/52
2.115 bits
1/52
5.7 bits

## Slide 7: Entropy
In information theory, the entropy H(X) is the average amount of information contained in each piece of data received about the value of X:
Example: X={A, B, C, D}
choicei | pi | log2(1/pi)
“A” | 1/3 | 1.58 bits
“B” | 1/2 | 1 bit
“C” | 1/12 | 3.58 bits
“D” | 1/12 | 3.58 bits
H(X) = (1/3)(1.58) +
(1/2)(1) +
2(1/12)(3.58)
= 1.626 bits

## Slide 8: Meaning of Entropy
Suppose we have a data sequence describing the values of the random variable X.
Urk, this isn’t good 
This is okay, just inefficient
bits
H(X)
Average number of bits used to transmit choice
This is perfect!

## Slide 9: Encodings
An encoding is an unambiguous mapping between bit strings and the set of possible data.
Encoding for each symbol |  |  |  | Encoding for “ABBA”
A | B | C | D | 
00. 01 10 11 00 01 01 00
01 1 000 001 01 1 1 01
0 1 10 11 0 1 1 0
ABBA?
ABC?
ADA?
✗

## Slide 10: Encodings as Binary Trees
B⟷0
A⟷11
C⟷100
D⟷101
It’s helpful to represent an unambiguous encoding as a binary tree with the symbols to be encoded as the leaves. The labels on the path from the root to the leaf give the encoding for that leaf.
Encoding
Binary tree
01111
B
0
A
1
1
D
1
C
0
0
BAA
Notes: https://openclipart.org/detail/9007/sheep-by-johnny_automatic-9007

## Slide 11: Fixed-length Encodings
If all choices are equally likely (or we have no reason to expect otherwise), then a fixed-length code is often used. Such a code will use at least enough bits to represent the information content.
1
0
1
0
1
0
A
B
C
D
All leaves have the same depth!
Examples:
4-bit binary-coded decimal (BCD) digits
7-bit ASCII for printing characters
Fixed-length are often a little inefficient…
Note that the entropy for N equally-probable symbols is
=log2(N)
log2(10)=3.322
log2(94)=6.555

## Slide 12: Encoding Positive Integers
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
It is straightforward to encode positive integers as a sequence of bits. Each bit is assigned a weight. Ordered from right to left, these weights are increasing powers of 2. The value of an N-bit number encoded in this fashion is given by the following formula:
Smallest number: Largest number:
V = 0*211 + 1*210 + 1*29 + …
= 1024 + 512 + 256 +128 + 64 + 16
= 2000
0
2N-1

## Slide 13: Hexademical Notation
Hexadecimal - base 16
0000 - 0 1000 - 8 0001 - 1 1001 - 9 0010 - 2 1010 - A 0011 - 3 1011 - B 0100 - 4 1100 - C 0101 - 5 1101 - D 0110 - 6 1110 - E 0111 - 7 1111 - F
Long strings of binary digits are tedious and error-prone to transcribe, so we usually use a higher-radix notation, choosing the radix so that it’s simple to recover the original bits string.
A popular choice is transcribe numbers in base-16, called hexadecimal, where each group of 4 adjacent bits are representated as a single hexadecimal digit.
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
0
D
7
0b011111010000 = 0x7D0

## Slide 14: Encoding Signed Integers
N bits
“0” for “+”
“1” for “-”
Range: – (2N-1 – 1) to 2N-1 – 1
We use a signed magnitude representation for decimal numbers, encoding the sign of the number (using “+” and “-”) separately from its magnitude (using decimal digits).
We could adopt that approach for binary representations:
But: two representations for 0 (+0, -0) and we’d need different circuitry for addition and subtraction
1 1 1 1 1 1 0 1 0 0 0 0
-2000

## Slide 15: Two’s Complement Encoding
20
21
22
23
…
2N-2
-2N-1
…
…
N bits
“sign bit”
Range: – 2N-1 to 2N-1 – 1
In a two’s complement encoding, the high-order bit of the N-bit representation has negative weight:
Negative numbers have “1” in the high-order bit
Most negative number: 10…0000
Most positive number: 01…1111
If all bits are 1: 11…1111
If all bits are 0: 00…0000
-2N-1
+2N-1 - 1
-1
0

## Slide 16: More Two’s Complement
Let’s see what happens when we add the N-bit values for -1 and 1, keeping an N-bit answer:
11…1111
+00…0001
Just use ordinary binary addition, even when one or both of the operands are negative. 2’s complement is perfect for N-bit arithmetic!
To compute B-A, we’ll just use addition and compute B+(-A). But how do we figure out the representation for -A?
To negate a two’s complement value: bitwise complement and add 1.
0000000
A+(-A) = 0 = 1 + -1
-A = (-1 – A) + 1
= ~A + 1
1
-Ai
~Ai

## Slide 17: Variable-length Encodings
We’d like our encodings to use bits efficiently:
GOAL: When encoding data we’d like to match the length of the encoding to the information content of the data.
On a practical level this means:
  Higher probability → __________ encodings
  Lower probability → __________ encodings
Such encodings are termed variable-length encodings.
shorter
longer

## Slide 18: Example
choicei | pi | encoding
“A” | 1/3 | 11
“B” | 1/2 | 0
“C” | 1/12 | 100
“D” | 1/12 | 101
B
C
D
A
1
0
1
0
1
0
010011011101
Expected length of this encoding:
Expected length for 1000 symbols:
  With fixed-length, 2 bits/symbol = ________ bits
  With variable-length code = ________ bits
  Lower bound (entropy) = ________ bits
Entropy: H(X) = 1.626 bits
High probability,
Less information
Low probability,
More information
B→0
A→11
C→100
D→101
B C A B A D
2000
1667
(2)(1/3) + (1)(1/2) + (3)(1/12)(2) = 1.667 bits
1626

## Slide 19: Huffman’s Algorithm
Given a set of symbols and their probabilities, constructs an optimal variable-length encoding.
Huffman’s Algorithm:
Build subtree using 2 symbols with lowest pi
At each step choose two symbols/subtrees with lowest pi, combine to form new subtree
Result: optimal tree built from the bottom-up
Example:
A=1/3, B=1/2, C=1/12, D=1/12
C
D
1/12
1/12
1
0
1/6
A
1
0
1/3
1/2
B
1
0
1/2

## Slide 20: Can We Do Better?
Huffman’s Algorithm constructed an optimal encoding… does that mean we can’t do better?
To get a more efficient encoding (closer to information content) we need to encode sequences of choices, not just each choice individually. This is the approach taken by most file compression algorithms…
AA=1/9, AB=1/6, AC=1/36, AD=1/36
BA=1/6, BB=1/4, BC=1/24, BD=1/24
CA=1/36, CB=1/24, CC=1/144, CD=1/144
DA=1/36, DB=1/24, DC=1/144, DD=1/144
Using Huffman’s Algorithm on pairs:
Average bits/symbol = 1.646 bits
Lookup “LZW”
on Wikipedia

## Slide 21: Error Detection and Correction
Suppose we wanted to reliably transmit the result of a single coin flip:
“tails”
Heads: “0”
Tails: “1”
Further suppose that during processing a single-bit error occurs, i.e., a single “0” is turned into a “1” or a “1” is turned into a “0”.
0
“heads”
1
Notes: https://openclipart.org/detail/181695/man-on-telephone-by-liftarn-181695
https://openclipart.org/detail/181694/woman-on-telephone-by-liftarn-181694
https://openclipart.org/image/300px/svg_to_png/168991/hand-ok.png
https://openclipart.org/image/300px/svg_to_png/132733/coste.png

## Slide 22: Hamming Distance
HAMMING DISTANCE: The number of positions in which the corresponding digits differ in two encodings of the same length.
0110010
0100110
Differs in 2 positions so Hamming distance is 2…

## Slide 23: Hamming Distance & Bit Errors
The Hamming distance between a valid binary code word and the same code word with a single-bit error is 1.
1
0
“heads”
“tails”
single-bit error
The problem with our simple encoding is that the two valid code words (“0” and “1”) also have a Hamming distance of 1. So, a single-bit error changes a valid code word into another valid code word…

## Slide 24: Single-bit Error Detection
What we need is an encoding where a single-bit error does not produce another valid code word.
“heads”
“tails”
10
01
single-bit error
A parity bit can be added to any length message and is chosen to make the total number of “1” bits even (aka “even parity”). If min HD(code words) = 1, then min HD(code words + parity) = 2.
0
1
0
1

## Slide 25: Parity check = Detect Single-bit errors
To check for a single-bit error (actually any odd number of errors), count the number of 1s in the received message and if it’s odd, there’s been an error. 0 1 1 0 0 1 0 1 0 0 1 1  original word with parity 0 1 1 0 0 0 0 1 0 0 1 1  single-bit error (detected) 0 1 1 0 0 0 1 1 0 0 1 1  2-bit error (not detected)
One can “count” by summing the bits in the word modulo 2 (which is equivalent to XOR’ing the bits together).

## Slide 26: Detecting Multi-bit Errors
111
000
“heads”
“tails”
To detect E errors, we need a minimum Hamming distance of E+1 between code words.
001
100
010
011
101
110
With this encoding, we can detect up to two bit errors. Note that HD(000,111) = 3…

## Slide 27: Single-bit Error Correction
By increasing the Hamming distance between valid code words to 3, we guarantee that the sets of words produced by single-bit errors don’t overlap. So assuming at most one error, we can perform error correction since we can tell what the valid code was before the error happened.
To correct E errors, we need a minimum Hamming distance of 2E+1 between code words.
111
000
001
100
010
011
101
110
“heads”
“tails”
“heads”
“tails”

## Slide 28: Summary
Information resolves uncertainty
Choices equally probable:
  N choices down to M⇒ log2(N/M) bits of information
  use fixed-length encodings
  encoding numbers: 2’s complement signed integers
Choices not equally probable:
  choicei with probability pi ⇒ log2(1/pi) bits of information
  average amount of information = H(X) = ∑pilog2(1/pi)
  use variable-length encodings, Huffman’s algorithm
To detect E-bit errors: Hamming distance > E
To correct E-bit errors: Hamming distance > 2E
Next time:
  encoding information electrically
  the digital abstraction
  combinational devices