## Slide 1: 9. Programmable Machines
6.004x Computation Structures
Part 2 – Computer Architecture
Copyright © 2015 MIT EECS

## Slide 2: Example: Factorial
int a = 1;
int b = N;
do {
a = a * b;
b = b – 1;
} while (b != 0)
C:
factorial(N) = N! = N*(N-1)*…*1
initially: a = 1, b = 5
after iter 1: a = 5, b = 4
after iter 2: a = 20, b = 3
after iter 3: a = 60, b = 2
after iter 4: a = 120, b = 1
after iter 5: a = 120, b = 0
Done!

## Slide 3: Example: Factorial
int a = 1;
int b = N;
do {
a = a * b;
b = b – 1;
} while (b != 0)
C:
factorial(N) = N! = N*(N-1)*…*1
  Helpful to translate into hardware
  D-registers (a, b)
  2-bits of state (start, loop, done)
  Boolean transitions (b’==0, b’!=0)
  Register assignments in states (e.g., a  a * b)
High-level FSM:
start
loop
done
a  1
b  N
a  a * b
b  b - 1
b’!=0
b’==0
a  a
b  b
start: a ← 1, b ← 5
loop: a ← 5, b ← 4
loop: a ← 20, b ← 3
loop: a ← 60, b ← 2
loop: a ← 120, b ← 1
loop: a ← 120, b ← 0
done:

## Slide 4: Datapath for Factorial
Draw registers
Draw combinational circuit for each assignment
Connect to input muxes
start
loop
done
a  1
b  N
a  a * b
b  b - 1
b != 0
b == 0
a  a
b  b
1
32
N
32
0 1 2
waSEL
2
32
0 1 2
wbSEL
2
32
*
32
a
32
b
32
+
-1
32

## Slide 5: Control FSM for Factorial
Draw combinational logic for transition conditions
Implement control FSM:
  States: High-level FSM states
  Inputs: Transition logic outputs
  Outputs: Mux select signals
start
0
loop
1
done
2
a  1
b  N
a  a * b
b  b - 1
b’!=0
b’==0
a  a
b  b
1
N
a
b
0 1 2
0 1 2
waSEL
wbSEL
*
+
-1
==
0
z
z
Control FSM
waSEL
wbSEL
(2 bits)
(2 bits)
S | Z | waSEL | wbSEL | S’
00 | 0 | 10 | 00 | 01
00 | 1 | 10 | 00 | 01
01 | 0 | 01 | 01 | 01
01 | 1 | 01 | 01 | 10
10 | 0 | 00 | 10 | 10
10 | 1 | 00 | 10 | 10

## Slide 6: Control FSM Hardware
A[2:0] | D[5:0]
000 | 10 00 01
001 | 10 00 01
010 | 01 01 01
011 | 01 01 10
100 | 00 10 10
101 | 00 10 10
waSEL
Next state
Current state
IN
2
2
wbSEL
ROM
8 locs x 6 bits
A[0]
A[2:1]
D[1:0]
ROM contents
D[3:2]
D[5:4]

## Slide 7: So Far: Single-Purpose Hardware
Problem Procedure (High-level FSM) Implementation
Systematic way to implement high-level FSM as a datapath + control FSM
  Is this implementation an FSM itself?
  If so, can you draw the truth table?
How should we generalize our approach so we can solve many problems with one set of hardware?
  More storage for operands and results
  A larger repertoire of operations
  General-purpose datapath

## Slide 8: A Simple Programmable Datapath
Each cycle, this datapath:
  Reads two operands (a, b) from 4 registers (R0-R3)
  Performs one operation of +, -, *, NAND on operands
  Optionally writes result to a register
Control FSM:
R0
R1
R2
R3
+
-
*
NAND
==?
z
aSEL
bSEL
wSEL
opSEL
Control FSM
aSEL
bSEL
opSEL
wSEL
z
wEN
wEN
LE
LE
LE
LE
0 1 2 3

## Slide 9: A Control FSM for Factorial
Assume initial register contents:
Control FSM:
loopmul
loop
sub
done
R0 value = 1
R1 value = N
R2 value = -1
R3 value = 0
asel = 0
bsel = 1
opsel = 2 (*)
wen = 1
wsel = 0
asel = 1
bsel = 3
opsel = X
wen = 0
wsel = X
asel = 1
bsel = 2
opsel = 0 (+)
wen = 1
wsel = 1
loopbeq
R0  R0 * R1
R1  R1 + R2
asel = 1
bsel = 3
opsel = X
wen = 0
wsel = X
N! in R0
z == 1
z == 0

## Slide 10: New Problem  New Control FSM
You can solve many more problems with this datapath!
  Exponentiation, division, square root, …
  But nothing that requires more than four registers
By designing a control FSM, we are programming the datapath
Early digital computers were programmed this way!
  ENIAC (1943):
    First general-purpose digital computer
    Programmed by setting huge array of dials and switches
    Reprogramming it took about 3 weeks

## Slide 11
"Eniac" by Unknown - U.S. Army Photo.
Notes: "Eniac" by Unknown - U.S. Army Photo. Licensed under Public Domain via Commons - https://commons.wikimedia.org/wiki/File:Eniac.jpg#/media/File:Eniac.jpg

## Slide 12
U.S. Army Photo.
Notes: https://commons.wikimedia.org/wiki/File:Two_women_operating_ENIAC.gif

## Slide 13: The von Neumann Model
Many approaches to build a general-purpose computer. Almost all modern computers are based on the von Neumann model (John von Neumann, 1945)
Components:
Input/ Output
  Central processing unit: Performs operations on values in registers
  Main memory: Array of W words of N bits each
  Input/output devices to communicate with the outside world
Central Processing Unit
Datapath
Control FSM
status
control
& memory
Main Memory
address
data

## Slide 14: Key Idea: Stored-Program Computer
Express program as a sequence of coded instructions
Memory holds both data and instructions
CPU fetches, interprets, and executes successive instructions of the program
Central
Processing
Unit
Main Memory
instruction
instruction
instruction
data
data
data
op
ra rb
rc
rc ← op(ra,rb)
0xba5eba11
But, how do we know which words hold instructions and which words hold data?

## Slide 15: Anatomy of a von Neumann Computer
registers
operations
Datapath
Internal storage
Control Unit
control
status
…
dest
asel
fn
bsel
status
ALU
PC
1101000111011
• Instructions coded as binary data
• Program Counter or PC: Address of the instruction to be executed
• Logic to translate instructions into control signals for datapath
R1 ←R2+R3
instructions
address
Main Memory
data
address

## Slide 16: Instructions
Instructions are the fundamental unit of work
Each instruction specifies:
  An operation or opcode to be performed
  Source operands and destination for the result
In a von Neumann machine, instructions are executed sequentially
  CPU logically implements this loop:
  By default, the next PC is current PC + size of current instruction unless the instruction says otherwise
Fetch instruction
Decode instruction
Read src operands
Execute
Write dst operand
Compute next PC

## Slide 17: Instruction Set Architecture (ISA)
ISA: The contract between software and hardware
  Functional definition of operations and storage locations
  Precise description of how software can invoke and access them
The ISA is a new layer of abstraction:
  ISA specifies what the hardware provides, not how it’s implemented
  Hides the complexity of CPU implementation
  Enables fast innovation in hardware (no need to change software!)
    8086 (1978): 29 thousand transistors, 5 MHz, 0.33 MIPS
    Pentium 4 (2003): 44 million transistors, 4 GHz, ~5000 MIPS
    Both implement x86 ISA
  Dark side: Commercially successful ISAs last for decades
    Today’s x86 CPUs carry baggage of design decisions from the 70’s

## Slide 18: Instruction Set Architecture Design
Designing an ISA is hard:
  How many operations?
  What types of storage, how much?
  How to encode instructions?
  How to future-proof?
How to decide? Take a quantitative approach
  Take a set of representative benchmark programs
  Evaluate versions of your ISA and implementation with and without feature
  Pick what works best overall (performance, energy, area…)
Corollary: Optimize the common case
Let’s design our own instruction set: the Beta!

## Slide 19: Beta ISA: Storage
PC
CPU State
r0
r1
r2
...
r31
000000....0
32-bit “words”
General Registers
Main Memory
0
1
2
3
(4 bytes)
32-bit “words”
0
31
Up to 232 bytes (4GB of memory) organized as 230 4-byte words
Why separate registers and main memory?
Tradeoff: Size vs speed and energy
r31 hardwired to 0
Each memory word is 32-bits wide, but for historical reasons the β uses byte memory addresses. Since each word contains four 8-bit bytes, addresses of consecutive words differ by 4.
0x00
0x04
0x08
0x0C
0x10
0x12
Address

## Slide 20: Storage Conventions
Variables live in memory
Registers hold temporary values
To operate with memory variables
  Load them
  Compute on them
  Store the results
0x1000:
0x1004:
0x1008:
0x1010:
0x100C:
n
r
x
y
int x, y;
y = x * 37;
R0 ← Mem[0x1008]
R0 ← R0 * 37
Mem[0x100C] ← R0

## Slide 21: Beta ISA: Instructions
Three types of instructions:
  Arithmetic and logical: Perform operations on general registers
  Loads and stores: Move data between general registers and main memory
  Branches: Conditionally change the program counter
All instructions have a fixed length: 32 bits (4 bytes)
  Tradeoff (vs variable-length instructions):
    Simpler decoding logic, next PC is easy to compute
    Larger code size

## Slide 22: Beta ALU Instructions
Example coded instruction: ADD
32-bit hex: 0x80611000
We prefer to write a symbolic representation: ADD(r1,r2,r3)
ADD(ra,rb,rc):
“Add the contents of ra to the contents of rb; store the result in rc”
OPCODE = 100000, encodes ADD
rc=3,
encodes R3 as destination
ra=1, rb=2
encodes R1 and R2 as
source locations
Reg[rc]  Reg[ra] + Reg[rb]
1
0
0
0
0
0
0
0
0
1
1
0
0
0
0
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
unused
OPCODE
rc
ra
rb
unused
Format:
Similar instructions for other ALU operations:
arithmetic: ADD, SUB, MUL, DIV
compare: CMPEQ, CMPLT, CMPLE
boolean: AND, OR, XOR, XNOR
shift: SHL, SHR, SRA

## Slide 23: Implementation Sketch #1
32 registers
operations
…
rc
ra
fn
ALU
0
rb
PC
Now that we have our first set of instructions, we can create a more concrete implementation sketch:
OPCODE
rc
ra
rb
unused
4
+

## Slide 24: Should We Support Constant Operands?
Many programs use small constants frequently
  e.g., our factorial example: 0, 1, -1
  Tradeoff:
    When used, they save registers and instructions
    More opcodes  more complex control logic and datapath
Analyzing operands when running SPEC CPU benchmarks, we find that constant operands appear in
>50% of executed arithmetic instructions
  Loop increments, scaling indicies
>80% of executed compare instructions
  Loop termination condition
>25% of executed load instructions
  Offsets into data structures

## Slide 25: Beta ALU Instructions with Constant
arithmetic: ADDC, SUBC, MULC, DIVC
compare: CMPEQC, CMPLTC, CMPLEC
boolean: ANDC, ORC, XORC, XNORC
shift: SHLC, SHRC, SRAC
Similar instructions for other ALU operations:
Example instruction: ADDC adds register contents and constant:
Symbolic version: ADDC(r1,-3,r3)
“Add the contents of ra to const; store the result in rc”
OPCODE = 110000, encoding ADDC
rc=3,
encoding R3 as destination
ra=1,
encoding R1 as first operand
Reg[rc]  Reg[ra] + sext(const)
16-bit two’s complement constant, encoding -3 as second operand (will be sign-extended to become 32-bit two’s complement operand)
ADDC(ra,const,rc):
1
1
0
0
0
0
0
0
0
1
1
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
Format:
OPCODE
rc
ra
16-bit signed constant

## Slide 26: Implementation Sketch #2
32 registers
operations
…
rc
ra
fn
ALU
0
rb
PC
Next we add the datapath hardware to support small constants as the second ALU operand:
4
+
OPCODE
rc
ra
16-bit signed constant
bsel
sxt(const)

## Slide 27: Beta Load and Store Instructions
LD(ra,const,rc) Reg[rc]  Mem[Reg[ra] + sext(const)]
Load rc with the contents of the memory location
ST(rc,const,ra) Mem[Reg[ra] + sext(const)]  Reg[rc]
Store the contents of rc into the memory location
OPCODE
rc
ra
16-bit signed constant
address
Loads and stores move data between the internal registers and main memory
Address calculation is just like ADDC instruction!
To access memory the CPU has to generate an address. LD and ST compute the address by adding the sign-extended constant to the contents of register ra.
To access a constant address, specify R31 as ra.
To use only a register value as the address, specify a constant of 0.

## Slide 28: Using LD and ST
Variables live in memory
Registers hold temporary values
To operate with memory variables
  Load them
  Compute on them
  Store the results
0x1000:
0x1004:
0x1008:
0x1010:
0x100C:
n
r
x
y
int x, y;
y = x * 37;
R0 ← Mem[0x1008]
R0 ← R0 * 37
Mem[0x100C] ← R0
LD(R31,0x1008,R0)
MULC(R0,37,R0)
ST(R0,0x100C,R31)

## Slide 29: Can We Solve Factorial With ALU Instructions?
No! Recall high-level FSM:
Factorial needs to loop
So far we can only encode sequences of operations on registers
Need a way to change the PC based on data values!
  Called “branching”. If the branch is taken, the PC is changed. If the branch is not taken, keep executing sequentially.
a  a * b
b  b - 1
Conditional
branch
mul
sub
done
loop
b == 0
b != 0
Branch taken
Branch not taken
Branch target

## Slide 30: Beta Branch Instructions
NPC  PC + 4 Reg[rc]  NPC
if (Reg[ra] != 0)
PC  NPC + 4*offset
else
PC  NPC
BNE(ra,offset,rc): Branch if not equal
NPC  PC + 4 Reg[rc]  NPC
if (Reg[ra] == 0)
PC  NPC + 4*offset
else
PC  NPC
BEQ(ra,offset,rc): Branch if equal
“offset” is a SIGNED CONSTANT encoded as part of the instruction!
BEQ or BNE
rc
ra
16-bit signed constant
The Beta’s branch instructions provide a way to conditionally change the PC to point to a nearby location...
... and, optionally, remembering (in Rc) where we came from (useful for procedure calls).
offset = distance in words to branch target, counting from the instruction following the BEQ/BNE. Range: -32768 to +32767.

## Slide 31: Can We Solve Factorial Now?
Remember control FSM for our simple programmable datapath?
Control FSM states  instructions!
  Not the case in general
  Happens here because datapath is similar to basic von Neumann datapath
// Assume r1 = N
ADDC(r31, 1, r0) // r0 = 1
L:MUL(r0, r1, r0) // r0 = r0 * r1
SUBC(r1, 1, r1) // r1 = r1 – 1
BNE(r1, L, r31) // if r1 != 0, run MUL next
// at this point, r0 = N!
int a = 1;
int b = N;
do {
a = a * b;
b = b – 1;
} while (b != 0)
loopmul
loop
sub
done
loopbne
z == 1
z == 0

## Slide 32: Beta JMP Instruction
Branches transfer control to some predetermined destination specified by a constant in the instruction. It will be useful to be able to transfer control to a computed address.
011011
rc
ra
unused
JMP(Ra,Rc): Reg[Rc]  PC + 4
PC  Reg[Ra]
Useful for procedure call return…
…
[0x100] BEQ(R31,sqrt,R28)
…
[0x678] BEQ(R31,sqrt,R28)
…
sqrt:
…
JMP(R28,R31)
R28 = 0x104
R28 = 0x67C
2nd time: PC←0x67C
1st time: PC←0x104

## Slide 33: Beta ISA Summary
Storage:
  Processor: 32 registers (r31 hardwired to 0) and PC
  Main memory: 32-bit byte addresses; each memory access involves a 32-bit word. Since there are 4 bytes/word, all addresses will be a multiple of 4.
Instruction formats:
Instruction types:
  ALU: Two input registers, or register and constant
  Loads and stores
  Branches, Jumps
OPCODE
rc
ra
rb
unused
OPCODE
rc
ra
16-bit signed constant
32 bits