## Slide 1: 21. Parallel Processing
6.004x Computation Structures
Part 3 – Computer Organization
Copyright © 2016 MIT EECS

## Slide 2: Processor Performance
Pipelining lowers tCLK. What about CPI?
CPI = CPIideal + CPIstall
  CPIideal: cycles per instruction if no stall
CPIstall contributors
  Data hazards
  Control hazards: branches, exceptions
  Memory latency: cache misses
CPI
tCLK

## Slide 3: 5-Stage Pipelined Processors
Advantages
  CPIideal is 1 (pipelining)
  Simple, elegant
    Still used in ARM & MIPS processors
Room for improvement
  Upper performance bound is CPI=1
  High-latency instructions not handled well
    1 stage for accesses to large caches or multiplier
    Long clock cycle time
  Unnecessary stalls due to rigid pipeline
    If one instruction stalls, anything behind it stalls
IF
WB
RF
ALU
MEM

## Slide 4: Improving 5-stage Pipeline Performance
Lower tCLK: deeper pipelines
  Overlap more instructions

## Slide 5: Limits to Pipeline Depth
Each pipeline stage introduces some overhead (O)
  Propagation delay of pipeline registers
  Setup and hold times
  Clock skew
  Inequalities in work per stage
    Cannot break up work into stages at arbitrary points
If original tCLK was T, with N stages tCLK is T/N+O
  If N→, speedup = T / (T/N+O) → T/O
    Assuming that CPI stays constant
  Eventually overhead dominates and deeper pipelines have diminishing returns
T
T/N
O
T/N
O

## Slide 6: Improving 5-stage Pipeline Performance
Lower tCLK: deeper pipelines
  Overlap more instructions
Higher CPIideal: wider pipelines
  Each pipeline stage processes multiple instructions
Lower CPIstall: out-of-order execution
  Execute each instruction as soon as its source operands are available
Balance conflicting goals
  Deeper & wider pipelines  more control hazards
  Branch prediction
It all works because of instruction-level parallelism (ILP)

## Slide 7: Instruction Level Parallelism (ILP)
  loop:
  LD(n, r1)
  CMPLT(r31, r1, r2)
  BF(r2, done)
  LD(r, r2) LD(n,r1) LD(n,r4)
  MUL(r1, r2, r3) SUBC(r4, 1, r4)
  ST(r3, r) ST(r4, n) BR(loop)
  done:
Sequential Code
“Safe” Parallel Code
  loop:
  LD(n, r1)
  CMPLT(r31, r1, r2)
  BF(r2, done)
  LD(r, r2)
  LD(n,r1)
  MUL(r1, r2, r3)
  ST(r3, r)
  LD(n,r4)
  SUBC(r4, 1, r4)
  ST(r4, n)
  BR(loop)
done:
These last two can be solved with renaming, i.e., giving each result a unique register name.
Read-after-write
Write-after-write
Write-after-read

## Slide 8: Wider or Superscalar Pipelines
Each stage operates on up to N instructions each clock cycle
  Known as wide or superscalar pipelines
  CPIideal = 1/N
Options (from simpler to harder)
  One integer and one floating-point instruction
  Any N=2 instructions
  Any N=4 instructions
  Any N=? Instructions
    What are the limits?
See http://people.ee.duke.edu/~sorin/ece252/lectures/3-superscalar.pdf

## Slide 9: A Modern Out-of-Order Superscalar Processor
For OoO: determine when operands are ready for inst.
Needed to avoid high CPISTALL on deep pipelines
Make sure side-effects happen in correct order!

## Slide 10: Limits To Single-Processor Performance
Pipeline depth: getting close to pipelining limits
  Clocking overheads, CPI degradation
Branch prediction & memory latency limit the practical benefits of out-of-order execution
Power grows superlinearly with higher frequency & more OoO logic
Extreme design complexity
Limited ILP  Must exploit DLP and TLP
  Data-Level Parallelism: Vector extensions, GPUs
  Thread-Level Parallelism: Multiple threads and cores

## Slide 11: Data-Level Parallelism
Same operation applied to multiple data elements
Exploit with vector processors or vector ISA extensions
        Each datapath has its own local storage (register file)
        All datapaths execute the same instruction
        Memory access with vector loads and stores + wide memory port
Reg File
ALU
PC
+1 or Branch
Reg File
ALU
Reg File
ALU
Reg File
ALU
Data
Memory
Instruction Memory
addr
addr
data
data
Addressing Unit
Control
for (int i = 0; i < 16; i++) x[i] = a[i] + b[i];

## Slide 12: Vector Code Example
CMOVE(16, R0)
loop: LD(R1, 0, R4)
LD(R2, 0, R5)
ADDC(R1, 4, R1)
ADDC(R2, 4, R2)
ADD(R4, R5, R6)
ST(R6, 0, R3)
ADDC(R3, 4, R3)
SUBC(R0, 1, R0)
BNE(R0, loop)
LD.V(R1, 0, V1)
LD.V(R2, 0, V2)
ADD.V(V1, V2, V3)
ST.V(V3, 0, R3)
for (i = 0; i < 16; i++) x[i] = a[i] + b[i];
Beta assembly
Equivalent vector assembly
# of cycles = 1 + 10*15 + 9 = 160
# of cycles = 4

## Slide 13: Data-dependent Vector Operations
LD.V(R1, 0, V1) // load a[i]
LD.V(R2, 0, V2) // load b[i]
LD.V(R3, 0, V3) // load c[i]
CMPLT.V(V1, V2) // set local predicate flags
// predicated instructions perform the
// indicated operation if the local predicate
// flag istrue or isfalse.
ADDC.V.iftrue(V3, 3, V3)
for (i = 0; i < 16; i++) if (a[i] < b[i]) c[i] = c[i] + 3;
Equivalent vector assembly

## Slide 14: Vector Processing Implementations
Advantages of vector ISAs:
  Compact: 1 instruction defines N operations
  Parallel: N operations are (data) parallel and independent
  Expressive: Memory operations describe regular patterns
Modern CPUs: Vector extensions & wider registers
  SSE: 128-bit operands (4x32-bit or 2x64-bit)
  AVX (2011): 256-bit operands (8x32-bit or 4x64-bit)
  AVX-512 (upcoming): 512-bit operands
  Explicit parallelism, extracted at compile time (vectorization)
GPUs: Designed for data parallelism from the ground up
  32 to 64 32-bit floating-point elements
  Implicit parallelism, scalar binary with multiple instances executed in lockstep (and regrouped dynamically)

## Slide 15: Multicore Processors
If applications have a lot of parallelism, using a larger number of simpler cores is more efficient!
Performance
Cost (area, energy…)
Cost/perf curve of possible core designs
High-perf, expensive core
Moderate perf, efficient core
2 cores
4 cores
What is the optimal tradeoff between core cost and number of cores?

## Slide 16: Amdahl’s Law
Speedup= timewithout enhancement / timewith enhancement
Suppose an enhancement speeds up a fraction f of a task by a factor of S
timenew = timeold·( (1-f) + f/S )
Soverall = timeold / timenew = 1 / ( (1-f) + f/S )
f
(1 - f)
(1 - f)
timenew
f/S
timeold
Corollary: Make the common case fast

## Slide 17: Amdahl’s Law and Parallelism
What is the maximum speedup you can get by running on a multicore machine?
Soverall = 1 / ( (1-f) + f/S )
f = 0.9, S=∞  Soverall = 10
What f do you need to use a 1000-core machine well?
Soverall 1 / (1-f)
lim
S→∞
Say you write a program that can do 90% of the work in parallel, but the other 10% is sequential
Soverall = 500  f = 0.998

## Slide 18: Thread-Level Parallelism
Divide computation among multiple threads of execution
  Each thread executes a different instruction stream
  More flexible than vector processing, but more expensive
Communication models:
  Shared memory:
    Single address space
    Implicit communication by memory loads & stores
  Message passing:
    Separate address spaces
    Explicit communication by sending and receiving messages
Mem
Mem
Mem
Network
Mem

## Slide 19: Multicore Caches
Multicores have multiple private caches for performance
We want the semantics of a single shared memory
Core 0
Main Memory (x=1, y=2)
Cache
(x=1, y=2)
Core 1
Cache
(x=1, y=2)
Core 2
Cache
Core 3
Cache
Memory
bus
Thread A (C0)
x = 3; print(y);
Thread B (C1)
y = 4; print(x);
Consider the following trivial threads running on C0 and C1:

## Slide 20: What Are the Possible Outcomes?
SEQUENCE A prints B prints
x=3; print(y); y=4; print(x); 2 1
x=3; y=4; print(y); print(x); 2 1
x=3; y=4; print(x); print(y); 2 1
y=4; x=3; print(x); print(y); 2 1
y=4; x=3; print(y); print(x); 2 1
y=4; print(x); x=3; print(y); 2 1
Plausible execution sequences:
Thread A
x = 3; print(y);
Thread B
y = 4; print(x);
$1: x = 1
y = 2
$2: x = 1
y = 2
Hey, we get the same answer every time… Let’s go build it!
X 3
X 4

## Slide 21: Uniprocessor Outcome
But, what are the possible outcomes if we ran Thread A and Thread B on a single timed-shared processor?
SEQUENCE A prints B prints
x=3; print(y); y=4; print(x); 2 3
x=3; y=4; print(y); print(x); 4 3
x=3; y=4; print(x); print(y); 4 3
y=4; x=3; print(x); print(y); 4 3
y=4; x=3; print(y); print(x); 4 3
y=4; print(x); x=3; print(y); 4 1
Plausible Uniprocessor execution sequences:
Thread A
x = 3; print(y);
Thread B
y = 4; print(x);
Notice that the outcome 2, 1 does not appear in this list!

## Slide 22: Sequential Consistency
Semantic constraint:
  Result of executing N parallel threads should correspond to some interleaved execution on a single processor.
Possible printed values: 2, 3; 4, 3; 4, 1.
  (each corresponds to at least one interleaved execution)
IMPOSSIBLE printed values: 2, 1
  (corresponds to NO valid interleaved execution).
Thread A
x = 3; print(y);
Thread B
y = 4; print(x);
Shared Memory
int x=1, y=2;
Weren’t caches supposed to be invisible to programs?

## Slide 23: Alternatives to Sequential Consistency?
ALTERNATIVE MEMORY SEMANTICS:
“WEAK” consistency
  EASIER GOAL: Memory operations from each thread appear to be performed in order issued by that thread ;
  Memory operations from different threads may overlap in arbitrary ways (not necessarily consistent with any interleaving).
ALTERNATIVE APPROACH:
  • Weak consistency, by default;
  • MEMORY BARRIER instruction: stalls thread until all previous memory operations have completed.
See http://www.rdrop.com/users/paulmck/scalability/paper/whymb.2010.07.23a.pdf for a very readable discussion of memory semantics in multicore systems.

## Slide 24: Fix: “Snoopy” Cache Coherence Protocol
Core 0
Main Memory (x=1, y=2)
Cache
(x=1, y=2)
Core 1
Cache
(x=1, y=2)
Core 2
Cache
Core 3
Cache
Idea: Have caches communicate over shared bus, letting other caches know when a shared cached value changes
“Snoopy”
bus
Goal: minimize contention for snoopy bus by communicating only when necessary, i.e., when there’s a shared value.

## Slide 25: Example: MESI Cache Coherence Protocol
Modified The cache line is present only in the current cache, and is dirty; it has been modified from the value in main memory. The cache is required to write the data back to main memory at some time in the future, before permitting any other read of the (no longer valid) main memory state.
Exclusive The cache line is present only in the current cache, but is clean; it matches main memory. It may be changed to the Shared state at any time, in response to a bus read request. Alternatively, it may be changed to the Modified state when writing to it.
Shared Indicates that this cache line may be stored in other caches of the machine and is clean; it matches the main memory. The line may be discarded (changed to the Invalid state) at any time. Writes to SHARED cache lines get special handling…
Invalid Indicates that this cache line is invalid (unused).
https://en.wikipedia.org/wiki/MESI_protocol
State
Tag
Data
Cache line:

## Slide 26: The Cache Has Two Customers!
State
Tag
Data
Cache line:
Read
Write
Store queue
CPU
Queue up write misses,
STORE_BARRIER inst waits until store queue is empty
Queue up invalidates,
READ_BARRIER inst waits until invalidate queue is empty
Read
Read w/ intent to modify
Write
Invalidate
Flags:
shared
Invalidate queue
Snoopy bus

## Slide 27: MESI Activity Diagram
CC0: https://en.wikipedia.org/wiki/MESI_protocol#/media/File:MESI_protocol_activity_diagram.png
Intel adds “F” state to choose which cache responds

## Slide 28: Cache Coherence in Action
Thread A
x = 3; print(y);
Thread B
y = 4; print(x);
$0: [S] x =1, [S] y = 2
$1: [S] x =1, [S] y = 2
1. x = 3 → $0 sends invalidate x, update cache
$0: [M] x =3, [S] y = 2
$1: [S] y = 2
2. y = 4 → $1 sends invalidate y, update cache
$0: [M] x =3
$1: [M] y = 4
3. print(x) → $1 read x, $0 responds with Shared flag, update mem
$0: [S] x =3
$1: [S] x = 3, [M] y = 4
4. print(y) → $0 read y, $1 responds with Shared flag, update mem
$0: [S] x =3, [S] y = 4
$1: [S] x = 3, [S] y = 4
1
2
3
4

## Slide 29: Parallel Processing Summary
Prospects for future CPU architectures:
Pipelining - Well understood, but mined-out Superscalar - At its practical limits Vector/GPU - Useful for special applications
Prospects for future Computer System architectures: Single-thread limits: forcing multicores, parallelism
Brains work well, with dismal clock rates … parallelism?
Needed: NEW models, NEW ideas, NEW approaches
FINAL ANSWER: It’s up to YOUR generation!
Notes: https://openclipart.org/detail/140701/brain