## Slide 1: 7. Performance Measures
6.004x Computation Structures
Part 1 – Digital Circuits
Copyright © 2015 MIT EECS

## Slide 2: Forget circuits… Let’s Solve a Real Problem
INPUT:
dirty laundry
OUTPUT:
6 more weeks
Device: Washer
Function: Fill, Agitate, Spin
WasherPD = 30 mins
Device: Dryer
Function: Heat, Spin
DryerPD = 60 mins
Notes: https://openclipart.org/detail/11223/various-clothing
https://openclipart.org/detail/29000/bleach-bottle

## Slide 3: One Load At a Time
Step 1:
Step 2:
TotalPD = WasherPD + DryerPD
= _________ mins
90
Everyone knows that the real reason that we put off doing laundry so long is not because we procrastinate, are lazy, or even have better things to do.
The fact is, doing one load at a time is not smart.

## Slide 4: Doing N Loads of Laundry
Here’s how they do laundry at Harvard, the “combinational” way.
Step 1:
Step 2:
Step 3:
Step 4:
TotalPD = N*(WasherPD + DryerPD)
= _________ mins
N*90
…
Of course, this is just an urban legend. No one at Harvard actually does laundry. The butlers all arrive on Wednesday morning, pick up the dirty laundry and return it all pressed and starched in time for afternoon tea.

## Slide 5: Doing N Loads… The 6.004 Way
6.004 students “pipeline” the laundry process.
That’s why we wait!
Step 1:
Step 2:
Step 3:
TotalPD = N * Max(WasherPD, DryerPD)
= ____________ mins
N*60
…
Actually, it’s more like N*60 + 30 if we account for the startup transient correctly. When doing pipeline analysis, we’re mostly interested in the “steady state” where we assume we have an infinite supply of inputs.

## Slide 6: Performance Measures
Latency: The delay from when an input is established until the output associated with that input becomes valid.
Harvard Laundry = _________ mins
6.004 Laundry = _________ mins
90
120
1/90
1/60
Assuming that the wash is started as soon as possible and waits (wet) in the washer until dryer is available.
Throughput:
The rate at which inputs or outputs are processed.
Harvard Laundry = _________ outputs/min
6.004 Laundry = _________ outputs/min

## Slide 7: Okay, Back To Circuits…
F
G
H
X
P(X)
F(X)
G(X)
For combinational logic: latency = tPD, throughput = 1/tPD.
We can’t get the answer faster, but are we making effective use of our hardware at all times?
G(X)
F(X)
P(X)
X
F & G are “idle”, just holding their outputs stable while H performs its computation

## Slide 8: Pipelined Circuits
use registers to hold H’s input stable!
F
G
H
X
P(X)
15
20
25
Now F & G can be working on input Xi+1 while H is performing its computation on Xi. We’ve created a 2-stage pipeline: if we have a valid input X during clock cycle j, P(X) is valid during clock j+2.
Suppose F, G, H have propagation delays of 15, 20, 25 ns and we are using ideal zero-delay registers:
latency
45
______
unpipelined
2-stage pipeline
50
1/25
throughput
1/45
______
worse
better

## Slide 9: Pipeline Diagrams
F & G
H
i
i+1
i+2
i+3
F(Xi+1)
G(Xi+1)
H(Xi)
F(Xi+2)
G(Xi+2)
H(Xi+1)
Clock cycle
Pipeline stages
The results associated with a particular set of input data moves diagonally through the diagram, progressing through one pipeline stage each clock cycle.
H(Xi+2)
…
F
G
H
X
P(X)
15
20
25
F(Xi)
G(Xi)
Xi stable here
P(Xi) available here

## Slide 10: Pipeline Conventions
DEFINITION:
  A well-formed K-Stage Pipeline (“K-pipeline”) is an acyclic circuit having exactly K registers on every path from an input to an output.
  a COMBINATIONAL CIRCUIT is thus an 0-stage pipeline.
COMPOSITION CONVENTION:
  Every pipeline stage, hence every K-Stage pipeline, has a register on its OUTPUT (not on its input).
ALWAYS:
  The CLOCK common to all registers must have a period sufficient to cover propagation over combinational paths PLUS (input) register tPD PLUS (output) register tSETUP.
The LATENCY of a K-pipeline is K times the period of the system’s clock.
The THROUGHPUT of a K-pipeline is the frequency of the clock.

## Slide 11: Ill-formed Pipelines
B
C
X
Y
A
Problem:
  Successive inputs get mixed: e.g., B(A(Xi+1), Yi). This happened because some paths from inputs to outputs have 2 registers, and some have only 1!
  This CAN’T HAPPEN on a well-formed K pipeline!
none
For what value of K is the following circuit a K-Pipeline? ANS: ____________
Consider a BAD job of pipelining:
2
1

## Slide 12: A Pipelining Methodology
Step 1:
Draw a line that crosses every output in the circuit, and mark the endpoints as terminal points.
Step 2:
Continue to draw new lines between the terminal points across various circuit connections, ensuring that every connection crosses each line in the same direction. These lines demarcate pipeline stages.
Adding a pipeline register at every point where a separating line crosses a connection will always generate a valid pipeline.
STRATEGY:
Focus your attention on placing pipelining registers around the slowest circuit elements (BOTTLENECKS).
A
4nS
B
3nS
C
8nS
D
4nS
E
2nS
F
5nS
T = 1/8ns
L = 24ns
INPUTS
OUTPUTS

## Slide 13: Pipeline Example
A
B
C
X
Y
2
1
1
0-pipe:
1-pipe:
2-pipe:
3-pipe:
LATENCY
THROUGHPUT
4
1/4
OBSERVATIONS:
  • 1-pipeline improves neither L or T.
  • T improved by breaking long combinational paths, allowing faster clock.
  • Too many stages cost L, don’t improve T.
  • Back-to-back registers are often required to keep pipeline well-formed.
4
1/4
1
4
1/2
2
1/2
6
3
+ increase throughput
− increase latency
− “bottleneck” problem

## Slide 14: Pipelined Components
A’ (2x1ns)
C
X
Y
1
Pipelined systems can be hierarchical:
  Replacing a slow combinational component with a k-pipe version may let us decrease the clock period
B
1
3
1
2
4
4-stage pipeline, throughput=1
  Must account for new pipeline stages in our plan
but... but...
How can I pipeline
a clothes dryer???

## Slide 15: How Do 6.004 Students Do Laundry?
They work around the bottleneck. First, they find a laundromat with two dryers for every washer. Then they use dryer #1 for odd-numbered wash loads and dryer #2 for even-numbered wash loads.
1/30
90
Throughput = ________ loads/min, Latency = ________ mins/load
minutes
0
30
60
90
120
Step 1
Step 2
Step 3
Step 4
Washer
Load #1
Load #1
Load #2
Load #3
Load #2
Load #3
Load #4
Load #4
Load #5
Load #6
Load #5
150
180
…
…
Step 5
Step 6
Dryer #1
Dryer #2
#1
#2
#3
#4

## Slide 16: Back To Our Bottleneck…
A
4nS
B
3nS
C
8nS
D
4nS
E
2nS
F
5nS
T = 1/8ns
L = 24ns
Recall our earlier example...
  C – the slowest component – limits clock period to 8 ns.
  HENCE throughput limited to 1/8ns.
We could improve throughput by
  Finding a pipelined version of C;
  OR ...
  interleaving multiple copies of C!

## Slide 17: Circuit Interleaving
We can simulate a pipelined version of a slow component by replicating the critical element and alternate inputs between the various copies.
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
Xi
C(Xi-2)
clk
Q
This is a simple 2-state FSM that alternates between 0 and 1 on each clock

## Slide 18: Circuit Interleaving
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
Xi
C(Xi-2)
clk
FSM Q
X1
X input
X2
X3
X4
C0 input
C0 output
X1
X3
C(X1)
C(X3)
reg output
C(X1)
C(X2)
C(X3)
reg input
C(X1)
C(X2)
C(X3)
C1 input
C1 output
X2
X4
C(X2)
Cycle #1
Cycle #2
Cycle #3
Cycle #4

## Slide 19: Circuit Interleaving
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
x
x
C(Xi-2)
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
0
1
C(Xi-2)
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
Xi
1
0
C(Xi-2)
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
0
1
C0
G
D
Q
D
Q
1
0
C’
G
D
Q
C1
C(Xi-2)
Throughput = 1/clock
Latency = 2 clocks
N-way
interleave
N registers
…
N-way interleaving is equivalent to N pipeline Stages...
2-Clock Martinizing
“In by ti, out by ti+2”
Notes: Note 10/7/04 SAW:
This slide used to say “N-1 registers” rather than N registers as the equivalent to an N-way interleaved component (and apparenly has for many terms). I don’t understand this, tho maybe I’m missing some subtlety. It seems to me that for the interleaved component:
Clk: 0 1 2 3 4
Input: X0 X1 X2 X3 X4
Top latch out: X0 X0 X2 X2 X4
Bot latch out: X1 X1 X3 X3
Mux sel in: 0 1 0 1 0
Mux 0 in: [C1(X1)] C1(X1) [C1(X3)]
Mux 1 in: [C0(X0)] C0(X0)[C0(X2)] C0(X2)
Mux OUT: C0(X0) C1(X1) C0(X2)
Output: C0(X0) C1(X1) C0(X2)
Which is equialent to a (FAST) combinational C module followed by 2 registers.

## Slide 20: Combine Techniques
We can combine interleaving and pipelining. Here, C’ interleaves two C elements and has an effective tCLK of 4 ns and a latency of 8 ns.
Since C’ behaves as a 2-stage pipeline, two of our pipelining contours must pass through the C’ component.
A
4ns
B
3ns
C’
2x4ns
D
4ns
E
2ns
F
5ns
By combining interleaving with pipelining we move the bottleneck from the C element to the F element.
T = 1/5ns
L = 25ns

## Slide 21: And Add A Little Parallelism…
Step 1:
We can combine interleaving and pipelining with parallelism.
Throughput =
____________ _____load/min
Latency = _______ min
Step 2:
Step 3:
Step 4:
Step 5:
2/30 = 1/15
90
1 step = 30 minutes

## Slide 22: Control Structure Alternatives
Synchronous, globally-timed:
X
“here’s X”
“got X”
CLK
here’s X
got X
X
X2
X1
Synchronous, locally-timed:
Local FSMs control flow of data using “handshake” signals
X
“here’s X”
“got X”
here’s X
got X
X
X2
X1
Asynchronous, locally-timed system using transition signaling:
1
2
3
4

## Slide 23: Self-timed Example
X
A
C
B
A(X)
here’s …
Got it.
I get it! A sees “got it” as 1 when both B and C have asserted “got it”. And then “got it” returns to 0 when both B and C have deasserted “got it”.
1
0
Heres
Got
Heres2
Got1
Got2
Heres1
Heres
Got
Got1
Got2

## Slide 24: Self-timed Example
X
A
C
B
A(X)
here’s …
Got it.
Elegant, timing-independent design:
  • Each component specifies its own time constraints
  • Local adaptation to special cases (eg, multiplication by 0)
  • Module performance improvements automatically exploited
  • Can be made asynchronous (no clock at all!) or synchronous

## Slide 25: Control Structure Taxonomy
Synchronous
Asynchronous
Globally
Timed
Locally
Timed
Centralized clocked FSM generates all control signals.
Easy to design but fixed-sized interval can be wasteful (no data-dependencies in timing)
Central control unit tailors current time slice to current tasks.
Large systems lead to very complicated timing generators… just say no!
Start and Finish signals generated by each major subsystem, synchronously with global clock.
The best way to build large systems that have independently-timed components.
Each subsystem takes asynchronous Start, generates asynchronous Finish (perhaps using local clock).
The “next big idea” for the last several decades: a lot of design work to do in general, but extra work is worth it in special cases

## Slide 26: Summary
Latency (L) = time it takes for given input to arrive at output
Throughput (T) = rate at which new outputs appear
For combinational circuits: L = tPD of circuit, T = 1/L
For K-pipelines (K > 0):
  always have register on output(s)
  K registers on every path from input to output
  Inputs available shortly after clock i, outputs available shortly after clock (i+K)
  tCLK = tPD,REG + tPD of slowest pipeline stage + tSETUP
  T = 1/tCLK
    more throughput ⇒ split slowest pipeline stage(s)
    use replication/interleaving if no further splits possible
  L = K*tCLK = K / T
    pipelined latency ≥ combinational latency