## Slide 1: 5. Sequential Logic
6.004x Computation Structures
Part 1 – Digital Circuits
Copyright © 2015 MIT EECS

## Slide 2: Something We Can’t Build (Yet)
What if you were given the following design specification:
When the button is pushed: 1) Turn the light on if it is off
2) Turn the light off if it is on
The light should change state within a second of the button press
button
light
What makes this device different from those we’ve discussed before?
“State” – i.e., the device has memory
The output was changed by a input “event” (pushing a button) rather than an input “level”
#1
#2

## Slide 3: Digital State: What We’d Like to Build
Plan: Build a Sequential Circuit with stored digital STATE –
  Memory stores CURRENT state, produced at output
  Combinational Logic computes
    NEXT state (from input, current state)
    OUTPUT bits (from input, current state)
  State changes on LOAD control input
Combinational
Logic
Current
State
Next
State
Input
Output
Memory
Device
LOAD
Sequence of values
Trigger periodically
Needed:
Loadable
Memory

## Slide 4: Memory: Using Capacitors
We’ve chosen to encode information using voltages and we know from physics that we can “store” a voltage as charge on a capacitor:
Pros:
compact – low cost/bit (on BIG memories)
Cons:
complex interface
stable? (noise, …)
it leaks! ⇒ refresh
To write:
Drive bit line, turn on access fet, force storage cap to new voltage
NFET serves as access switch
VREF
word line
bit line
Suppose we use feedback to refresh continuously?
To read: precharge bit line, turn on access fet,
detect (small) change in bit line voltage
C

## Slide 5: Memory: Using Feedback
IDEA: use positive feedback to maintain storage indefinitely. Our logic gates are built to restore marginal signal levels, so noise shouldn’t be a problem!
VIN
VOUT
Result: a bistable storage element
Feedback constraint:
VIN = VOUT
VTC for
inverter pair
VIN
VOUT
Three solutions:
two end-points are stable
middle point is metastable
Not affected
by noise
We’ll get back to this!
0 1 0
1 0 1

## Slide 6: Settable Memory Element
Y
S
B
It’s easy to build a settable storage element (called a latch) using a lenient MUX:
D0
D1
G
0
0
1
1
D
--
--
0
1
Q’
0
1
--
--
Q
0
1
0
1
“state” signal
appears as both
input and output
Q stable
Q follows D
A
D
G
Q
Q’
Here’s a feedback path, so it’s no longer a combinational circuit.
D: data input
G: gate input
Q: state output
S

## Slide 7: New Device: D Latch
G
D
Q
D
TPD
V1
V2
V2
V1
TPD
G
Q
G=1:
Q follows D
G=0:
Q holds
G=1: Q Follows D, independently of Q’
G=0: Q Holds stable Q’, independently of D
Q
0
1
D
G
Q’
Circuit:
Schematic Symbol:
BUT… A change in D or G contaminates Q, hence Q’ … how can this possibly work?

## Slide 8: A Plea for Lenience
3.
TPD
TPD
2.
TPD
1.
0
1
D
G
Q
D
V1
V2
V2
V1
G
Q
Assume LENIENT Mux, propagation delay of TPD
Then output valid when
Q’
Does lenience guarantee a working latch?
  Q=D stable for TPD , independently of G; or
  G=1, D stable for TPD, independently of Q’; or
  G=0, Q stable for TPD , independently of D
What if D and G change at about the same time…

## Slide 9: …With a Little Discipline
Dynamic Discipline for our latch:
D Stable
0
1
A
D
G
Q
To reliably latch V2:
Q’
Apply V2 to D, holding G=1
After another TPD, Q’ & D both valid for TPD; will hold Q=V2 independently of G
Set G=0, while Q’ & D hold Q=D
After TPD, V2 appears at Q=Q’
After another TPD, G=0 and Q’ are sufficient to hold Q=V2 independently of D
D
G
Q
V2
V2
TPD
TPD
TSETUP
THOLD
TPD
TSETUP = 2TPD: interval prior to G transition for which D must be stable & valid
THOLD = TPD: interval following G transition for which D must be stable & valid

## Slide 10: Let’s Try It Out!
Combinational
Logic
G
D
Q
Current
State
New
State
Input
Output
When G=1, latch is Transparent…
  … provides a combinational path from D to Q.
Can’t work without tricky timing constraints on G=1 pulse:
  Must fit within contamination delay of logic
  Must accommodate latch setup, hold times
Want to signal an INSTANT, not an INTERVAL…
Looks like a stupid
approach to me…

## Slide 11: Flakey Control Systems
Gate closed
Gate open
Sequence of values
How do we ensure only one car gets through?
Notes: https://openclipart.org/detail/1656/fabia---back-view-by-ryanlerch

## Slide 12: Solution: Escapement Strategy (2 gates)
Gate 1: open
Gate 2: closed
Sequence of values
Gate 1
Gate 2
Gate 1: closed
Gate 2: open
Gate 1
Gate 2
Key: at no time is there a path through both gates
Notes: https://openclipart.org/detail/1656/fabia---back-view-by-ryanlerch

## Slide 13: (Edge-Triggered) D Register
G
D
Q
G
D
Q
D
CLK
Q
input
output
Observations:
  only one latch “transparent” at any time:
    input latch closed when output is open
    output latch closed when input is open
  ⇒ no combinational path through register
The gate of this latch is open when the clock is low
The gate of this latch is open when the clock is high
(the feedback path in one of the input or output latches is always active)
What does that one do?
0
1
0
1S
D
G
Q

## Slide 14: D-Register Waveforms
G
D
Q
G
D
Q
D
CLK
D
Q
D
CLK
Q
input
output
D
CLK
Q
input latch closed
output latch open
input latch open
output latch closed
Q

## Slide 15: Um, about that hold time…
G
D
Q
G
D
Q
D
CLK
Q
input
output
D
CLK
Output latch is closing ⇒ ☆ must meet setup/hold times but input latch is opening so ☆ may change
The input’s contamination delay must meet the hold time of the output: tCD,M ≥ tH,S

## Slide 16: D-Register Timing 1
CLK
D
Q
D
Q
D
CLK
Q
≤tPD
tPD: maximum propagation delay, CLK→Q
≥tCD
tCD: minimum contamination delay, CLK→Q
≥tSETUP
tSETUP: setup time
  guarantee that D has propagated through feedback path before input latch closes
≥tHOLD
tHOLD: hold time
  guarantee input latch is closed and data is stable before allowing D to change

## Slide 17: Single-clock Synchronous Circuits
Single-clock Synchronous Discipline
• No combinational cycles
• Only care about value of register data inputs just before rising edge of clock
• Period greater than every combinational delay + setup time
• Change saved state after noise-inducing logic transitions have stopped!
We’ll use registers in a highly constrained way to build digital systems:
• Single periodic clock signal shared among all clocked devices
Does that symbol register?

## Slide 18: Timing in a Single-clock System
œ
CLK
t1
t1 = tCD,reg1 + tCD,L ≥ tHOLD,reg2
L
D
Q
D
Q
CLK
reg1
reg2
Questions for register-based designs:
  how much time for useful work (i.e. for combinational logic delay)?
  what happens if there’s no combinational logic between two registers?
  what happens if CLK signal doesn’t arrive at the two registers at exactly the same time (a phenomenon known as “clock skew”)?
t2
t2 = tPD,reg1 + tPD,L + tSETUP,reg2 ≤ tCLK
QR1
tCD,reg1
tCD, L
tPD, L
tPD,reg1
QR1
tSETUP,reg2

## Slide 19: Model: Discrete Time
Active Clock Edges punctuate time ---
  Discrete Clock periods
  Sequences of states
  Simple rules – eg truth tables – relating outputs to inputs and the current state)
ABSTRACTION: Finite State Machines (next lecture!)
Combinational
Logic
Current
State
Next
State
Input
Output
DREG
Memory
Clock
State updated every rising clock edge

## Slide 20: Sequential Circuit Timing
Questions:
  Constraints on tCD for the logic?
  Minimum clock period?
  Setup, Hold times for Inputs?
Combinational
Logic
Current
State
Next
State
Input
Output
Clock
tCD,L = ? tPD,L = 5ns
tCD,R = 1ns tPD,R = 3ns tS,R = 2ns
tH,R = 2ns
tCD,L ≥ 1 ns
tS,INPUT = tPD,L + tS,R = 7 nS
tH,INPUT = tH,R - tCD,L= 1 nS
tCD,R (1 ns) + tCD,L(?) ≥ tH,R(2 ns)
tCLK ≥ tPD,R+tPD,L+ tS,R = 10nS
clk
Next State
tS,R
tH,R
Input
tPD,L
tCD,L

## Slide 21: Summary
Basic memory elements:
  Feedback, detailed analysis => basic level-sensitive devices (eg, latch)
  2 Latches => Register
  Dynamic Discipline: constraints on input timing
Synchronous 1-clock logic:
  Simple rules for sequential circuits
  Yields clocked circuit with TS, TH constraints on input timing
Finite State Machines
  Next Lecture Topic!
>tS
>tH
Clk
Q
D
>tCD
<tPD
D Q
D Q
Out
In
Clk
Combinational
logic