## Slide 1: 19. Concurrency & Synchronization
6.004x Computation Structures
Part 3 – Computer Organization
Copyright © 2016 MIT EECS

## Slide 2: Interprocess Communication
Why have multiple processes?
  Concurrency
  Asynchrony
  Processes as a programming primitive
  Data-/Event-driven
Classic Example: “Producer-Consumer” Problem
P
PRODUCER
C
CONSUMER
loop: <xxx>;
send(c); goto loop
loop: c = rcv();
<yyy>; goto loop
P1
P2
Code
Stack
Data
Code
Stack
Data
Shared
Data
How to communicate?
  Shared Memory (overlapping contexts)...
  Synchronization instructions (hardware support)
  Supervisor calls
Real-World Examples: Compiler/Assembler,
Application Frontend/Backend,
UNIX pipeline

## Slide 3: Synchronous Communication
PRODUCER
2
<xxx>
3
<xxx>
<xxx>
1
send
1
send
2
send
3
CONSUMER
<yyy>
1
rcv
1
<yyy>
2
rcv
2
<yyy>
3
rcv
3
loop: <xxx>;
send(c); goto loop
loop: c = rcv();
<yyy>; goto loop
rcvi ≺ sendi+1
sendi ≺ rcvi
• Can’t consume data before it’s produced
a ≺ b
Precedence Constraints:
“a precedes b”
• Producer can’t “overwrite” data before it’s consumed

## Slide 4: FIFO Buffering
RELAXES interprocess synchronization constraints. Buffering relaxes the following OVERWRITE constraint to:
P
C
N-character FIFO buffer
<xxx>;
send(c0);
rcv(); //c0
<yyy>;
<xxx>;
send(c1);
rcv(); //c1
<yyy>;
<xxx>;
send(c2);
rcv(); //c2
<yyy>;
<xxx>;
send(c3);
time
c0
c1
c2
c0
c1
c2
c0
c1
c2
c0
c1
c2
c3
rcvi ≺ sendi+N
c0
c1
c2
c3
c0
c1
c0
c0
c0
Read index
(out)
Write index
(in)
c0
“Circular Buffer:”

## Slide 5: Example: Bounded Buffer Problem
send(char c){
buf[in] = c;
in = (in+1)% N;
}
char rcv(){
char c;
c = buf[out];
out = (out+1)% N;
return c;
}
PRODUCER:
CONSUMER:
char buf[N]; /* The buffer */
int in=0, out=0;
SHARED MEMORY:
Problem: Doesn’t enforce precedence constraints
(e.g. rcv( ) could be invoked prior to any send() )

## Slide 6: Semaphores (Dijkstra)
Programming construct for synchronization:
  NEW DATA TYPE: semaphore, an integer ≥ 0
  semaphore s = K; // initialize s to K
  NEW OPERATIONS (defined on semaphores):
    wait(semaphore s)
    wait until s > 0, then s = s – 1
    signal(semaphore s)
    s = s + 1 (one WAITing process may now be able to proceed)
  SEMANTIC GUARANTEE: A semaphore s initialized to K enforces the constraint:
Often you will see P(s) used for wait(s) and V(s) used for signal(s)!
P = “proberen”(test) or “pakken”(grab)
V= “verhogen”(increase)
signal(s)i ≺ wait(s)i+K
This is a precedence relationship: the ith call to signal must complete before the the (i+K)th call to wait will succeed.
Notes: https://openclipart.org/detail/27848/y-semaphore
https://en.wikipedia.org/wiki/Edsger_W._Dijkstra#/media/File:EdsgerDijkstra.jpg

## Slide 7: Semaphores for Precedence
Process A
A1;
A2;
A3;
A4;
A5;
Process B
B1;
B2;
B3;
B4;
B5;
Goal: want statement A2 in process A to complete before statement B4 in Process B begins.
A2 ≺ B4
Recipe:
Declare semaphore = 0
signal(s) at start of arrow
wait(s) at end of arrow
signal(s);
wait(s);
semaphore s = 0;

## Slide 8: Semaphores for Resource Allocation
Abstract problem:
• POOL of K resources
• Many processes, each needs resource for occasional uninterrupted period
• MUST guarantee that at most K resources are in use at any time.
Semaphore Solution:
In shared memory:
semaphore s = K; // K resources
Using resources:
wait(s); // Allocate a resource
… // use it for a while
signal(s); // return it to pool
Invariant: Semaphore value = number of resources left in pool

## Slide 9: Bounded Buffer Problem w/ Semaphores
send(char c)
{
buf[in] = c;
in = (in+1)%N;
signal(chars);
}
char rcv()
{ char c;
wait(chars);
c = buf[out];
out = (out+1)%N;
return c;
}
PRODUCER:
CONSUMER:
char buf[N]; /* The buffer */
int in=0, out=0;
semaphore chars=0;
SHARED MEMORY:
PRECEDENCE managed by semaphore: sendi ≺ rcvi
RESOURCE managed by semaphore chars: # of chars in buf
Does this work?

## Slide 10: Flow Control Problems
Q: What keeps PRODUCER from putting N+1 characters into the N-character buffer?
P
C
N-character FIFO buffer
A: Nothing.
sendi ≺ rcvi
WHAT we’ve got thus far:
  Result: OVERFLOW.
WHAT we still need:
rcvi ≺ sendi+N

## Slide 11: Bounded Buffer Problem w/ more Semaphores
Resources managed by semaphore: characters in FIFO, spaces in FIFO. Works with single producer, consumer. But what about multiple producers and consumers?
send(char c)
{
wait(space);
buf[in] = c;
in = (in+1)%N;
signal(chars);
}
char rcv()
{
char c;
wait(chars);
c = buf[out];
out = (out+1)%N;
signal(space);
return c;
}
PRODUCER:
CONSUMER:
char buf[N]; /* The buffer */
int in=0, out=0;
semaphore chars=0, space=N;
SHARED MEMORY:

## Slide 12: Simultaneous Transactions
Suppose you and your friend visit the ATM at exactly the same time, and remove $50 from your account. What happens?
Debit(int account, int amount) {
t = balance[account]; balance[account] = t – amount;
}
What is supposed to happen?
Withdraw(6004, 50)
Withdraw(6004, 50)
Process # 1 Process #2
LD(R10, balance, R0) SUB(R0, R1, R0)
ST(R0, balance, R10)
… …
LD(R10, balance, R0) SUB(R0, R1, R0)
ST(R0, balance, R10)
NET: You have $100, and your bank balance is $100 less.
ATM
ATM

## Slide 13: But, What If…
Process # 1 Process #2
LD(R10, balance, R0)
…
LD(R10, balance, R0) SUB(R0, R1, R0)
ST(R0, balance, R10)
…
SUB(R0, R1, R0)
ST(R0, balance, R10)
…
NET: You have $100 and your bank balance is $50 less!
We need to be careful when writing concurrent programs. In particular, when modifying shared data.
For certain code segments, called CRITICAL SECTIONS, we would like to ensure that no two executions overlap.
This constraint is called MUTUAL EXCLUSION.
Solution: embed critical sections in wrappers (e.g., “transactions”) that guarantee their atomicity, i.e., make them appear to be single, instantaneous operations.
Notes: https://openclipart.org/detail/227246/cash

## Slide 14: Semaphores for Mutual Exclusion
Debit(int account, int amount) { t = balance[account]; balance[account] = t – amount;
}
RESOURCE managed by “lock” semaphore:
Access to critical section
ISSUES:
Granularity of lock 1 lock for whole balance database? 1 lock per account? 1 lock for all accounts ending in 004
“a precedes b
or
b precedes a”
(i.e., they don’t overlap)
a ≺≻ b
signal(lock); // Finished with lock
semaphore lock = 1;
wait(lock); // Wait for exclusive access
Look up “database” on Wikipedia to learn about systems that support efficient transactions on shared data.

## Slide 15: Producer/Consumer Atomicity Problems
Consider multiple PRODUCER processes:
P1
C
N-character FIFO buffer
P2
...
buf[in] = c;
in = (in+1) % N;
...
...
buf[in] = c;
in = (in+1) % N;
...
P
1
P
2
BUG: Producers interfere with each other.

## Slide 16: Bounded Buffer Problem w/ even more Semaphores
send(char c)
{
wait(space);
wait(lock);
buf[in] = c;
in = (in+1)%N;
signal(lock);
signal(chars);
}
char rcv()
{ char c;
wait(chars);
wait(lock);
c = buf[out];
out = (out+1)%N;
signal(lock);
signal(space);
return c;
}
PRODUCER:
CONSUMER:
char buf[N]; /* The buffer */
int in=0, out=0;
semaphore chars=0, space=N;
semaphore lock=1;
SHARED MEMORY:

## Slide 17: The Power of Semaphores
send(char c)
{
wait(space);
wait(lock)
buf[in] = c;
in = (in+1)%N;
signal(lock);
signal(chars);
}
char rcv()
{ char c;
wait(chars);
wait(lock);
c = buf[out];
out = (out+1)%N;
signal(lock);
signal(space);
return c;
}
PRODUCER:
CONSUMER:
char buf[N]; /* The buffer */
int in=0, out=0;
semaphore chars=0, space=N;
semaphore lock=1;
SHARED MEMORY:
A single synchronization primitive that enforces both:
Precedence relationships:
sendi ≺ rcvi
rcvi ≺ sendi+N
Mutual-exclusion relationships:
protect variables in and out

## Slide 18: Semaphore Implementation
Semaphores are themselves shared data and implementing WAIT and SIGNAL operations will require read/modify/write sequences that must executed as critical sections. So how do we guarantee mutual exclusion in these particular critical sections without using semaphores?
Approaches:
  SVC implementation, using atomicity of kernel handlers. Works in timeshared processor sharing a single uninterruptable kernel.
  Implementation of a simple lock using a special instruction (e.g. “test and set”), depends on atomicity of single instruction execution. Works with shared-bus multiprocessors supporting atomic read-modify-write bus transactions. Using a simple lock to implement critical sections, we can use software to implement other semaphore functionality.
  Implementation using atomicity of individual read or write operations. For example, see “Dekker’s Algorithm” on Wikipedia.

## Slide 19: Semaphores as a Supervisor Call
wait_h( ) {
int *addr; addr = VtoP(User.Regs[R0]); // get arg if (*addr <= 0) { User.Regs[XP] = User.Regs[XP] – 4; sleep(addr);
} else
*addr = *addr - 1;
}
signal_h( ) {
int *addr; addr = VtoP(User.Regs[R0]); // get arg *addr = *addr + 1;
wakeup(addr);
}
Calling sequence:
…
// put address of lock
// into R0
CMOVE(lock, R0)
SVC(WAIT) or SVC(SIGNAL)
SVC call is not interruptible since it is executed in kernel mode.

## Slide 20: Hardware Support for Semaphores
TCLR(RA, literal, RC) test and clear location
PC ← PC + 4 EA ← Reg[Ra] + literal Reg[Rc] ← MEM[EA] MEM[EA] ← 0
Executed ATOMICALLY (cannot be interrupted)
Can easily implement mutual exclusion using binary semaphore
wait: TCLR(R31, lock, R0) BEQ(R0,wait) … critical section …
CMOVE(1,R0)
ST(R0, lock, R31)
wait(lock)
signal(lock)
Atomicity guaranteed by memory

## Slide 21: Synchronization: The Dark Side
The naïve use of synchronization constraints can introduce its own set of problems, particularly when a process requires access to more than one protected resource.
Transfer(int account1, int account2, int amount) {
wait(lock[account1]); wait(lock[account2]); balance[account1] = balance[account1] - amount; balance[account2] = balance[account2] + amount; signal(lock[account2]);
signal(lock[account1]);
}
Transfer(6004, 6005, 50)
Transfer(6005, 6004, 50)
DEADLOCK (aka “deadly embrace”)!
ATM
ATM
Notes: https://openclipart.org/detail/161629/go-go-sumo-sumo-1859

## Slide 22: Dining Philosophers
• Take (wait for) LEFT stick
• Take (wait for) RIGHT stick
• EAT until sated
• Replace both sticks
PHILOSOPHER'S ALGORITHM:
Philosophers think deep thoughts, but have simple secular needs. When hungry, a group of N philosophers will sit around a table with N chopsticks interspersed between them. Food is served, and each philosopher enjoys a leisurely meal using the chopsticks on either side to eat.
They are exceedingly polite and patient, and each follows the following dining protocol:
Shut up!!
Wait, I think I see a problem here...
Notes: https://openclipart.org/detail/403/turkey
https://openclipart.org/detail/1252/turkey
https://openclipart.org/detail/1025/turkey-platter

## Slide 23: Deadlock!
CONDITIONS:
1) Mutual exclusion - only one process can hold a resource at a given time
2) Hold-and-wait - a process holds allocated resources while waiting for others
3) No preemption - a resource can not be removed from a process holding it
4) Circular Wait
SOLUTIONS:
Avoidance
-or-
Detection and Recovery
No one can make progress because they are all waiting for an unavailable resource
He still doesn’t look too happy…
Cousin Tom is spared!

## Slide 24: One Solution
• Take LOW stick
• Take HIGH stick
• EAT
• Replace both sticks.
1
2
3
4
5
KEY: Assign a unique number to each chopstick, request resources in globally consistent order:
New Algorithm:
SIMPLE PROOF:
Deadlock means that each philosopher is waiting for a resource held by some other philosopher …
But, the philosopher holding the highest numbered chopstick can’t be waiting for any other philosopher (no hold-and-wait cycle) …
Thus, there can be no deadlock.

## Slide 25: Dealing With Deadlocks
Cooperating processes:
  Establish a fixed ordering to shared resources and require all requests to be made in the prescribed order
Transfer(int account1, int account2, int amount) { int a = min(account1, account2);
int b = max(account1, account2);
wait(lock[a]); wait(lock[b]); balance[account1] = balance[account1] - amount; balance[account2] = balance[account2] + amount; signal(lock[b]);
signal(lock[a]);
}
Transfer(6004, 6005, 50)
Transfer(6005, 6004, 50)
ATM
ATM
Unconstrained processes:
- O/S discovers circular wait & kills waiting process
- Transaction model
- Hard problem

## Slide 26: Summary
Communication among asynchronous processes requires synchronization….
  Precedence constraints: a partial ordering among operations
  Semaphores as a mechanism for enforcing precedence constraints
  Mutual exclusion (critical sections, atomic transactions) as a common compound precedence constraint
  Solving Mutual Exclusion via binary semaphores
  Synchronization serializes operations, limits parallel execution.
Many alternative synchronization mechanisms exist!
Deadlocks:
  Consequence of undisciplined use of synchronization mechanism
  Can be avoided in special cases, detected and corrected in others.