## Slide 1: 16. Virtual Memory
6.004x Computation Structures
Part 3 – Computer Organization
Copyright © 2016 MIT EECS

## Slide 2: Reminder: A Typical Memory Hierarchy
Everything is a cache for something else
Registers
Level 1 Cache
Level 2 Cache
Level 3 Cache
Main Memory
Flash Drive
Hard Disk
On chip
Other chips
Mechanical devices
On the datapath
Access time | Capacity | Managed By
1 cycle | 1 KB | Software/Compiler
2-4 cycles | 32 KB | Hardware
10 cycles | 256 KB | Hardware
40 cycles | 10 MB | Hardware
200 cycles | 10 GB | Software/OS
10-100us | 100 GB | Software/OS
10ms | 1 TB | Software/OS
Notes: Registers run in picoseconds, but because of the power they dissipate and the size of the circuitry, we can only have a small number of them.
Here we show a 3 level cache because that is what most of us have in our processors today.
The idea is to make your processor look like it has a large memory that runs fast. So we add caches. Unless you are accessing something new or something you haven’t accessed in a while, then you should be able to get your data from the cache.
Today we will augment that by essentially making the DRAM a cache for the larger Flash and hard disk memories.

## Slide 3: Reminder: Hardware Caches
Other implementation choices:
  Block size
  Replacement policy (LRU, Random, …)
  Write policy (write-through, write-behind, write-back)
address
Direct-mapped
Each address maps to a single location in the cache, given by index bits
N
address
N-way set-associative
Each address can map to any of N locations (ways) of a single set, given by its index bits
address
Fully associative
Any location can map to any address

## Slide 4: Reminder: A Typical Memory Hierarchy
Everything is a cache for something else
Registers
Level 1 Cache
Level 2 Cache
Level 3 Cache
Main Memory
Flash Drive
Hard Disk
On chip
Other chips
Mechanical devices
On the datapath
Access time | Capacity | Managed By
1 cycle | 1 KB | Software/Compiler
2-4 cycles | 32 KB | Hardware
10 cycles | 256 KB | Hardware
40 cycles | 10 MB | Hardware
200 cycles | 10 GB | Software/OS
10-100us | 100 GB | Software/OS
10ms | 1 TB | Software/OS
Before:
Hardware Caches
TODAY:
Virtual Memory
Notes: Registers run in picoseconds, but because of the power they dissipate and the size of the circuitry, we can only have a small number of them.
Here we show a 3 level cache because that is what most of us have in our processors today.
The idea is to make your processor look like it has a large memory that runs fast. So we add caches. Unless you are accessing something new or something you haven’t accessed in a while, then you should be able to get your data from the cache.
Today we will augment that by essentially making the DRAM a cache for the larger Flash and hard disk memories.

## Slide 5: Extending the Memory Hierarchy
Problem: DRAM vs disk has much more extreme differences than SRAM vs DRAM
  Access latencies:
    DRAM ~10-100x slower than SRAM
    Disk ~100,000x slower than DRAM
  Importance of sequential accesses:
    DRAM: Fetching successive words ~5x faster than first word
    Disk: Fetching successive words ~100,000x faster than first word
Result: Design decisions driven by enormous cost of misses
CPU
Fast SRAM
DRAM
Cache
Main memory
Hard disk
Secondary storage
~10ms
~1 TB
~100ns
~10 GB
~1-10ns
~10 KB – 10 MB
Notes: Today we are adding a hard disk to make the total address space that we can access much larger.
Disk is 100,000 times slower than DRAM. Huge cost of a miss so we really need to make sure that misses hardly ever happen.
Sequential accesses become more critical with hard disk than with DRAM.

## Slide 6: Impact of Enormous Miss Penalty
If DRAM was to be organized like an SRAM cache, how should we design it?
  Associativity: High, minimize miss ratio
  Block size: Large, amortize cost of a miss over multiple words (locality)
  Write policy: Write back, minimize number of writes
Is there anything good about misses being so expensive?
  We can handle them in software! What’s 1000 extra instructions (~1us) vs 10ms?
  Approach: Handle hits in hardware, misses in software
    Simpler implementation, more flexibility
Notes: Block size – bring in a thousand or multiple thousand words upon a miss in order to really take advantage of the faster access time of consecutive disk accesses.
Associativity – want to make it be the case that multiple processes can run at the same time. So if P1 accesses it’s address 0 and P2 accesses its address 0, we don’t want those 2 addresses to collide.

## Slide 7: Virtual Memory
Two kinds of addresses:
  CPU uses virtual addresses
  Main memory uses physical addresses
Hardware translates virtual addresses to physical addresses via an operating system (OS)-managed table, the page map
CPU
DRAM
Main memory
MMU
Memory management unit
Virtual addresses
(VAs)
Physical addresses
(PAs)
CPU
Page Map
0
1
0
1
N-1
P-1
Disk
Not all virtual addresses may have a translation

## Slide 8: Virtual Memory Implementation: Paging
Divide physical memory in fixed-size blocks, called pages
  Typical page size (2p): 4KB -16 KB
  Virtual address: Virtual page number + offset bits
  Physical address: Physical page number + offset bits
  Why use lower bits as offset?
MMU maps virtual pages to physical pages
  Use page map to perform translation
  Cause a page fault (a miss) if virtual page is not resident in physical memory.
Virtual Page #
Using main memory as a page cache = paging or demand paging
offset
Physical Page #
offset
p
32-p

## Slide 9: Demand Paging
Basic idea:
  Start with all virtual pages in secondary storage, MMU “empty”, ie, there are no pages resident in physical memory
  Begin running program… each VA “mapped” to a PA
    Reference to RAM-resident page: RAM accessed by hardware
    Reference to a non-resident page: page fault, which traps to software handler, which
      Fetches missing page from DISK into RAM
      Adjusts MMU to map newly-loaded virtual page directly in RAM
      If RAM is full, may have to replace (“swap out”) some little-used page to free up RAM for the new page.
  Working set incrementally loaded via page faults, gradually evolves as pages are replaced…

## Slide 10: Simple Page Map Design
One entry per virtual page
  Resident bit R = 1 for pages stored in RAM, or 0 for non-resident (disk or unallocated). Page fault when R = 0
  Contains physical page number (PPN) of each resident page
  Dirty bit D = 1 if we’ve changed this page since loading it from disk (and therefore need to write it to disk when it’s replaced)
PAGE MAP
X
X
X
D
R
Virtual Memory
Physical Memory
1
1
1
1
0
0
0
PPN

## Slide 11: Example: Virtual  Physical Translation
0 | 1 | 2
-- | 0 | --
0 | 1 | 4
-- | 0 | --
1 | 1 | 0
1 | 1 | 1
-- | 0 | --
-- | 0 | --
-- | 0 | --
-- | 0 | --
-- | 0 | --
-- | 0 | --
1 | 1 | 7
1 | 1 | 6
1 | 1 | 5
0 | 1 | 3
Setup:
256 bytes/page (28)
16 virtual pages (24)
8 physical pages (23)
12-bit VA (4 vpn, 8 offset)
11-bit PA (3 ppn, 8 offset)
LRU page: VPN = 0xE
LD(R31,0x2C8,R0):
VA = 0x2C8, PA = _______
16-entry
Page Map
8-page
Phys. Mem.
D R PPN
VPN 0x4
VPN 0x5
VPN 0x0
VPN 0xF
VPN 0x2
VPN 0xE
VPN 0xD
VPN 0xC
0x000
0x0FC
0x100
0x1FC
0x200
0x2FC
0x300
0x3FC
0x400
0x4FC
0x500
0x5FC
0x600
0x6FC
0x700
0x7FC
0x4C8
VPN = 0x2
→ PPN = 0x4
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
8
4
VA
offset
VPN
8
3
PA
PPN

## Slide 12: Page Faults
If a page does not have a valid translation, MMU causes a page fault. OS page fault handler is invoked, handles miss:
  Choose a page to replace, write it back if dirty. Mark page as no longer resident
      Are there any restrictions on which page we can we select? **
  Read page from secondary storage into available physical page
  Update page map to show new page is resident
  Return control to program, which re-executes memory access
Physical Memory
Page Map
CPU
Disk
R=0
Before Page Fault
R=1
VPN 1
Physical Memory
Page Map
CPU
Disk
R=0
After Page Fault
R=1
VPN 5
** https://en.wikipedia.org/wiki/Page_replacement_algorithm#Page_replacement_algorithms

## Slide 13: Example: Page Fault
0 | 1 | 2
-- | 0 | --
0 | 1 | 4
-- | 0 | --
1 | 1 | 0
1 | 1 | 1
-- | 0 | --
-- | 0 | --
-- | 0 | --
-- | 0 | --
-- | 0 | --
-- | 0 | --
1 | 1 | 7
1 | 1 | 6
1 | 1 | 5
0 | 1 | 3
Setup:
256 bytes/page (28)
16 virtual pages (24)
8 physical pages (23)
12-bit VA (4 vpn, 8 offset)
11-bit PA (3 ppn, 8 offset)
LRU page: VPN = 0xE
ST(BP,-4,SP), SP = 0x604
VA = 0x600, PA = _______
16-entry
Page Table
8-page
Phys. Mem.
D R PPN
1 1 5
-- 0 --
VPN 0x4
VPN 0x5
VPN 0x0
VPN 0xF
VPN 0x2
VPN 0xE
VPN 0xD
VPN 0xC
0x000
0x0FC
0x100
0x1FC
0x200
0x2FC
0x300
0x3FC
0x400
0x4FC
0x500
0x5FC
0x600
0x6FC
0x700
0x7FC
VPN 0x6
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
0x500
VPN = 0x6
Not resident, it’s on disk
Choose page to replace (LRU = 0xE)
D[0xE] = 1, so write 0x500-0x5FC to disk
Mark VPN 0xE as no longer resident
Read in page VPN 0x6 from disk into 0x500-0x5FC
Set up page map for VPN 0x6 = PPN 0x5
PA = 0x500
This is a write so set D[0x6] = 1
8
4
VA
offset
VPN
8
3
PA
PPN

## Slide 14: Virtual Memory: the CS View
int VtoP(int Vaddr) {
int VPageNo = Vaddr >> p;
int PO = Vaddr & ((1 << p) – 1);
if (R[VPageNo] == 0)
PageFault(VPageNo);
return (PPN[VPageNo] << p) | PO;
}
/* Handle a missing page... */
void PageFault(int VPageNo) {
int i;
i = SelectLRUPage();
if (D[i] == 1)
WritePage(DiskAdr[i],PPN[i]);
R[i] = 0;
PPN[VPageNo] = PPN[i];
ReadPage(DiskAdr[VPageNo],PPN[i]);
R[VPageNo] = 1;
D[VPageNo] = 0;
}
Virtual Page #
Physical Page #
Problem: Translate
VIRTUAL ADDRESS
to PHYSICAL ADDRESS
Multiply by 2P, the page size

## Slide 15: The HW/SW Balance
IDEA:
  devote HARDWARE to high-traffic, performance-critical path
  use (slow, cheap) SOFTWARE to handle exceptional cases
HARDWARE performs address translation, detects page faults:
  running program interrupted (“suspended”);
  PageFault(…) is forced;
  On return from PageFault; running program continues
int VtoP(int VPageNo,int PO) {
if (R[VPageNo] == 0)PageFault(VPageNo);
return (PPN[VPageNo] << p) | PO;
}
/* Handle a missing page... */
void PageFault(int VPageNo) {
int i = SelectLRUPage();
if (D[i] == 1) WritePage(DiskAdr[i],PPN[i]);
R[i] = 0;
PA[VPageNo] = PPN[i];
ReadPage(DiskAdr[VPageNo],PPN[i]);
R[VPageNo] = 1;
D[VPageNo] = 0;
}
hardware
software

## Slide 16: Page Map Arithmetic
PAGEMAP
PHYSICAL MEMORY
D
R
PPN
Vpage#
PO
1
1
1
0
1
p
v
Ppage#
PO
m
(v + p) bits in virtual address
(m + p) bits in physical address
2v number of VIRTUAL pages
2m number of PHYSICAL pages
2p bytes per physical page
2v+p bytes in virtual memory
2m+p bytes in physical memory
(m+2)2v bits in the page map
Typical page size: 4KB -16 KB
Typical (v+p): 32-64 bits
(4GB-16EB)
Typical (m+p): 30-40+ bits (1GB-1TB)
Long virtual addresses allow ISAs to support larger memories  ISA longevity

## Slide 17: Example: Page Map Arithmetic
Virtual Page #
PhysPg #
SUPPOSE...
  32-bit Virtual address (v+p)
  30-bit physical address (m+p)
  4 KB page size (p = 12)
THEN:
  # Physical Pages = ___________
  # Virtual Pages = _____________
  # Page Map Entries = _________
  # Bits In pagemap = __________
Use fast SRAM for page map??? OUCH!
218 = 256K
220
220 = 1M
20*220 ~ 20M
0
11
12
31
0
11
12
29
12
20
18

## Slide 18: RAM-Resident Page Maps
Small page maps can use dedicated SRAM… gets expensive for big ones!
Solution: Move page map to main memory:
Virtual Address
Physical Memory
virtual page number
physical page number
Physical memory pages that hold page map entries
PROBLEM Each memory reference
now takes 2 accesses
to physical memory!
+
Page Map Ptr

## Slide 19: Translation Look-aside Buffer (TLB)
Problem: 2x performance hit… each memory reference now takes 2 accesses!
Solution: Cache the page map entries
physical page number
IDEA: LOCALITY in memory
reference patterns → SUPER locality in
references to page map
VARIATIONS:
multi-level page map
paging the page map!
TLB: small cache of page table entries
Associative lookup by VPN
Virtual Address
Physical Memory
virtual page number
physical page number
+
Page Tbl Ptr
TLB hit
TLB miss
https://en.wikipedia.org/wiki/Translation_lookaside_buffer

## Slide 20: MMU Address Translation
32
32-bit virtual address
3
Page fault
(handled by SW)
1
Look in TLB: VPN→PPN cache
Usually implemented as a small fully-associative cache
2
Data
20
12
PTBL
D R PPN
virtual page number
20
12

## Slide 21: Putting it All Together: MMU with TLB
Suppose
  virtual memory of 232 bytes
  physical memory of 224 bytes
  page size is 210 (1 K) bytes
  4-entry fully associative TLB
  [p = 10, v = 22, m = 14]
How many pages can reside in physical memory at one time?
How many entries are there in the page table?
How many bits per entry in the page table? (Assume each entry has PPN, resident bit, dirty bit)
How many pages does the page table occpy?
What fraction of virtual memory can be resident?
What is the physical address for virtual address 0x1804? What components are involved in the translation?
Same for 0x1080
Same for 0x0FC
R D PPN
-------
0 0 7
1 1 9
1 0 0
0 0 5
1 0 5
0 0 3
1 1 2
1 0 4
1 0 1
…
214
222
16
223 bytes = 213 pages
1/28
VPN | R D PPN
----+--------
0 | 0 0 3
6 | 1 1 2
1 | 1 1 9
3 | 0 0 5
Page Map
TLB
Tag
Data
VPN
0
1
2
3
4
5
6
7
8
[VPN=6] 0x804
[VPN=4] 0x1480
[VPN=0] page fault

## Slide 22: Contexts
A context is a mapping of VIRTUAL to PHYSICAL locations, as dictated by contents of the page map:
PAGEMAP
X
X
X
D
R
Virtual Memory
Physical Memory
Several programs may be simultaneously loaded into main memory, each in its separate context:
Virtual
Memory 1
Virtual
Memory 2
Physical
Memory
“Context switch”:
reload the page map?
map1
map2

## Slide 23: Contexts: A Sneak Preview
Virtual
Memory 1
Virtual
Memory 2
Physical
Memory
1. TIMESHARING among several programs
  • Separate context for each program
  • OS loads appropriate context into page map when switching among programs
2. Separate context for OS “Kernel” (e.g., interrupt handlers)...
  • “Kernel” vs “User” contexts
  • Switch to Kernel context on interrupt;
  • Switch back on interrupt return.
First Glimpse of a
VIRTUAL MACHINE

## Slide 24: Memory Management & Protection
Applications are written as if they have access to the entire virtual address space, without considering where other applications reside
  Enables fixed conventions (e.g., program starts at 0x1000, stack is contiguous and grows up, …) without worrying about conflicts
OS Kernel controls all contexts, prevents programs from reading and writing into each other’s memory
Stack
Code
Heap
Address Space

## Slide 25: Multi-level Page Maps
32
32-bit virtual address
3
Page fault
(handled by SW)
1
2
Data
10
12
PDIR
D R PPN
10
virtual page number
20
12
Page Directory
(1 page)
Partial Page Table
(1 page)
D R PPN
Instead of one page map with 220 entries, “virtualize the page table”:
One permanently-resident page holds “page directory” which has 1024 entries pointing to 1024-entry partial page tables in virtual memory!
Translation
Look-aside
Buffer

## Slide 26: Rapid Contex -Switching
physical page number
Virtual Address
Physical Memory
Context & Virtual page number
physical page number
+
PageTblPtr
TLB hit
TLB miss
Context #
Add a register to hold index of current context. To switch contexts: update Context # and PageTblPtr registers. Don’t have to flush TLB since each entry’s tag includes context # in addition to virtual page number

## Slide 27: Using Caches with Virtual Memory
Cache
MMU
CPU
Main memory
Virtually-Addressed Cache
Tags from virtual addresses
FAST: No MMU time on HIT
Problem: Must flush cache after context switch
Physically-Addressed Cache
Tags from physical addresses
Avoids stale cache data after context switch
SLOW: MMU time on HIT
Cache
MMU
CPU
Main memory

## Slide 28: Best of Both Worlds: Overlapped Operation
OBSERVATION: If cache index bits are a subset of page offset bits, tag access in a physical cache can overlap page map access. Tag from cache is compared with physical page address from MMU to determine hit/miss.
Problem: Limits # of bits of cache index → increase cache capacity by increasing associativity
Cache
CPU
Main memory
MMU
Cache index comes entirely from address bits in page offset – don’t need to wait for MMU to start cache lookup!

## Slide 29: Summary: Virtual Memory
Goal 1: Exploit locality on a large scale
  Programmers want a large, flat address space, but use a small portion!
  Solution: Cache working set into RAM from disk
  Basic implementation: MMU with single-level page map
    Access loaded pages via fast hardware path
    Load virtual memory on demand: page faults
  Several optimizations:
    Moving page map to RAM, for cost reasons
    Translation Lookaside Buffer (TLB) to regain performance
  Cache/VM interactions: Can cache physical or virtual locations
Goals 2 & 3: Ease memory management, protect multiple contexts from each other
  We’ll see these in detail on the next lecture!