## Slide 1: 3. CMOS Technology

## Slide 2: Combinational Device Wish List
Design our system to tolerate some amount of error ⇒ Add positive noise margins ⇒ VTC: gain>1 & nonlinearity
Lots of gain ⇒ big noise margin
Cheap, small
Changing voltages will require us to dissipate power, but if no voltages are changing, we’d like zero power dissipation
Want to build devices with useful functionality (what sort of operations do we want to perform?)
VOL
VIL
VIH
VOH
Vin
Vout
Vin
Vout

## Slide 3: N-Channel MOSFET: Physical View
W
L
gate
drain
source
bulk
Polysilicon wire
Doped p-type silicon substrate
Inter-layer SiO2 insulation
Very thin (<20Å) high-quality SiO2 insulating layer isolates gate from channel region.
Heavily doped n-type diffusions
Channel region: electric field from charges on gate locally “inverts” type of substrate to create a conducting channel between source and drain.
MOSFETs (metal-oxide-semiconductor field-effect transistors) are four-terminal voltage-controlled switches. Current flows between the diffusion terminals if the voltage on the gate terminal is large enough to create a conducting “channel”, otherwise the mosfet is off and the diffusion terminals are not connected.
IDS ∝ W/L
IDS

## Slide 4: N-Channel MOSFET: Electrical View
The four terminals of a Field Effect Transistor (gate, source, drain and bulk) connect to conductors that generate a set of electric fields in the channel region which depend on the relative voltages of each terminal.
Olivier Deleage and Peter Scott (CC BY-SA 3.0)
Want VP ≤ VN
Notes: http://commons.wikimedia.org/wiki/File:MOSFET_functioning.svg

## Slide 5: N-channel MOSFET IDS vs. VDS
Ohmic: IDS = VDS/R
saturated
VTH = 0.5V
Increasing VGS
IDS
VDS

## Slide 6: FETs Come in Two Flavors
The use of both NFETs and PFETs – complimentary transistor types – is a key to CMOS (complementary MOS) logic families.
p
p
n
G
D
S
B
G
S
D
B
G
S
D
B
Connect B to GND to keep PN reverse-biased
(Vp ≤ Vn); keeps D and S insulated from B
Connect B to VDD to keep PN reverse-biased
n
n
p
D
S
G
B
NFET: n-type source/drain diffusions in a p-type substrate. Positive threshold voltage; inversion forms n-type channel
PFET: p-type source/drain diffusions in a n-type substrate. Negative threshold voltage; inversion forms p-type channel.

## Slide 7: CMOS Recipe
D (higher potential)
G
S (lower potential)
S
D
NFET Operating regions:
“off”:
VGS < VTH,NFET
PFET Operating regions:
“off”:
VGS > VTH,PFET
S
D
If we follow two rules when constructing CMOS circuits, we can model the behavior of the mosfets as simple voltage-controlled switches:
Rule #1: only use NFETs in pulldown circuits
PFET threshold = ~ −0.5V
S (higher potential)
G
D (lower potential)
VGS⬆︎ ⇒ “R”⬇︎
Rule #2: only use PFETs in pullup circuits
“0” → off
“1” → on
“1” → off
“0” → on
S
D
“
“
NFET threshold = ~0.5V
“on”:
VGS > VTH,NFET
S
D
“
“
“on”:
VGS < VTH,PFET

## Slide 8: CMOS Inverter VTC
VOL
VIL
VIH
VOH
Vin
Vout
Ipu
Ipd
Steady state reached when Vout reaches value where Ipu = Ipd.
When VIN is low, the nfet is off and the pfet is on, so current flows into the output node and VOUT eventually reaches VDD (> VOH) at which point no more current will flow.
Pfet “on” nfet “off”
When VIN is high, the pfet is off and the nfet is on, so current flows out of the output node and VOUT eventually reaches GND (< VOL) at which point no more current will flow.
Pfet “off” nfet “on”
When VIN is in the middle, both the pfet and nfet are “on” and the shape of the VTC depends on the details of the devices’ characteristics. CMOS gates have very high gain in this region (small changes in VIN produce large changes in VOUT) and the VTC is almost a step function.
S
D
G
S
D
G
VDD
pullup
pulldown

## Slide 9: Beyond Inverters: Complementary pullups and pulldowns
We want complementary pullup and pulldown logic, i.e., the pulldown should be “on” when the pullup is “off” and vice versa.
pullup
pulldown
F(inputs)
on
off
driven “1”
off
on
driven “0”
on
on
driven “X”
off
off
no connection
Now you know what the “C”
in CMOS stands for!
Since there’s plenty of capacitance on the output node, when the output becomes disconnected it “remembers” its previous voltage -- at least for a while. The “memory” is the load capacitor’s charge. Leakage currents will cause eventual decay of the charge (that’s why DRAMs need to be refreshed!).
Pullup switches
Pulldown switches
Power supply
Ground
output
inputs

## Slide 10: CMOS Complements
What a nice VOH you have...
Thanks. It runs in the family...
conducts when A is high
conducts when A is low: A
conducts when A is high and B is high: A.B
A
B
A
B
conducts when A is low or B is low: A+B = A.B
conducts when A is high or B is high: A+B
A
B
A
B
conducts when A is low and B is low: A.B = A+B
A
A

## Slide 11: A Pop Quiz!
What function does
this gate compute?
A B Z
0 0
0 1
1 0
1 1
1
16λ
82λ
Current technology:λ= 14nm
COST for an older 45nm process:
$3500 per 300mm wafer
300mm round wafer = π(150e-3)2 = .07m2
NAND gate = (82)(16)(45e-9)2=2.66e-12m2
2.6e10 NAND gates/wafer (= 100 billion FETS!)
marginal cost of NAND gate: 132n$
NAND
1
1
0

## Slide 12: General CMOS Gate Recipe
Step 1. Figure out the pullup network that does what you want, e.g.,
(Determine what combination of inputs generates a high output)
A
B
C
Step 2. Walk the hierarchy replacing nfets with pfets, series subnets with parallel subnets, and parallel subnets with series subnets
A
B
C
Step 3. Combine pfet pullup network from Step 1 with nfet pulldown network from Step 2 to form a fully-complementary CMOS gate.
A
B
C
A
B
C
Does this recipe work for all logic functions?

## Slide 13: CMOS Gates Are Naturally Inverting
In a CMOS gate, rising inputs (0→1) lead to falling outputs
NFETs go from “off” to “on” → pulldown paths connected → output may be connected to ground
PFETs go from “on” to “off” → pullup paths disconnected → output may be disconnected from VDD
Corollary: you can’t build positive logic, e.g., AND, with one CMOS gate
A B A∙B
0 0
0 1
1 0
1 1
0
0
0
1
A=1, B rising…
Oops, output is
also rising!
For CMOS gate:
All inputs 0 → nfets off, pfets on → output must be 1
All inputs 1 → nfets on, pfets off → output must be 0

## Slide 14: CMOS Timing Specifications
VOUT
time constant
τ = RPD∙CL
time constant
τ = RPU∙CL
VIN
Electrical model:
Waveforms:
Circuit:
VIN
R
Vout
CW
CP
CN

## Slide 15: Propagation Delay
Propagation delay (tPD): An UPPER BOUND on the delay from valid inputs to valid outputs.
GOAL:
minimize
propagation
delay!
ISSUE:
keep capacitances
low and transistors fast
VOUT
≤ tPD
≤ tPD
VIN
VOL
VOH
VIL
VIH

## Slide 16: Contamination Delay
Contamination delay (tCD): A LOWER BOUND on the delay from any invalid input to an invalid output
VOUT
VIN
VOL
VOH
VIL
VIH
≥ tCD
≥ tCD
Do we really need tCD?
Usually not… it’ll be important when we design circuits with registers (coming soon!)
If tCD is not specified, safe to assume it’s 0.

## Slide 17: The Combinational Contract
A
B
A B
0 1
1 0
tPD propagation delay
tCD contamination delay
A
B
Must be ___________
Must be ___________
Notes:
1. No Promises during
2. Default (conservative) spec: tCD = 0
≤ tPD
≥ tCD

## Slide 18: Acyclic Combinational Circuits
If NAND gates have a tPD = 4nS and tCD = 1nS
B
C
A
Y
tPD = _______ nS
tCD = _______ nS
12
2
tPD is the maximum cumulative propagation delay over all paths from inputs to outputs
tCD is the minimum cumulative contamination delay over all paths from inputs to outputs

## Slide 19: One Last Timing Issue…
Recall the rules for combinational devices:
Output guaranteed to be valid when all inputs have been valid for at least tPD, and, outputs may become invalid no earlier than tCD after an input changes!
A
B
Z
tPD
tCD
A
Z
B
0
0
1
1
0
1
0
1
1
0
0
0
A
B
Z
NOR:
A
B
Z
tPD
tCD
Many gate implementations—e.g., CMOS— adhere to even tighter restrictions.

## Slide 20: What Happens In This Case?
A
B
Z
tPD
tCD
A
B
Z
A
B
Z
0
X
1
0
1
X
1
0
0
A
B
Z
0
0
1
1
0
1
0
1
1
0
0
0
A
B
Z
NOR:
Lenient
NOR:
LENIENT Combinational Device: Output guaranteed to be valid when any combination of inputs sufficient to determine the output value has been valid for at least tPD. Tolerates transitions -- and invalid levels -- on irrelevant inputs!
CMOS NOR:
Input A=1 is sufficient to determine the output
X
X
X

## Slide 21: Summary
CMOS
  Only use NFETs in pulldowns, PFETs in pullups → mosfets behave as voltage-controlled switches
  Series/parallel Pullup and pulldown switch circuits are complementary
  CMOS gates are naturally inverting (rising input transition can only cause falling output transition, and vice versa).
  “Perfect” VTC (high gain, VOH = VDD, VOL = GND) means large noise margins and no static power dissipation.
Timing specs
  tPD: upper bound on time from valid inputs to valid outputs
  tCD: lower bound on time from invalid inputs to invalid outputs
  If not specified, assume tCD = 0
  Lenient gates: output unaffected by some input transitions
Next time: logic simplification, other canonical forms