## Slide 1: The Digital Abstraction
1
1
0
0
1
0
0
1
0
0
1
Making bits concrete
Analog issues
Digital signaling
The static discipline
Noise margins

## Slide 2: Concrete Encoding of Information
To this point we’ve discussed encoding information using bits. But where do bits come from?
If we’re going to design a machine that manipulates information, how should that information be physically encoded?
What makes a good bit?
- small, inexpensive (we want a lot of them)
- stable (reliable, repeatable)
- ease and speed of manipulation (access, transform, combine, transmit, store)
Captmondo (CC BY-SA 3.0)
Rosetta Stone
Madeleine Price Ball (CC BY-SA 3.0)
DNA
Notes: https://en.wikipedia.org/wiki/DNA#mediaviewer/File:DNA_chemical_structure.svg
https://en.wikipedia.org/wiki/Rosetta_Stone#mediaviewer/File:RosettaStoneAsPartOfOriginalStele.jpg

## Slide 3: Let’s Use Electrical Phenomenon…
Consider using phenomenon associated with charged particles:
voltages phase
currents frequency
In this course we’ll use voltages to encode information. But the best choice depends on the intended application…
zero
Voltage pros:
easy generation, detection
lots of engineering knowledge
potentially low power in steady state
Voltage cons:
easily affected by environment
DC connectivity required?
R & C effects slow things down

## Slide 4: Representing Information with Voltage
Representation of each (x,y) point on a B&W image:
0 volts: BLACK
1 volt: WHITE
0.37 volts: 37% Gray
How much information at each point?
John Phelan (CC BY 3.0)
Suppose we can reliably distinguish voltages that differ by 1/2N volts. Then we can represent N bits of information by voltages in the range 0V to 1V. What are realistic values for N?
Notes: https://en.wikipedia.org/wiki/Massachusetts_Institute_of_Technology#mediaviewer/File:MIT_Building_10_and_the_Great_Dome,_Cambridge_MA.jpg

## Slide 5: Using Voltages to Encode a Picture
Representation of a picture:
Scan points in some prescribed raster order… Generate voltage waveform:
John Phelan (CC BY 3.0)
NTSC TV signal
white
black
sync
Notes: https://en.wikipedia.org/wiki/Massachusetts_Institute_of_Technology#mediaviewer/File:MIT_Building_10_and_the_Great_Dome,_Cambridge_MA.jpg

## Slide 6: Information Processing = Computation
Pre-packaged functionality: rely on behavior without having to be an analog engineer
Predictable composition of functions → Tinker-toy assembly
Guaranteed behavior: if components work, system will work!
v
Copy
v
Inv
v
1-v
Why have processing blocks?
Wow, rules simple enough for a programmer to follow!

## Slide 7: Let’s Build a System!
?
Copy
Inv
Copy
Inv
Copy
Inv
Copy
Inv
output
input
(In Theory)
(Reality)

## Slide 8: Why Did Our System Fail?
Why doesn’t theory match reality?
  1. COPY block doesn’t work right
  2. INV block doesn’t work right
  3. Theory is imperfect
  4. Reality is imperfect
  5. Our system architecture stinks
ANSWER: all of the above!
Noise and inaccuracy are inevitable; we can’t reliably reproduce infinite information − we must design our system to tolerate some amount of error if it is to process information reliably.

## Slide 9: The Digital Abstraction
Real World
“Ideal” Abstract World
Volts or
Electrons or
Ergs or Gallons
Bits
0/1
Keep in mind that the world is not digital, we would simply like to engineer it to behave that way. Furthermore, we must use real physical phenomena to implement digital designs!
Noise
Manufacturing Variations

## Slide 10: Using Voltages “Digitally”
Key idea: encode only one bit of information: 2 values “0”, “1”
Use the same uniform representation convention for every component and wire in our digital system
Attempt #1:
volts
VTH
V < VTH
interpreted as “0”
V ≥ VTH
interpreted as “1”
✗
V ≤ VL
interpreted as “0”
V ≥ VH
interpreted as “1”
VL
VH
Attempt #2:
volts
VL< V < VH
“Forbidden to ask”
✓?
Hard to distinguish VTH-εfrom VTH+ε

## Slide 11: A Digital Processing Element
Static
discipline
Output a “1” if at
least 2 out of 3 of
my inputs are a “1”.
Otherwise, output “0”.
I will generate a valid
output in no more than
2 minutes after
seeing valid inputs
input A
input B
input C
output Y
A combinational device is a circuit element that has
  one or more digital inputs
  one or more digital outputs
  a functional specification that details the value of each output for every possible combination of valid input values
  a timing specification consisting (at minimum) of an upper bound tPD on the required time for the device to compute the specified output values from an arbitrary set of stable, valid input values

## Slide 12: A Combinational Digital System
A set of interconnected elements is a combinational device if
  each circuit element is combinational
  every input is connected to exactly one output or to some vast supply of constant 0’s and 1’s
  the circuit contains no directed cycles
Why is this true?

## Slide 13: Is This a Combinational Device?
A, B and C are combinational devices. Is the following circuit a combinational device?
A
B
C
Does it have digital inputs?
Does it have digital outputs?
Can you derive a functional description?
Can you derive a tPD?
P
Q
R
S

## Slide 14: Will This System Work?
Combinational
device
Combinational
device
Upstream device transmits a signal at VL-ε, a valid “0”. Noise on the connecting wire causes the downstream device to receive VL+ε, a signal in the forbidden zone.
Noise
Valid “0”: VL-ε
VL+ε: not a valid signal
Hmm. Looks like the output voltage needs to be adjusted so that a signal will still be valid when it reaches an input even if there’s noise.

## Slide 15: Where Does Noise Come From?
Parasitic resistance, inductance, capacitance
  IR drop, L(dI/dt) drop, LC ringing from current steps
Imprecision of component values
  Manufacturing variations, allowable tolerances
Environmental effects
  External EM fields, temperature variations, etc.
…
+
-
Integrated circuit
R’s and C’s from Aluminum wiring layers
Current loads from on-chip devices
Power supply
L’s from chip leads

## Slide 16: Needed: Noise Margins!
A combinational device accepts marginal inputs and provides unquestionable outputs (to leave room for noise).
volts
NOISE MARGINS
Forbidden Zone
VIL
VIH
VALID INPUT REPRESENTATIONS
Valid
“0”
Valid
“1”
VOL
VOH
VALID OUTPUT REPRESENTATIONS
Proposed fix: separate specifications for inputs and outputs
digital output: “0” ≤ VOL, “1” ≥ VOH
digital input: “0” ≤ VIL, “1” ≥ VIH
VOL < VIL < VIH < VOH

## Slide 17: A Buffer
0
0
1
1
A simple combinational device:
Static Discipline requires that the VTC avoid the shaded regions (aka “forbidden zones”), which correspond to valid inputs but invalid outputs.
Voltage Transfer Characteristic (VTC):
Plot of Vout vs. Vin where each measurement is taken after any transients have died out.
Vout
Vin
VOL
VOH
VIL
VIH
Note: VTC does not tell you anything about how fast a device is — it measures static behavior not dynamic behavior

## Slide 18: Voltage Transfer Characteristic
Vout
Vin
VOL
VOH
VIL
VIH
2) Note that the center white region is taller than it is wide (VOH-VOL > VIH-VIL). Net result: combinational devices must have GAIN > 1 and be NONLINEAR.
1) Note the VTC can do anything when VIL < VIN < VIH.

## Slide 19: Can This Be a Combinational Inverter?
VOUT
VIN
1
2
3
4
5
0
0
1
2
3
4
5
(0,5)
(1,4)
(2.5,1)
(3,0.5)
VOL
Suppose that you measured the voltage transfer curve of the device shown below. Can we find a signaling specification that would allow this device to be a combinational inverter?
The device must be able to actually produce the desired output level. Thus, VOL can be no lower than 0.5 V.
VIH
VIL
VOH
VIH must be high enough to produce VOL
Now, find noise margin N and compute
  VOH = VIH + N
  VIL = VOL + N
Try VOL = 0.5 V
Try VIH = 3 V
Try N = 0.5 V
Then verify that VOUT ≥ VOH when VIN ≤ VIL.
Device is a combinational inverter when VOL=0.5, VIL=1, VIH=3, VOH=3.5

## Slide 20: Summary
Use voltages to encode information
“Digital” encoding
  valid voltage levels for representing “0” and “1”
  forbidden zone avoids mistaking “0” for “1” and vice versa
  gives rise to notion of signal VALIDITY.
Noise
  Want to tolerate real-world conditions: NOISE.
  Key: tougher standards for output than for input
  devices must have gain and have a non-linear VTC
Combinational devices
  Each logic family has Tinkertoy-set simplicity, modularity
  predictable composition: “parts work → whole thing works”
  static discipline
    digital inputs, outputs; restore marginal input voltages
    complete functional spec
    valid inputs lead to valid outputs in bounded time

## Slide 21: Next Time: Building Logic with Transistors
It’s about
time!
I’d have preferred the DNA…