## Slide 1: Finite State Machines
State transition diagrams
FSM party games!
Example: RoboAnt
Metastability
Finally!
Some ENGINEERING!
Great -- Theory!

## Slide 2: Our New Machine
Combinational
Logic
Current
State
Next
State
Input
Output
Clock
State Registers
k
k
m
n
Acyclic graph
Obeys static discipline
Can be exhaustively enumerated by a truth table of 2k+m rows and k+n output columns
Engineered cycles
Works only if dynamic discipline obeyed
Remembers k bits for a total of 2k unique combinations

## Slide 3: A Simple Sequential Circuit…
Lets make a digital binary Combination Lock:
Specification:
  One input ( “0” or “1”)
  One output (“Unlock” signal)
  UNLOCK is 1 if and only if:
    Last 4 inputs were the “combination”: 0110
Lock
IN
U
CLK
How many state bits do I need?

## Slide 4: Abstraction du jour: Finite State Machines
A FINITE STATE MACHINE has
Clocked
FSM
k STATES: S1 … Sk (one is “initial” state)
m INPUTS: I1 … Im
n OUTPUTS: O1 … On
Transition Rules: s’(s, I) for each state s and input I
Output Rules: Out(s) or Out(s, I) for each state s and input I
m
inputs
n
outputs

## Slide 5: State Transition Diagram
SX
U=0
S0
U=0
0
S01
U=0
1
S011
U=0
1
S0110
U=1
0
1
0
0
0
1
1
XXX
U=0
NAME
of state
OUTPUT
when in this
state
0
INPUT
causing
transition
Heavy circle
Means
INITIAL state
Designing our lock …
Need an initial state; call it SX.
Must have a separate state for each step of the proper entry sequence
Must handle other (erroneous) entries
Why do these
go to S0 and S01?

## Slide 6: Valid State Diagrams
Arcs leaving a state must be:
(1) mutually exclusive
  can’t have two choices for a given input value
(2) collectively exhaustive
  every state must specify what happens for each possible input combination. “Nothing happens” means arc back to itself.
S1
S3
0
0
S2
1
1
1
0
1
0
MOORE Machine:
Outputs on States
S1
S3
0/0
0/1
S2
1/0
1/0
1/0
MEALY Machine:
Outputs on Transitions
0
0/0
Inputs/outputs

## Slide 7: State Transition Diagram as a Truth Table
SX
U=0
S0
U=0
0
S01
U=0
1
S011
U=0
1
S0110
U=1
0
1
0
0
0
1
1
All state transition diagrams can be described by truth tables…
Binary encodings are assigned to each state (a bit of an art)
The truth table can then be simplified using the reduction techniques we learned for combinational logic
IN Current State Next State Unlock
0 SX S0 0
1 SX SX 0
0 S0 S0 0
1 S0 S01 0
0 S01 S0 0
1 S01 S011 0
0 S011 S0110 0
1 S011 SX 0
0 S0110 S0 1
1 S0110 S01 1
000 000
001 001
011 011
010 010
100 100
001 000
001 011
001 010
100 000
001 011
The assignment of codes to states can be arbitrary, however, if you choose them carefully you can greatly reduce your logic requirements.

## Slide 8: Now Put It In Hardware!
ROM
16x4
unlock
Next state
Current state
IN
Trigger update periodically (“clock”)
3
3
We assume
inputs are
synchronized
with clock…
5 states
⇒ 3-bit encoding
4 inputs ⇒ 24 locations, each location supplies
4 bits

## Slide 9: Discrete State, Discrete Time
Clock
STATE
NEXT
Clock
Period
1
Clock
Period
2
Clock
Period
3
Clock
Period
4
Clock
Period
5
ROM
NEXT
STATE
inputs
outputs
s
s
s state bits ⇒ 2s possible states
Two design choices:
(1) outputs only depend on state
(2) outputs depend on inputs + state
(Moore)
(Mealy)

## Slide 10: Housekeeping Issues…
ROM
or
gates
NEXT
STATE
inputs
outputs
s
s
1. Initialization? Clear the memory?
2. Unused state encodings? - waste ROM (use gates)
- what does it mean? - can the FSM recover?
3. Choosing encoding for state?
4. Synchronizing input changes with
state update?
IN
CLK
U
Now, that’s a funny looking state machine
reset
1 0
initial

## Slide 11: FSM States
ROM
k
k
1. What can you say about the number of states?
2. Same question:
m
States
n
States
x
y
z
3. Here’s an FSM. Can you discover its rules?
You Win!
1
0

## Slide 12: What’s My Transition Diagram?
1
0
1
0
1
0
1
1
0
1
0
1
0
0
vs.
0=OFF,
1=ON?
"1111" =
Surprise!
If you know NOTHING about the FSM, you’re never sure!
If you have a BOUND on the number of states, you can discover its behavior:
K-state FSM: Every (reachable) state can be reached in < k steps.
BUT ... FSMs may be equivalent!
1
You Win!
1
0

## Slide 13: FSM Equivalence
1
0
1
0
1
0
1
1
0
1
0
1
0
0
vs.
ARE THEY DIFFERENT?
  NOT in any practical sense! They are EXTERNALLY INDISTINGUISHABLE, hence interchangeable.
FSMs are EQUIVALENT iff every input sequence yields identical output sequences.
ENGINEERING GOAL:
  • HAVE an FSM which works...
  • WANT simplest (ergo cheapest) equivalent FSM.

## Slide 14: Let’s Build a RoboAnt
SENSORS: antennae L and R, each 1 if in contact with something.
ACTUATORS: Forward Step F, ten-degree turns TL and TR (left, right).
8 legs?
GOAL: Make our ant smart enough to get out of a maze like:
STRATEGY: "Right antenna to the wall"

## Slide 15: Lost In Space
?
LOST
F
L+R
_ _
L R
“lost” is the
initial state
Action: Go forward until we hit something.

## Slide 16: Bonk!
LOST
F
L+R
_ _
L R
RCCW
L+R
TL
_ _
L R
Action: Turn left (CCW) until we don’t touch anymore

## Slide 17: A Little to the Right…
LOST
F
RCCW
L+R
L+R
Wall1
TR,F
R
_
R
TL
_ _
L R
_ _
L R
Action: Step and turn right a little, look for wall

## Slide 18: Then a Little to the Left
LOST
F
Wall1
TR,F
RCCW
R
L+R
L+R
_
R
TL
_ _
L R
_ _
L R
_ _
L R
Wall2
TL,F
L
_
L R
Action: Step and turn left a little, till not touching (again)

## Slide 19: Dealing With Outside Corners
LOST
F
Wall2
TL,F
Wall1
TR,F
RCCW
R
L+R
L+R
_
R
L
TL
_ _
L R
_ _
L R
_ _
L R
_
L R
TR,F
Corner
R
_
R
Action: Step and turn right until we hit perpendicular wall
Hey, this might
even work!

## Slide 20: Equivalent State Reduction
Observation: two states are equivalent if
1. Both states have identical outputs; AND
2. Every input ⇒ equivalent states.
Reduction Strategy:
  Find pairs of equivalent states, MERGE them.
LOST
F
Wall2
TL,F
Wall1
TR,F
RCCW
R
L+R
L+R
_
R
L
TL
_ _
L R
_ _
L R
_ _
L R
_
L R
TR,F
Corner
R
_
R

## Slide 21: An Evolutionary Step
Behaves exactly as previous (5-state) FSM, but requires half the ROM in its implementation!
Merge equivalent states Wall1 and Corner into a single new, combined state.
LOST
F
Wall2
TL,F
Wall1
TR,F
RCCW
R
L+R
L+R
_
R
L
TL
_ _
L R
_ _
L R
_ _
L R
_
L R

## Slide 22: Building The Transition Table
00 0 1 | 01 0 0 1 00 1 0 | 01 0 0 1
00 1 1 | 01 0 0 1
L+R
L+R
01 0 1 | 01 0 1 0
01 1 0 | 01 0 1 0
01 1 1 | 01 0 1 0
RCCW
TL
S L R | S’ TR TL F -------+-----------
00 0 0 | 00 0 0 1
LOST
F
_ _
L R

## Slide 23: Implementation Details
S L R | S’ TR TL F -------+-----------
00 0 0 | 00 0 0 1
00 1 - | 01 0 0 1 00 - 1 | 01 0 0 1 01 1 - | 01 0 1 0
01 - 1 | 01 0 1 0
01 0 0 | 10 0 1 0
10 – 0 | 10 1 0 1 10 – 1 | 11 1 0 1 11 1 - | 01 0 1 1
11 0 0 | 10 0 1 1
11 0 1 | 11 0 1 1
LOST
RCCW
WALL1
WALL2
S1’ S1S0
00 01 11 10
00 0 1 1 1
LR 01 0 0 1 1
11 0 0 0 1
10 0 0 0 1
S0’ S1S0
00 01 11 10
00 0 0 0 0
LR 01 1 1 1 1
11 1 1 1 1
10 1 1 1 0
Complete Transition table

## Slide 24: Ant Schematic

## Slide 25: FSMs All the Way Down?
• More than ants:
Swarming, flocking, and schooling can result from collections of very simple FSMs
• Perhaps most physics:
Cellular automata, arrays of simple FSMs, can more accurately model fluids than numerical solutions to PDEs
• What if: We replaced the ROM with a RAM and have outputs that modify the RAM?
... You'll see FSMs for the rest of your life!
I prefer to think we ascended…
Did we all descend from FSMs???

## Slide 26: The World Doesn’t Run on Our Clock!
What if each button input is an asynchronous 0/1 level?
Lock
B1
U
B0
0
1
0
1
To build a system with asynchronous inputs, we have to break the rules: we cannot guarantee that setup and hold time requirements are met at the inputs!
So, we need a “synchronizer” at each input:
0
1
(Unsynchronized)
U(t)
(Synchronized)
S(t)
Clock
Synchronizer
Valid except for brief periods following active clock edges
But what about the
dynamic
discipline?

## Slide 27: The Bounded-time Synchronizer
Sync
IN
CLK
S
IN:
CLK:
a
t
t
IN
a
t
t
C
Synchronizer specifications:
finite tD (decision time)
finite tE (allowable error)
value of S at time tC+tD:
  1 if tIN < tC – tE
  0 if tIN > tC + tE
  0, 1 otherwise
IN:
CLK:
S:
t
D
>
t
E
CASE 1
t
D
>
t
E
CASE 2
t
D
CASE 3
UNSOLVABLE
For NO finite values of tE and tD is this spec realizable, even with reliable components!
A classic problem

## Slide 28: Unsolvable? That can’t be true…
Let’s just use a D Register:
D
Q
IN:
CLK:
a
t
t
IN
a
t
t
C
DECISION TIME is TPD of register.
ALLOWABLE ERROR is max(tSETUP, tHOLD)
Our logic:
TPD after TC, we’ll have
  Q=1 iff tIN + tSETUP < tC
  Q=0 iff tC + tHOLD < tIN
  Q=0 or 1 otherwise.
We’re lured by the digital abstraction into assuming that Q must be either 1 or 0. But let’s look at the input latch in the flip flop when IN and CLK change at about the same time...
G
D
Q
G
D
Q
IN
CLK
input
output

## Slide 29: The Mysterious Metastable State
Vin
Vout
VTC of “closed” latch
VTC of feedback path (Vin=Vout)
Latched in a ‘0’ state
Latched in a ‘1’ state
Latched in an undefined state
Y
0
1
Q
Vout
Vin
Recall that the latch output is the solution to two simultaneous constraints:
1. The VTC of path thru MUX; and
2. Vin = Vout
In addition to our expected stable solutions, we find an unstable equilibrium in the forbidden zone called the “Metastable State”

## Slide 30: Metastable State: Properties
It corresponds to an invalid logic level.
It’s an unstable equilibrium; a small perturbation will cause it to move toward a stable 0 or 1.
It will settle to a valid 0 or 1... eventually.
BUT – depending on how close it is to the Vin=Vout “fixed point” of the device – it may take arbitrarily long to settle out.
EVERY bistable system exhibits at least one metastable state!
metastable state
If metastable at t0:
p(metastable at t0+T) decreases exponentially with increasing T
p(metastable at t0+T) > 0 for finite T

## Slide 31: Solution: Delay Increases Reliability
D Q
D Q
Out
Combinational
logic
D Q
In
Clk
D Q
D Q
Out
Combinational
logic
D Q
D Q
In
Clk
Extra registers between the asynchronous input and your logic are the best insurance against metastable states.
For higher clock rates, consider adding additional registers.
Quarantine time
reduces p(metastable)
A metastable state here will probably resolve itself to a valid level before it gets into my circuit.
And one here will almost certainly get resolved.