## Slide 1: 1. Basics of Information

## Slide 2: Quantifying Information

## Slide 3: What is “Information”?
Information, noun:
Data communicated or received that resolves recipient’s uncertainty about a particular fact or circumstance.
We’ll be measuring information in circumstances where there are a finite number of possibilities.
Amount of information received depends on the recipient’s context.
Notes: http://commons.wikimedia.org/wiki/File:Poker-sm-222-Kh.png

## Slide 4: Example: Resolving Uncertainty
“The card is a heart.”
“The card is not the Ace of spades.”
“The card is a face card (J, Q, K).”
“The card is the suicide king.”
You receive some data about a card drawn at random from a standard deck of 52 playing cards.
# of possibilities remaining
13
51
12
1
Which of the following data conveys the most information, i.e., eliminates the most uncertainty?
Measure of uncertainty: number of possible cards more possibilities → more uncertainty
  initially: 52 possible cards
Notes: http://commons.wikimedia.org/wiki/File:Poker-sm-222-Kh.png

## Slide 5: Quantifying Information (Claude Shannon, 1948)
Given discrete random variable X
N possible values:
Associated probabilities:
Information received when learning that choice was xi:
x1, x2, …, xN
p1, p2, …, pN
1/pi is proportional to the uncertainty of choice xi.
Information is measured in bits (binary digits) = number of 0/1’s required to encode choice(s)

## Slide 6: Information Conveyed by Data
Common case: Suppose you’re faced with N equally probable choices, and you receive data that narrows it down to M choices. The probability that data would be sent is M∙(1/N) so the amount of information you have received is
Even when data doesn’t resolve all the uncertainty

## Slide 7: Example: Information Content
Examples:
information in one coin flip: N= M= Info content=
card drawn from fresh deck is a heart: N= M= Info content=
roll of 2 dice: N= M= Info content=
2
1
log2(2/1) = 1 bit
52
13
log2(52/13) = 2 bits
36
1
log2(36/1) = 5.17
.17 bits ???

## Slide 8: Probability & Information Content
data | pdata | log2(1/pdata)
a heart |  | 
not the Ace of spades |  | 
a face card (J, Q, K) |  | 
the “suicide king” |  | 
Information content
13/52
2 bits
51/52
0.028 bits
12/52
2.115 bits
1/52
5.7 bits
Shannon’s definition for information content lines up nicely with our intuition: we get more information when the data resolves more uncertainty about the randomly selected card.

## Slide 9: Entropy
In information theory, the entropy H(X) is the average amount of information contained in each piece of data received about the value of X:
Example: X={A, B, C, D}
choicei | pi | log2(1/pi)
“A” | 1/3 | 1.58 bits
“B” | 1/2 | 1 bit
“C” | 1/12 | 3.58 bits
“D” | 1/12 | 3.58 bits
H(X) = (1/3)(1.58) +
(1/2)(1) +
(1/12)(3.58) + (1/12)(3.58)
= 1.626 bits

## Slide 10: Meaning of Entropy
Suppose we have a data sequence describing the values of the random variable X.
bits
H(X)
Average number of bits used to transmit choice
Urk, this isn’t good
This is okay, just inefficient
This is perfect!

## Slide 11: Encoding Information

## Slide 12: Encodings
An encoding is an unambiguous mapping between bit strings and the set of possible data.
Encoding for each symbol |  |  |  | Encoding for “ABBA”
A | B | C | D | 
00 01 10 11 00 01 01 00
01 1 000 001 01 1 1 01
0 1 10 11 0 1 1 0
✗
ABBA?
ABC?
ADA?

## Slide 13: Encodings as Binary Trees
B⟷0
A⟷11
C⟷100
D⟷101
It’s helpful to represent an unambiguos encoding as a binary tree with the symbols to be encoded as the leaves. The labels on the path from the root to the leaf give the encoding for that leaf.
Encoding
Binary tree
01111
B
0
A
1
1
D
1
C
0
0
BAA
Notes: https://openclipart.org/detail/9007/sheep-by-johnny_automatic-9007

## Slide 14: Fixed-length Encodings
If all choices are equally likely (or we have no reason to expect otherwise), then a fixed-length code is often used. Such a code will use at least enough bits to represent the information content.
1
0
1
0
1
0
A
B
C
D
All leaves have the same depth!
Examples:
4-bit binary-coded decimal (BCD) digits
7-bit ASCII for printing characters
Note that the entropy for N equally-probable symbols is
=log2(N)
log2(10)=3.322
log2(94)=6.555
Fixed-length encodings are often a little inefficient…

## Slide 15: Encoding Positive Integers
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
It is straightforward to encode positive integers as a sequence of bits. Each bit is assigned a weight. Ordered from right to left, these weights are increasing powers of 2. The value of an N-bit number encoded in this fashion is given by the following formula:
Smallest number: Largest number:
V = 0*211 + 1*210 + 1*29 + …
= 1024 + 512 + 256 +128 + 64 + 16
= 2000
0
2N-1

## Slide 16: Hexademical Notation
Hexadecimal - base 16
0000 - 0 1000 - 8 0001 - 1 1001 - 9 0010 - 2 1010 - A 0011 - 3 1011 - B 0100 - 4 1100 - C 0101 - 5 1101 - D 0110 - 6 1110 - E 0111 - 7 1111 - F
Long strings of binary digits are tedious and error-prone to transcribe, so we usually use a higher-radix notation, choosing the radix so that it’s simple to recover the original bits string.
A popular choice is to transcribe numbers in base-16, called hexadecimal, where each group of 4 adjacent bits are represented as a single hexadecimal digit.
211
210
29
28
27
26
25
24
23
22
21
20
0
1
1
1
1
1
0
1
0
0
0
0
0
D
7
0b011111010000 = 0x7D0

## Slide 17: Encoding Signed Integers
N bits
“0” for “+”
“1” for “-”
Range: – (2N-1 – 1) to 2N-1 – 1
We use a signed magnitude representation for decimal numbers, encoding the sign of the number (using “+” and “-”) separately from its magnitude (using decimal digits).
We could adopt that approach for binary representations:
But: two representations for 0 (+0, -0) and we’d need different circuitry for addition and subtraction
1 1 1 1 1 1 0 1 0 0 0 0
-2000

## Slide 18: Two’s Complement Encoding
20
21
22
23
…
2N-2
-2N-1
…
…
N bits
“sign bit”
Range: – 2N-1 to 2N-1 – 1
In a two’s complement encoding, the high-order bit of the N-bit representation has negative weight:
Negative numbers have “1” in the high-order bit
Most negative number: 10…0000
Most positive number: 01…1111
If all bits are 1: 11…1111
If all bits are 0: 00…0000
-2N-1
+2N-1 - 1
-1
0

## Slide 19: More Two’s Complement
Let’s see what happens when we add the N-bit values for -1 and 1, keeping an N-bit answer:
11…1111
+00…0001
To compute B-A, we’ll just use addition and compute B+(-A). But how do we figure out the representation for -A?
0000000
A+(-A) = 0 = 1 + -1
-A = (-1 – A) + 1
= ~A + 1
1 1 … 1 1
- An-1 An-2 … A1 A0
~An-1 ~An-1 … ~A1 ~A0
~A
To negate a two’s complement value: bitwise complement and add 1.
Just use ordinary binary addition, even when one or both of the operands are negative. 2’s complement is perfect for N-bit arithmetic!

## Slide 20: Variable-length Encodings

## Slide 21: Variable-length Encodings
We’d like our encodings to use bits efficiently:
GOAL: When encoding data we’d like to match the length of the encoding to the information content of the data.
On a practical level this means:
  Higher probability → __________ encodings
  Lower probability → __________ encodings
Such encodings are termed variable-length encodings.
shorter
longer

## Slide 22: Example
choicei | pi | encoding
“A” | 1/3 | 11
“B” | 1/2 | 0
“C” | 1/12 | 100
“D” | 1/12 | 101
B
C
D
A
1
0
1
0
1
0
010011011101
Expected length of this encoding:
Expected length for 1000 symbols:
  With fixed-length, 2 bits/symbol = ________ bits
  With variable-length code = ________ bits
  Lower bound (entropy) = ________ bits
Entropy: H(X) = 1.626 bits
High probability,
Less information
Low probability,
More information
B→0
A→11
C→100
D→101
B C A B A D
2000
1667
(2)(1/3) + (1)(1/2) + (3)(1/12)(2) = 1.667 bits
1626

## Slide 23: Huffman’s Algorithm
Given a set of symbols and their probabilities, constructs an optimal variable-length encoding.
Huffman’s Algorithm:
Build subtree using 2 symbols with lowest pi
At each step choose two symbols/subtrees with lowest pi, combine to form new subtree
Result: optimal tree built from the bottom-up
Example:
A=1/3, B=1/2, C=1/12, D=1/12
C
D
1/12
1/12
1
0
1/6
A
1
0
1/3
1/2
B
1
0
1/2

## Slide 24: Can We Do Better?
Huffman’s Algorithm constructed an optimal encoding… does that mean we can’t do better?
To get a more efficient encoding (closer to information content) we need to encode sequences of choices, not just each choice individually. This is the approach taken by most file compression algorithms…
AA=1/9, AB=1/6, AC=1/36, AD=1/36
BA=1/6, BB=1/4, BC=1/24, BD=1/24
CA=1/36, CB=1/24, CC=1/144, CD=1/144
DA=1/36, DB=1/24, DC=1/144, DD=1/144
Using Huffman’s Algorithm on pairs:
Average bits/symbol = 1.646 bits
Lookup “LZW”
on Wikipedia

## Slide 25: Error Detection and Correction

## Slide 26: Error Detection and Correction
Suppose we wanted to reliably transmit the result of a single coin flip:
“tails”
Heads: “0”
Tails: “1”
1
Further suppose that during processing a single-bit error occurs, i.e., a single “0” is turned into a “1” or a “1” is turned into a “0”.
0
“heads”
Notes: https://openclipart.org/detail/181695/man-on-telephone-by-liftarn-181695
https://openclipart.org/detail/181694/woman-on-telephone-by-liftarn-181694
https://openclipart.org/image/300px/svg_to_png/168991/hand-ok.png
https://openclipart.org/image/300px/svg_to_png/132733/coste.png

## Slide 27: Hamming Distance
HAMMING DISTANCE: The number of positions in which the corresponding digits differ in two encodings of the same length.
0110010
0100110
Differs in 2 positions so Hamming distance is 2…

## Slide 28: Hamming Distance & Bit Errors
The Hamming distance between a valid binary code word and the same code word with a single-bit error is 1.
1
0
“heads”
“tails”
single-bit error
The problem with our simple encoding is that the two valid code words (“0” and “1”) also have a Hamming distance of 1. So a single-bit error changes a valid code word into another valid code word…

## Slide 29: Single-bit Error Detection
What we need is an encoding where a single-bit error does not produce another valid code word.
“heads”
“tails”
10
01
single-bit error
A parity bit can be added to any length message and is chosen to make the total number of “1” bits even (aka “even parity”). If min HD(code words) = 1, then min HD(code words + parity) = 2.
0
1
0
1

## Slide 30: Parity check = Detect Single-bit errors
To check for a single-bit error (actually any odd number of errors), count the number of 1s in the received message and if it’s odd, there’s been an error. 0 1 1 0 0 1 0 1 0 0 1 1  original word with parity 0 1 1 0 0 0 0 1 0 0 1 1  single-bit error (detected) 0 1 1 0 0 0 1 1 0 0 1 1  2-bit error (not detected)
One can “count” by summing the bits in the word modulo 2 (which is equivalent to XOR’ing the bits together).

## Slide 31: Detecting Multi-bit Errors
111
000
“heads”
“tails”
To detect E errors, we need a minimum Hamming distance of E+1 between code words.
001
100
010
011
101
110
With this encoding, we can detect up to two bit errors. Note that HD(000,111) = 3…

## Slide 32: Single-bit Error Correction
By increasing the Hamming distance between valid code words to 3, we guarantee that the sets of words produced by single-bit errors don’t overlap. So assuming at most one error, we can perform error correction since we can tell what the valid code was before the error happened.
In general, to correct E errors, we need a minimum Hamming distance of 2E+1 between code words.
111
000
001
100
010
011
101
110
“heads”
“tails”
“heads”
“tails”
With this encoding: use majority voting to determine heads or tails

## Slide 33: (n,k,d) Systematic Block Codes
Split message into k-bit blocks
Add p parity bits to each block, making each block n bits long.
Often, we’ll use the notation (n,k,d) where d is the minimum Hamming distance between code words.
The ratio k/n is called the code rate and is a measure of the code’s overhead (always ≤ 1, larger is better).
Message bits
Parity bits
k
n=k+p
The entire block is called a “code word” and this is an (n,k) code.
p

## Slide 34: Hamming Single-Error-Correcting Codes
Basic idea:
  Use multiple parity bits, each covering a subset of the data bits.
  No two message bits belong to exactly the same subsets, so a single error will generate a unique set of parity check errors.
B1
B0
B3
B2
P0
P1
P2
Suppose we check the parity and discover that P1 and P2 indicate an error?
bit B2 must have flipped
What if only P2 indicates an error?
P2 itself had the error!
This is a (7,4,3) code! Note that n+1 = 2p
P0 = B0B1B3
P1 = B0B2B3
P2 = B1B2B3
Modulo-2 addition, aka XOR

## Slide 35: Checking the parity
Transmit: Compute the parity bits and send them along with the message bits
Receive: After receiving the (possibly corrupted) message, compute a syndrome bit (Ei) for each parity bit. For the code on previous slide:
If all the Ei are zero: no errors!
If Ei=1, then there was a parity error involving Pi. The particular combination of the Ei can be used to figure out which bit to correct.
E0 = B0  B1  B3  P0
E1 = B0  B2  B3  P1
E2 = B1  B2  B3  P2

## Slide 36: Using the Syndrome to Correct Errors
Continuing example from previous slide: there are three syndrome bits, giving us a total of 8 encodings.
E2E1E0 | Single Error Correction
0 0 0 | No errors
0 0 1 | P0 has an error, flip to correct
0 1 0 | P1 has an error, flip to correct
0 1 1 | B0 has an error, flip to correct
1 0 0 | P2 has an error, flip to correct
1 0 1 | B1 has an error, flip to correct
1 1 0 | B2 has an error, flip to correct
1 1 1 | B3 has an error, flip to correct
The 8 encodings indicate the 8 possible correction actions: no errors, error in one of 4 data bits, error in one of 3 parity bits. In general. we need (n+1) ≤ 2p for single-bit error correction.
What happens if there is more than one error?

## Slide 37: Summary: Basics of Information
Information resolves uncertainty
Choices equally probable:
  N choices down to M⇒ log2(N/M) bits of information
  use fixed-length encodings
  encoding numbers: 2’s complement signed integers
Choices not equally probable:
  choicei with probability pi ⇒ log2(1/pi) bits of information
  average amount of information = H(X) = ∑pilog2(1/pi)
  use variable-length encodings, Huffman’s algorithm
To detect E-bit errors: Hamming distance > E
To correct E-bit errors: Hamming distance > 2E
Next time:
  encoding information electrically
  the digital abstraction
  combinational devices

## Slide 38: Next Time: Encoding Information Using Voltages
I’ll have to remember to wear
insulating shoes