## Slide 1: SVCs, Devices, and Interrupts
Interrupts for Async I/O
ReadKey SVC example
“Real Time”
  Latencies & Deadlines
Weak priorities
Strong priorities
Loop:
LD(R3,0,R0)
ADDC(R3,4,R3)
SUBC(R2,1,R2)
BNE(R2,Loop)
…
(Cough) Excuse me, sir…

## Slide 2: OS Organization: I/O Devices
Timer Handler
KERNEL
MState
DPYNUM=0
P1:
P1
loop:SVC(0)
    ...
    SVC(1)
    ...
    BR(loop)
P2
loop:SVC(2)
    ...
    SVC(3)
    ...
    BR(loop)
PN
loop:SVC(3)
    ...
    SVC(1)
    ...
    BR(loop)
User
Mode
PC[31]=0
Kernel
Mode
PC[31]=1
USER PROCESSES
Scheduler
MState
DPYNUM=1
P2:
MState
DPYNUM=27
PN:
…
…
Keyboard Handler
Key
Buffer
Mouse Handler
Click
Buffer
Saved
Regs
(MState)
Illegal Op Handler
Yield
WrCh
GetKey
…

## Slide 3: Asynchronous I/O Handling
SVC call from application
Application:
  …
  ReadKey() // read key into R0
  …
. . .
“A”
Device Buffer
(in OS Kernel)
KeyHit_h() { (read ASCII code, put in buffer)
}
INTERRUPT from Keyboard n
INTERRUPT to OS
IN
OUT
ReadKey_h() { (remove next char from buffer, return in R0)
…}
TRAP to OS
IN
OUT

## Slide 4: Interrupt-based Asynch I/O
OPERATION: NO attention to Keyboard during normal operation
  • on key strike: hardware asserts IRQ to request interrupt
  • USER program interrupted, PC+4 of interrupted inst. saved in XP
  • state of USER program saved on KERNEL stack;
  • Keyboard handler invoked, runs to completion;
  • state of USER program restored; program resumes.
TRANSPARENT to USER program.
Keyboard Interrupt Handler (in O.S. KERNEL):
struct Device {
char Flag, Data;
} Keyboard;
KeyHit_h() {
Buffer[inptr] = Keyboard.Data;
inptr = (inptr + 1) % BUFSIZE;
}
Assume each keyboard has an associated buffer

## Slide 5: ReadKey SVC: Attempt #1
SVC recap: SVC, encoded as illegal instruction, causes an exception. OS notices special SVC opcode, dispatches to appropriate sub-handler based on index in low-bits of SVC inst.
First draft of a ReadKey SVC handler (supporting a virtual keyboard): returns next keystroke on a user’s keyboard in response to the SVC request:
Problem: Can’t interrupt code running in the supervisor mode… so the buffer never gets filled.
ReadKey_h()
{
int kbdnum = ProcTbl[Cur].DPYNum;
  while (BufferEmpty(kbdnum)) {
  /* busy wait loop */
  }
  UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
ReadKey_h()
{
int kbdnum = ProcTbl[Cur].DPYNum;
  while (BufferEmpty(kbdnum)) {
  /* busy wait loop */
  }
  UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
Notes: https://openclipart.org/detail/192993/silhouette-of-female-typing-on-a-computer

## Slide 6: ReadKey SVC: Attempt #2
A BETTER keyboard SVC handler:
ReadKey_h()
{
int kbdnum = ProcTbl[Cur].DPYNum;
  if (BufferEmpty(kbdnum)) {
  /* busy wait loop */
  UserMState.Regs[XP] = UserMState.Regs[XP]-4;
  } else
  UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
Problem: The process just wastes its time-slice waiting for someone to hit a key...
This one actually works!
That’s a funny way to write a loop

## Slide 7: ReadKey SVC: Attempt #3
EVEN BETTER: On I/O wait, YIELD remainder of quantum:
ReadKey_h()
{
int kbdnum = ProcTbl[Cur].DPYNum;
  if (BufferEmpty(kbdnum)) {
  UserMState.Regs[XP] = UserMState.Regs[XP]-4;
  Scheduler( );
  } else
  UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
RESULT: Better CPU utilization!!
Does timesharing cause CPU use to be less efficient?
  COST: Scheduling, context-switching overhead; but
  GAIN: Productive use of idle time of one process by running another.

## Slide 8: Sophisticated Scheduling
To improve efficiency further, we can avoid scheduling processes in prolonged I/O wait:
  Processes can be in ACTIVE or WAITING (“sleeping”) states;
  Scheduler cycles among ACTIVE PROCESSES only;
  Active process moves to WAITING status when it tries to read a character and buffer is empty;
  Waiting processes each contain a code (eg, in PCB) designating what they are waiting for (eg, keyboard N);
  Device interrupts (eg, on keyboard N) move any processes waiting on that device to ACTIVE state.
UNIX kernel utilities:
  sleep(reason) - Puts CurProc to sleep. “Reason” is an arbitrary binary value giving a condition for reactivation.
  wakeup(reason) - Makes active any process in sleep(reason).

## Slide 9: ReadKey SVC: Attempt #4
ReadKey_h() { … if (BufferEmpty(kbdnum)) { User.Regs[XP] = User.Regs[XP] - 4; sleep(kbdnum); } else { … } }
sleep(status s) { ProcTbl[Cur].status = s; Scheduler(); }
Scheduler() {
…
while (ProcTbl[i].status != 0) { i = (i+1)%N; }
…
}
wakeup(status s) {
for (i = 0; i < N; i += 1) {
if (ProcTbl[i].status == s)
ProcTbl[i].status = 0;
}
}
SVC call from application
KeyHit_h() { … WriteBuffer(kbdnum, key); wakeup(kbdnum); … }
INTERRUPT from Keyboard n

## Slide 10: Example: Match Handler to OS
Model A: A timeshared Beta system whose OS kernel is uninterruptable
Model B: A timeshared Beta system which enables device interrupts during handing of SVC traps
Model C: A single-process (not timeshared) system which runs dedicated application code
R1
R2
R3
ReadCh_h() { // Version R1
if (BufferEmpty(0))
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
else
UserMState.Regs[0] = ReadInputBuffer(0);
}
ReadCh_h() { // Version R2
int kbdnum = ProcTbl[Cur].DPYNum;
while (BufferEmpty(kbdnum));
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
ReadCh_h() { // Version R3
int kbdnum = ProcTbl[Cur].DPYNum;
if (BufferEmpty(kbdnum)) {
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
Scheduler();
} else
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
Always reads from the same buffer
C
Oops!
Infinite loop?
B
A
Notes: Model A: R3
Model B: R2
Model C: R1

## Slide 11
Model A: A timeshared Beta system whose OS kernel is uninterruptable
Model B: A timeshared Beta system which enables device interrupts during handing of SVC traps
Model C: A single-process (not timeshared) system which runs dedicated application code
Which handler & OS?
“I get compile-time errors; Scheduler and ProcTbl are undefined!”
R1
R2
R3
ReadCh_h() { // Version R1
if (BufferEmpty(0))
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
else
UserMState.Regs[0] = ReadInputBuffer(0);
}
ReadCh_h() { // Version R2
int kbdnum = ProcTbl[Cur].DPYNum;
while (BufferEmpty(kbdnum));
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
ReadCh_h() { // Version R3
int kbdnum = ProcTbl[Cur].DPYNum;
if (BufferEmpty(kbdnum)) {
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
Scheduler();
} else
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
 | A | B | C
R1 |  |  | X
R2 |  | X | 
R3 | X |  | 
X
X
X
X
X
Notes: User has handler R3 on system C. R3 is the only handler that calls Scheduler() and C is not timeshared it’s the only OS that would have a scheduler.

## Slide 12
Model A: A timeshared Beta system whose OS kernel is uninterruptable
Model B: A timeshared Beta system which enables device interrupts during handing of SVC traps
Model C: A single-process (not timeshared) system which runs dedicated application code
Which handler & OS?
“Hey, now the system always reads everybody’s input from keyboard 0.
In addition, it seems to waste a lot more CPU cycles than it used to.”
R1
R2
R3
ReadCh_h() { // Version R1
if (BufferEmpty(0))
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
else
UserMState.Regs[0] = ReadInputBuffer(0);
}
ReadCh_h() { // Version R2
int kbdnum = ProcTbl[Cur].DPYNum;
while (BufferEmpty(kbdnum));
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
ReadCh_h() { // Version R3
int kbdnum = ProcTbl[Cur].DPYNum;
if (BufferEmpty(kbdnum)) {
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
Scheduler();
} else
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
 | A | B | C
R1 |  |  | X
R2 |  | X | 
R3 | X |  | 
X
X
X
X
X
Notes: User has handler R1 on system A. R1 is the only handler that assumes keyboard 0. The model A user was using a handler (R3) which called scheduler when the buffer R1 A was empty which in theory wastes fewer CPU cycles than busy looping. So when the user substitutes R1, the program busy loops when the buffer is empty. The model B user wouldn't have the same complaint since the handler she was using (R2) already loops.

## Slide 13
Model A: A timeshared Beta system whose OS kernel is uninterruptable
Model B: A timeshared Beta system which enables device interrupts during handing of SVC traps
Model C: A single-process (not timeshared) system which runs dedicated application code
Which handler & OS?
“Neat, the new system seems to work fine.
It even wastes less CPU time than it used to!”
R1
R2
R3
ReadCh_h() { // Version R1
if (BufferEmpty(0))
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
else
UserMState.Regs[0] = ReadInputBuffer(0);
}
ReadCh_h() { // Version R2
int kbdnum = ProcTbl[Cur].DPYNum;
while (BufferEmpty(kbdnum));
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
ReadCh_h() { // Version R3
int kbdnum = ProcTbl[Cur].DPYNum;
if (BufferEmpty(kbdnum)) {
UserMState.Regs[XP] = UserMState.Regs[XP] – 4;
Scheduler();
} else
UserMState.Regs[0] = ReadInputBuffer(kbdnum);
}
 | A | B | C
R1 |  |  | X
R2 |  | X | 
R3 | X |  | 
X
X
X
X
X
Notes: User has handler R3 on system B. The model B, who used to use R2, is happy because we’ve replaced the kernel busy loop in the old handler with a call to scheduler.

## Slide 14: The Need for “Real Time”
Side-effects of CPU virtualization + abstraction of machine resources (memory, I/O, registers, etc. ) + multiple “processes” executing concurrently + better CPU utilization - Processing throughput is more variable
Our approach to dealing with the asynchronous world - I/O - separate “event handling” from “event processing”
Difficult to meet “hard deadlines” - control applications, e.g., ESC on cars - playing videos/MP3s
Real-time as an alternative to time-sliced or fixed-priority preemptive scheduling
Notes: https://openclipart.org/detail/234997/push-back-time

## Slide 15: Interrupt Latency
One way to measure the real-time performance of a system is INTERRUPT LATENCY:
  HOW MUCH TIME can elapse between an interrupt request and the START of its handler?
time
Request
Sometimes bad things happen when service is delayed beyond its “dead”-line:
  Missed characters
  Automobile crashes
  Nuclear meltdowns
“HARD”
Real time
constraints
Latency (L)
Service
Time (S)
Deadline (D)
What is largest L such that LMAX + S = D?
Notes: https://openclipart.org/detail/190427/death-and-the-hour-glass

## Slide 16: Sources of Interrupt Latency
What causes interrupt latency:
  State save, context switch.
  Periods of un-interruptability:
    Long, uninterruptable instructions – e.g. block moves
    Explicitly disabled periods (e.g. .during service of other interrupts).
time
Request
Latency
Service
Time
Deadline?
GOAL: BOUND (and minimize) interrupt latency!
  Optimize interrupt sequence context switch
  Make unbounded-time instructions interruptable (state in registers, etc).
  Avoid/minimize disable time
  Allow handlers to be interrupted, in certain cases.
But, this is application dependent!
We can consider this when we write our O/S
We can address this in our ISA

## Slide 17: Scheduling of Multiple Devices
DEVICE
Keyboard
Disk
Printer
Service
Time
800
500
400
Actual w/c
Latency
________
________
________
"TOY" System scenario:
What is the WORST CASE latency seen by each device?
Req: K,P,D
P
K
D
Req: D,P,K
D
P
K
Req: K,D,P
K
D
P
Assumptions:
  Infrequent interrupt requests (each happens only once/scenario)
  Simultaneous requests might be served in ANY order…. Whence
  Service of EACH device might be delayed by ALL others!
500 + 400 = 900
800 + 400 = 1200
800+ 500 = 1300
Can we do better?

## Slide 18: Weak (Non-preemptive) Priorities
ISSUE: Processor becomes interruptable on returning to user mode, several interrupt requests are pending. Which is served first?
Latencies with WEAK PRIORITIES:
Service of each device might be delayed by:
  Service of 1 other (arbitrary) device, whose interrupt request was just honored; +
  Service of ALL higher-priority devices.
D
P
K
Req:
P,K,D
Req:
K,P,D
K
P
D
DEVICE
Keyboard
Disk
Printer
Service
Time
800
500
400
Actual w/c
Latency
________
________
________
900
800
1300
WEAK PRIORITY ORDERING: Check in prescribed sequence, e.g.:
DISK > PRINTER > KEYBOARD.
vs 1200 –
Now delayed by only 1 service!

## Slide 19: Setting Priorities
How should priorities be assigned given hard real-time constraints? We’ll assume each device has a service deadline D.
  If not otherwise specified, assume D is the time until the next request for the same device, e.g., the keyboard handler should be finished processing one character before the next arrives.
“Earliest Deadline” is a strategy for assigning priorities that is guaranteed to meet the deadlines if any priority assignment can meet the deadlines:
  Sort the requests by their deadlines
  Assign the highest priority to the earliest deadline, second priority to the next deadline, and so on.
  Weak priority scheduling: choose the pending request with the highest priority, i.e., that has the earliest deadline.

## Slide 20: The Need for Preemption
Without preemption, ANY interrupt service can delay ANY other service request… the slowest service time constrains response to fastest devices. Often, tight deadlines can’t be met using this scheme alone.
EXAMPLE: 800 uSec deadline (hence 300 uSec maximum interrupt latency) on disk service, to avoid missing next sector...
need PREEMPTION: Allow handlers for LOWER PRIORITY interrupts to be interrupted by HIGHER priority requests!
~0
[D] 500
[D,P] 900
CAN'T SATISFY the disk requirement in this system using weak priorities!
Latency using weak priority | Device | Service Time (S) | Deadline (D) | LMAX
900us | Keyboard | 800us |  | 
800us | Disk | 500us | 800us | 300us
1300us | Printer | 400us |  | 
Latency w/ preemption
Priority
1
3
2

## Slide 21: Strong Priority Implementation
SCHEME:
  Expand supervisor bit in PC to be a PRIORITY integer PRI (eg, 3 bits for 8 levels)
  ASSIGN a priority to each device.
  Prior to each instruction execution:
    Find priority PDEV of highest requesting device, say Di
    Take interrupt if and only if PDEV > PRI, set PRI = PDEV.
Strong priorities:
KEY: Priority in Processor state
Allows interruption of (certain) handlers
Allows preemption, but not reentrance
BENEFIT: Latency seen at high priorities UNAFFECTED by service times at low priorities.
PC:
Program Counter
PRI
STRONG PRIORITY ORDERING: Allow handlers for LOWER PRIORITY interrupts to be preempted (interrupted) by HIGHER PRIORITY requests.

## Slide 22: Recurring Interrupts
Consider interrupts which recur at bounded rates:
Note that interrupt LATENCIES don't tell the whole story—consider COMPLETION TIMES, e.g., for Keyboard in the example above.
Keyboard service not complete until 3 ms after request!
D
P
K
P
P
D
P
P
D
D
P
K
D
P
D
P
P
Priority | Latency using strong priority | Device | Service Time (S) | Deadline (D) | LMAX | Max Freq.
1 | 900us | Keyboard | 800us |  |  | 100/s
3 | 0 | Disk | 500us | 800us | 300us | 500/s
2 | 500us | Printer | 400us |  |  | 1000/s

## Slide 23: Interrupt Load
P | Latency | Device | Service Time (S) | Deadline (D) | LMAX | Max Freq. | % Load
1 | 900us | Keyboard | 800us |  |  | 100/s | 
3 | 0 | Disk | 500us | 800us | 300us | 500/s | 
2 | 500us | Printer | 400us |  |  | 1000/s | 
How much CPU time is consumed by interrupt service?
D
P
K
P
P
D
P
P
D
P
P
D
D
P
K
P
P
D
P
10 ms. cycle
800us*100/s = 8%
500us*500/s = 25%
400us*1000/s = 40%
User-mode share of CPU = 1 – ∑(SDEV*max_freqDEV) = 0.27
Also check to see if enough CPU time to meet all deadlines

## Slide 24: Example: Mr. Blue Visits the ISS
≤ 10 mS
Task Period Service time Deadline
Supply ship guidance 30ms 5ms 25ms
Gyroscopes 40 10 20
Cabin pressure 100 ? 100
International Space Station’s on-board computer performs 3 tasks:
  guiding incoming supply ships to a safe docking
  monitoring gyros to keep solar panels properly oriented
  controlling air pressure in the crew cabin
Assuming a weak priority system:
What is the maximum service time for “cabin pressure” that still allows all constraints to be met?
Give a weak priority ordering that meets the constraints
What fraction of the time will the processor spend idle?
What is the worst-case completion time for each task?
16.67%
25%
10%
G > SSG > CP
48.33%
C,G = 10 + 10 + (5) = 25
C = 10 + (10) = 20
S,G = 5 + 10 + (10) = 25
10
Notes: https://openclipart.org/detail/176068/international-space-station
https://openclipart.org/detail/38137/kid-shaking
Since G can be delayed by a max of 10ms, no other device can take more than 10ms for service in a weak priority system – hence C must take <= 10ms.
If C service takes 10, then G must be highest since it can be delayed by at most 10. S must be next, with a max latency of 20; then C.
16.6% S + 25% G + 10% C = 51.66%, leaving 48.33% for app.
Since we’re asked for delay to COMPLETION of service, we must include service times of each device in its own delay:
S delayed by C, G = 10 + 10 (+ 5 svc time) = 25
G delayed by C = 10 (+ 10 svc time) = 20
C delayed by S, G = 5 + 10 (+ 10 svc time) = 25

## Slide 25: Example: Mr. Blue Visits ISS (cont’d.)
Our Russian collaborators don’t like the sound of a “weak” priority interrupt system and lobby heavily to use a “strong” priority interrupt system instead.
Task Period Service time Deadline
Supply ship guidance 30ms 5ms 25ms
Gyroscopes 40 10 20
Cabin pressure 100 ? 100
Assuming a strong priority system, G > SSG > CP:
What is the maximum service time for “cabin pressure” that still allows all constraints to be met?
What fraction of the time will the processor spend idle?
What is the worst-case completion time for each task?
100 – (3*10) – (4*5) = 50
50
16.67%
25%
50%
8.33%
100
10
[G] 10 + 5
Notes: Assume C is assigned the lowest (strong) priority.
If we maximize the svc time of C, its service might be interrupted by several requests from higher priority devices (G and S)…
In its 100ms window, 4 S requests and 3 G requests can happen (and will be given priority over C service. Thus, in this window, there is then
100 – 3*20 – 4*5 = 50ms
left for C service.

## Slide 26: Summary
Device interface – two parts:
  Device side: handle interrupts from device (transparent to apps)
  Application side: handle interrupts (SVCs) from application
Scheduler interaction:
  “Sleeping” (*inactive) processes waiting for device I/O
  Handler coding issues, looping thru User mode
Real Time constraints, scheduling, guarantees
  Complex, hard scheduling problems – a black art!
  Weak (non-preemptive) vs Strong (preemptive) priorities help…
  Common real-world interrupt systems:
    Fixed number (eg, 8 or 16) of strong priority levels
    Each strong priority level can support many devices, arranged in a weak priority chain