## Slide 1: 20. System-level Communication
6.004x Computation Structures
Part 3 – Computer Organization
Copyright © 2016 MIT EECS

## Slide 2: Computer System Technologies
Motherboards
SDRAM
LAN technology
Linux
Windows
10
Hard Disk
Drives
DRAM
Flash Memory
Graphics
Acceleration
ActiveX
Controls
App
Servers
What is the most important part of this picture?

## Slide 3: Technology comes & goes; interfaces last forever
Interfaces typically deserve more engineering attention than the technologies they interface…
  Abstraction: should outlast many technology generations
  Often “virtualized” to extend beyond original function (e.g. memory, I/O, services, machines)
  Represent more potential value to their proprietors than the technologies they connect.
Interface sob stories:
  Interface “warts”: Big/little Endian wars
  Early IBM PC reliance on the exact signaling of 8086 chips
... and many success stories:
  IBM 360 Instruction set architecture; Postscript; Compact Flash; ...
  TCP/IP-based packet networks

## Slide 4: System Interfaces & Modularity
CPU
MEM
I/O
DISK
I/O
MEM
Ancient Times (Ad hoc connections)
Late 60s (Processor-dependent Bus)
CPU
MEM
I/O
DISK
I/O
MEM
(Mostly) Point-to-point
80s (Processor-independent Bus)
CPU
CPU
I/O
DISK
I/O
MEM
90s (buses galore)
MEM
MEM
CPU L2/L3 $
DISK
I/O
I/O
Graphics I/O
PCIe lanes
Bridge

## Slide 5: Buses, Interconnect, So…?
Aren’t communication channels simply logic circuits with long wires?
Wires − interconnect engineer’s view:
  Transmission lines.
  Finite signal propagation velocity.
  Distance matters.
  Time matters.
  Reality matters.
Wires − circuit theorist’s view:
  Equipotential “nodes” of a circuit.
  Instant propagation of v, i over entire node.
  “distance” abstracted out of design model.
  Time issues dictated by RLC elements; wires are timeless.

## Slide 6: Electrical Model for Real Wires
http://cva.stanford.edu/books/dig_sys_engr/lectures/
Omegatron (CC BY-SA 3.0)
signal
Reference (e.g., ground)
 | Description | On chip | On PCB
R | Resistance of conductor | 150kΩ/m | 5Ω/m
L | Self-inductance of conductor (due to magnetic field induced by current) | 600nH/m | 300nH/m
C | Capacitance between signal and ground | 200pF/m | 100pF/m
G | Conductance between signal and ground (through insulator) | small | small
≡
(At high frequency)
Transmission Line
( propagation = m/s)
Z0
Notes: https://en.wikipedia.org/wiki/Transmission_li
http://cva.stanford.edu/books/dig_sys_engr/lectures/l2.pdfne#/media/File:Transmission_line_element.svg

## Slide 7: Real-World Consequences
• transmission line discontinuities (reflections off of impedance mismatches and terminations)
[Dally]Fig. 6-17
• charge storage in RC circuit
(narrow pulses are lost due to incomplete transitions)
[Dally]Fig. 6-19
[Dally]Fig. 6-20
• RLC ringing (triggered by voltage steps)
Fix: slower operation, limiting
voltage swings and slew rates
∆V from energy storage left over from earlier signaling on the wire:
Dally, W.J., Poulton, J. W., Digital Systems Engineering, 1998

## Slide 8: Space & Time Constraints
Space
Time
Communication
Storage
Fundamental Physical Constraints:
  Bounds on propagation speeds
    Signals travel ~18cm/ns on PCB
  Bounds on device density
    Must be finite distances between components
  Bounds on flow of charge
    finite currents → finite rise/fall times
    wire delays depend on loading
Moving information in space/time

## Slide 9: Gates, Wires, & Delays
Our tpd, tcd timing model
  bundles delays into device specs
  ignores loading, wire lengths
Reality check:
  long / heavily-loaded outputs will be slower
  can bundle internal wire delays into tpd of a device; but external load matters!
  partial fixes: buffers, distribution trees
  optimizing performance requires attention to loading issues (You’ll see this in the design project!).
32
A
B
Particularly problematic: system-wide interconnect!

## Slide 10: Interface Standard: Backplane Bus
Modular cards that plug into a common backplane:
CPUs
Memories
Bulk storage
I/O devices
S/W?
The backplane provides:
Power
Common system clock
Wires for communication
Notes: MOST COMMON communication technology WITHIN a computer... BACKPLANE BUS.
Single-Bus Organization pioneered by DEC in mid 60s... multiple buses common too.
MODULES, ADDRESS ASSIGNMENTS, PROTOCOLS...
All modules SHARE bussed lines.
*** SHOW EXAMPLES ***
START/FINISH: Locally Timed (Self Timed) protocols.
GENERALIZATION of memory read/write protocols.

## Slide 11: A Parallel Bus Transaction
CLK
assertion edge
sample edge
start
finish
operation
address
data
WRITE (Originator)
(Originator)
(Originator)
(Originator)
(Recipient)
ORIGINATOR:
1) Chooses bus operation
2) Asserts an address
3) Waits for a recipient to answer.
RECIPIENT:
1) Monitors start
2) Check address
3) If meant for me
a) look at bus operation
b) do operation
c) signal finish of cycle
BUS:
1) Monitors start 2) Start count down
3) If no one answers before
counter reaches 0 then
“time out”

## Slide 12: Bus Lines as Transmission Lines
?
?
?
?
ANALOG ISSUES:
  Propagation times
    Signals travel at ~18 cm/ns on a PCB
  Skew
    Different points along the bus see the signals at different times
    Bits of data propagate at slightly different rates along parallel wires
  Reflections & standing waves
    At each interface (places where the propagation medium changes) the signal may reflect if the impedances are not matched.
    Make a transition on a long line – may have to wait many transition times for echoes to subside.
https://en.wikipedia.org/wiki/Reflections_of_signals_on_conducting_lines
Spinningspark (CC BY-SA 3.0)
Transmission:
Reflection:
Notes: https://en.wikipedia.org/wiki/Reflections_of_signals_on_conducting_lines#/media/File:Discontinuity_on_transmission_line.svg

## Slide 13: Meanwhile, Outside the Box…
Application
Session
TCP
UDP
IP
Ethernet
Physical
Network
Transport
Token Ring
IDEA: Protocol “layers” that isolate application-level interface from low-level physical devices:
ETHERNET: In the mid-70’s Bob Metcalf (at Xerox PARC, an MIT alum) devised a bus for networking computers together.
  Inspired by Aloha net (radio)
  COAX replaced “ether”
  Bit-serial (optimized for long wires)
  Variable-length “packets”:
  - self-clocked data (no clock, skew!)
  - header (dest), data bits, checksum
  Issues: sharing, contention, arbitration, “backoff”
The network as an interface standard.

## Slide 14: Lessons learned: single driver, point-to-point
Issues:
Impedance troubles when driving in middle
Turn-around time when sharing a wire (wired-or glitch)
SLOW
Z0
Z0
BEST
Differential signaling over controlled impedance trace
Z0
Match impedance of driver to impedance of trace
OKAY
Single-ended signaling over controlled impedance trace
Z0
Match impedance of driver to impedance of trace

## Slide 15: Lessons learned: clock recovery
Receiver can infer presence of clock edge every time there’s a transition in the received samples.
Using sample period, extrapolate remaining edges
    -- Now know first and last sample for each bit -- Choose “middle” sample to determine message bit
  Can’t go too long without a clock edge → 8b10b encoding
(Sample period)(# samples/bit)
Receive samples
Inferred clock edges
Extrapolated clock edges

## Slide 16: Serial, Point-to-Point Communications
ETHERNET: Broadcast technology
  Sharing (contention) issues
  Multiple-drop-point issues…
  bit-serial (single wire!)
  “Packets” for multi-bit data
Evolution: Point-to-point
  10BaseT, separate R & T wires
  Each link connects only 2 hosts, one sends, the other receives
  Network riddled with switches, routers
Serial point-to-point bus replacements
  Multi Gbit/sec serial links!
  PCIe, Infiniband, SATA, USB, ...
  Packets, headers
  Switches, routing
  Trend: localized, superfast, serial networks!

## Slide 17: Improving on the bus: lessons learned from the network world
Bus issues:
  shared medium → arbitrate between requesters
  clock skew → parallel bit lines, variable timings
  multiple originators → turnaround time
  impedance discontinuities, stubs → reflections
O
R
REPLACEMENT: fast unidirectional serial point-to-point link
  one transmitter, one receiver → no arbitration, no turnaround
  serial packets replace parallel wire bundles
  clock recovered from data bits → no skew problems
  unidirectional, point-to-point → good signal quality
  need more throughput? → use multiple serial links in parallel…
  need many-to-many communication? → switches (like Ethernet)
  complex interface → Moore’s law to the rescue!
O
R
1x
O
R
4x

## Slide 18: Communications in Today’s Computers
One bus to rule them all,
One bus to join them,
One bus to bring them all
And to the CPU bind them.
QuickPath Interconnect:
→ 20 data + clk
← 20 data + clk
Differential signaling
6.4 GT/s
Notes: https://en.wikipedia.org/wiki/Intel_X58#/media/File:X58_Block_Diagram.png

## Slide 19: Example serial link: PCI Express (PCIe)
I = ±3.5mA
RT = 100Ω
V = ±350mV
LVDS
SIGNALING
Differential
Transmitter
Differential
Receiver
8b/10b
Encoded
Data
@ 5Gb/s
8b/10b
Encoded
Data
PCIe x1: one differential pair in each direction, also x2, x4, x8, …, x32
Data is organized into packets:
Physical Layer (v2.0)
“START”
DLL payload
“END”
Transaction Layer
16- or 20-byte
HEADER
0 to 4096 data bytes
2-byte
SEQNUM
TL payload
4-byte
LCRC
Data Link Layer
TRAIN

## Slide 20: Communication Topologies asymptotic cost/performance tradeoffs
RING
Each component has link to next component on ring
BUS
Shared communication channel allows only one message at a time
1-dimensional approaches:
Goal: enable communications between n components
  Each point-to-point link requires one hardware unit.
  Each point-to-point communication requires one time unit.
  Each link operates independently
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Notes: How to connect things? Gross block diagrams (topologies). Examine
  LATENCY for n nodes;
  THRUPUT for n nodes;
  COST for n nodes.
Connect everything to everything: engineering overkill.
  n(n-1) links - each requires a wire plus 2 interfaces.
  O(n**2) cost;
  O(n) latency (assuming constant size links);
  O(n) msgs/sec thruput.
Be more systematic: 2D Crossbar
  ... still quadratic cost.

## Slide 21: Quadratic-cost Topologies
COMPLETE GRAPH
Dedicated lines connecting each pair of communicating nodes. There are links.
CROSSBAR SWITCH
  Switch dedicated between each pair of nodes
  Each Ai can be connected to one Bj at any time
  Special cases:
    A = processors, B = memories
    A, B same type of node
    A, B same nodes (complete graph)
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Notes: How to connect things? Gross block diagrams (topologies). Examine
  LATENCY for n nodes;
  THRUPUT for n nodes;
  COST for n nodes.
Connect everything to everything: engineering overkill.
  n(n-1) links - each requires a wire plus 2 interfaces.
  O(n**2) cost;
  O(n) latency (assuming constant size links);
  O(n) msgs/sec thruput.
Be more systematic: 2D Crossbar
  ... still quadratic cost.

## Slide 22: Mesh Topologies
2-Dimensional Meshes
4-Neighbor
8-Neighbor
3-D, 6-Neighbor Mesh
Nearest-neighbor connectivity:
Point-to-point interconnect
- minimizes delays
- minimizes “analog” effects
Store-and-forward
(some overhead associated with communication routing)
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Notes: Reach O(k**2) nodes in k steps --
Latency for n=k**2 nodes is k.
Doesnt matter much what the local connectivity is; 4N, 8N about same.
NICE Property of 3D Mesh: can be implemented in 3D space!

## Slide 23: Logarithmic-latency Networks
BINARY TREE
HYPERCUBE
D dimensions → 2D nodes
Each node has D links
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Throughput | 
Latency | 
Cost | 
Notes: BINARY TREE: 3 ports/node.
Generalization of CUBE to arbitrarily many dimensions.

## Slide 24: Communication Technologies: Latency
Theorist's view:
  Each point-to-point link requires one hardware unit.
  Each point-to-point communication requires one time unit.
Topology | $ | Theoretical Latency | Actual Latency
Complete graph |  |  | 
Crossbar |  |  | 
1D Bus |  |  | 
2D Mesh |  |  | 
3D Mesh |  |  | 
Tree |  |  | 
N-cube |  |  | 
Topology | $ | Theoretical Latency | Actual Latency
Complete graph |  |  | 
Crossbar |  |  | 
1D Bus |  |  | 
2D Mesh |  |  | 
3D Mesh |  |  | 
Tree |  |  | 
N-cube |  |  | 
Topology | $ | Theoretical Latency | Actual Latency
Complete graph |  |  | 
Crossbar |  |  | 
1D Bus |  |  | 
2D Mesh |  |  | 
3D Mesh |  |  | 
Tree |  |  | 
N-cube |  |  | 
Topology | $ | Theoretical Latency | Actual Latency
Complete graph |  |  | 
Crossbar |  |  | 
1D Bus |  |  | 
2D Mesh |  |  | 
3D Mesh |  |  | 
Tree |  |  | 
N-cube |  |  | 
Engineer’s view:
  Loading increases with number of connections (bus, crossbar)
  Nodes have size: limits possible 2D, 3D density (other topologies)
Notes: OFTEN, topologies characterized by simple assumptions...
POPULAR HANGUP on worst-case latency!

## Slide 25: Communications Futures
Backplane buses have evolved into point-to-point links
  + links operate independently
  + links can be managed in groups
  + packetized data deals with errors
Specialized buses for memory
Networked “peripherals” for mobile devices…
New-generation communications...
  • how should 100 (1000?) cores communicate?
SATA
EISA
NuBus
PCI
SBUS
FireWire
DDR
SDRAM
USB