## Slide 1: Design Tradeoffs
Reducing power
Improving speed
Reducing area
Increasing throughput
Door #1: Performance
Door #2: Size
Door #3: Power

## Slide 2: Optimizing Your Design
There are a large number of implementations of the same functionality -- each represents a different point in the area-time-power space
Optimization metrics:
area
time
power
Area of the design
Throughput
Latency
Power consumption
Energy of executing a task
…
Justin14 (CC BY-SA 4.0)
©Advanced Micro Devices (with permission)
vs.
Notes: http://commons.wikimedia.org/wiki/File:White_AppleWatch_with_Screen.png
http://commons.wikimedia.org/wiki/File:ATI_Radeon_HD_4890_Graphics_Card.jpg

## Slide 3: CMOS Static Power Dissipation
MOSFET
1
2
1
Tunneling current through gate oxide: SiO2 is a very good insulator, but when very thin (< 20Å) electrons can tunnel across.
2
Current leakage from drain to source even though MOSFET is “off” (aka sub-threshold conduction)
  Leakage gets larger as difference between VTH and “off” gate voltage (eg, VOL in an nfet) gets smaller. Significant as VTH has become smaller.
  Fix: 3D FINFET wraps gate around inversion region
FINFET
Irene Ringworm (CC BY-SA 3.0)
Notes: http://commons.wikimedia.org/wiki/File:Doublegate_FinFET.PNG

## Slide 4: CMOS Dynamic Power Dissipation
VIN
C
VOUT
VIN moves from L to H to L
tCLK=1/fCLK
VOUT moves from H to L to H
C discharges and then recharges:
Power dissipated to discharge C:
Power dissipated to recharge C:

## Slide 5: CMOS Dynamic Power Dissipation
Power dissipated
= f C VDD2 per node = f N C VDD2 per chip
where f = frequency of charge/discharge N = number of changing nodes/chip
“Back of the envelope”:
f ~ 1GHz = 1e9 cycles/sec
N ~ 1e8 changing nodes/cycle
C ~ 1fF = 1e-15 farads/node
V ~ 1V
⇒ 100 Watts
trends
VIN
C
VOUT
VIN moves from L to H to L
VOUT moves from H to L to H
C discharges and then recharges:
tCLK=1/fCLK
Notes: https://openclipart.org/detail/83869/closed-envelope

## Slide 6: How Can We Reduce Power?
A[31:0]
B[31:0]
ALUFN[0]
Z
V
N
ALUFN[3:0]
add
boole
ALUFN[1:0]
shift
Z
V
N
cmp
ALUFN[2:1]
ALU[31:0]
ALUFN[5:4]
What if we could eliminate unnecessary transitions? When the output of a CMOS gate doesn’t change, the gate doesn’t dissipate much power!

## Slide 7: Fewer Transitions → Lower Power
A[31:0]
B[31:0]
ALUFN[0]
Z
V
N
ALUFN[3:0]
add
boole
ALUFN[1:0]
shift
Z
V
N
cmp
ALUFN[2:1]
ALU[31:0]
ALUFN[5:4]
D Q
G
D Q
G
D Q
G
ALUFN[5] == 0
ALUFN[5:4] == 10
ALUFN[5:4] == 11
Signals in this region make transitions only when ALU is doing a shift operation
Variations: Dynamically adjust tCLK or VDD (either overall or in specific regions) to accommodate workload.
Must computation consume energy? See §6.5 of Notes

## Slide 8: Improving Speed: Adder Example
Worse-case path: carry propagation from LSB to MSB, e.g., when adding 11…111 to 00…001.
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
An-1 Bn-1 An-2 Bn-2 A2 B2 A1 B1 A0 B0
Sn-1 Sn-2 S2 S1 S0
A B
CO CI
S
FA
A B
CO CI
S
FA
C
…
0
(N) is read “order N” and tells us that the latency of our adder grows in proportion to the number of bits in the operands.
 (N)
CI to CO
CIN-1 to SN-1
tPD = (N-1)*(tPD,NAND3 + tPD,NAND2) + tPD,XOR

## Slide 9: Performance/Cost Analysis
“Order Of” notation:
"g(n) is of order f(n)"
g(n) = Q(f(n))
g(n)=Q(f(n)) if there exist C2 ≥ C1 > 0 such that for all but finitely many integral n ≥ 0
Example: n2+2n+3 = Q(n2)
since n2 < n2+2n+3 < 2n2
“almost always”
Q(...) implies both inequalities; O(...) implies only the second.
g(n) = O(f(n))
Notes: We’ll see that this is a little
pessimistic...

## Slide 10: Carry Select Adders
Hmm. Can we get the high half of the adder working in parallel with the low half?
16-bit Adder
B[15:0]
A[15:0]
0
S[15:0]
16-bit Adder
B[31:16]
A[31:16]
0
1
16-bit Adder
1 0
S[31:16]
Two copies of the high half of the adder: one assumes a carry-in of “0”, the other carry-in of “1”.
Once the low half computes the actual value of the carry-in to the high half, use it select the correct version of the high-half addition.
Aha! Apply the same strategy to build 16-bit adders from 8-bit adders. And 8-bit adders from 4-bit adders, and so on. Resulting tPD for N-bit adder is (log N).
tPD = 16*tPD,CI→CO + tPD,MUX2 ≃ half of 32*tPD,CI→CO

## Slide 11: 32-bit Carry Select Adder
COUT SUM
COUT SUM
COUT SUM
S[4:0]
S[11:5]
S[20:12]
COUT,S[31:21]
B[4:0]
A[4:0]
B[11:5]
A[11:5]
B[20:12]
A[20:12]
B[31:21]
A[31:21]
Practical Carry-select addition: choose block sizes so that trial sums and carry-in from previous stage arrive simultaneously at MUX.
Select input is heavily loaded, so buffer for speed.
Design goal: have these two sets of signals arrive simultaneously at each carry-select mux

## Slide 12: Wanted: Faster Carry Logic!
Let’s see if we can improve the speed by rewriting the equations for COUT:
COUT = AB + ACIN + BCIN
= AB + (A + B)CIN
= G + P CIN
where G = AB and P = A + B
generate
propagate
Actually, P is usually defined as P = AB which won’t change COUT but will allow us to express S as a simple function of P and CIN: S = P  CIN
CO logic using only 3 NAND2 gates! Think I’ll borrow that for my FA circuit!
CI
A B
S
CO
G P

## Slide 13: Carry Look-ahead Adders (CLA)
We can build a hierarchical carry chain by generalizing our definition of the Carry Generate/Propagate (GP) Logic. We start by dividing our addend into two parts, a higher part, H, and a lower part, L. The GP function can be expressed as follows:
GHL = GH + PH GL
PHL = PH PL
Generate a carry out if the high part generates one, or if the low part generates one and the high part propagates it. Propagate a carry if both the high and low parts propagate theirs.
Hierarchical building block
P/G generation
1st level of
lookahead
GH PH
GHL PHL
GP
GL
PL
A B
CO CI
G P S
FA
GH PH
GHL PHL
GP
GL
PL
A B
CO CI
G P S
FA
H
L

## Slide 14: 8-bit CLA (generate G & P)
Q(log N)
GH PH GL
GHL PHL PL
GP
A B CO CI
G P S
FA
A B CO CI
G P S
FA
GH PH GL
GHL PHL PL
GP
GH PH GL
GHL PHL PL
GP
A B CO CI
G P S
FA
A B CO CI
G P S
FA
GH PH GL
GHL PHL PL
GP
GH PH GL
GHL PHL PL
GP
A B CO CI
G P S
FA
A B CO CI
G P S
FA
GH PH GL
GHL PHL PL
GP
GH PH GL
GHL PHL PL
GP
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A7 B7 A6 B6 A5 B5 A4 B4 A3 B3 A2 B2 A1 B1 A0 B0
We can build a tree of GP units to compute the generate and propagate logic for any sized adder. Assuming N is a power of 2, we’ll need N-1 GP units.
This will let us to quickly compute the carry-ins for each FA!
G7-0 P7-0
G3-0 P3-0
G1-0 P1-0
G3-2 P3-2
G7-4 P7-4
G5-4 P5-4
G7-6 P7-6

## Slide 15: 8-bit CLA (carry generation)
Q(log N)
Now, given a the value of the carry-in of the least-significant bit,we can generate the carries for every adder.
cH = GL + PLcin cL = cin
cH
cin
cL
GL
PL
cH
cin
cL
GL
PL
cH
cin
cL
GL
PL
cH
cin
cL
GL
PL
cH
cin
cL
GL
PL
cH
cin
cL
GL
PL
cH
cin
cL
GL
PL
C7 C6 C5 C4 C3 C2 C1 C0
C6 C4 C2 C0
C4 C0
C0
G3-0
P3-0
G1-0
P1-0
G5-4
P5-4
G6
P6
G4
P4
G2
P2
G0
P0
C
C
C
C
C
C
C
C4 = G3-0+P3-0 C0
C6 = G5-4+P5-4 C4
Notice that the inputs on the left of each C blocks are the same as the inputs on the right of each corresponding GP block.

## Slide 16: 8-bit CLA (complete)
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A B CO CI
G P S
FA
A7 B7 A6 B6 A5 B5 A4 B4 A3 B3 A2 B2 A1 B1 A0 B0
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
GH PH Cj
GL
PL
Ci
GP/C
GHL PHL Ci
tPD = (log N)
GH PH
GHL PHL
GP
GL
PL
cH
ci
cL
GL
PL
C
+
=
GH PH CH
GHL PHL Cin
GP/C
GL
PL
CL
CI
A B
S
CO
G P
Notice that we don’t need the carry-out output of the adder any more.
C0
To learn more, look up Kogge-Stone adders on Wikipedia.

## Slide 17: Binary Multiplication*
A0
A1
A2
A3
B0
B1
B2
B3
A0B0
A1B0
A2B0
A3B0
A0B1
A1B1
A2B1
A3B1
A0B2
A1B2
A2B2
A3B2
A0B3
A1B3
A2B3
A3B3
x
+
ABi called a “partial product”
Multiplying N-digit number by M-digit number gives (N+M)-digit result
Easy part: forming partial products (just an AND gate since BI is either 0 or 1)
Hard part: adding M N-bit partial products
1
0
1
0
0
0
1
0

The “Binary” Multiplication Table
* Actually unsigned binary multiplication
Hey, that looks like an AND gate

## Slide 18: Combinational Multiplier
HA
FA
FA
FA
FA
HA
FA
HA
HA
FA
FA
FA
a3
a2
a1
a0
z0
z1
z2
z3
z4
z5
z6
z7
b3
b2
b1
b0
CO
A B
S
a3
a2
a1
a0
a3
a2
a1
a0
a3
a2
a1
a0
CI
A B
S
CO
FA
HA
Latency = (N)
Throughput = (1/N)
Hardware = (N2)

## Slide 19: 2’s Complement Multiplication
X3 X2 X1 X0
* Y3 Y2 Y1 Y0
--------------------
X3Y0 X3Y0 X3Y0 X3Y0 X3Y0 X2Y0 X1Y0 X0Y0
+ X3Y1 X3Y1 X3Y1 X3Y1 X2Y1 X1Y1 X0Y1
+ X3Y2 X3Y2 X3Y2 X2Y2 X1Y2 X0Y2
- X3Y3 X3Y3 X2Y3 X1Y3 X0Y3
-----------------------------------------
Z7 Z6 Z5 Z4 Z3 Z2 Z1 Z0
X3Y0 X2Y0 X1Y0 X0Y0
+ X3Y1 X2Y1 X1Y1 X0Y1
+ X3Y2 X2Y2 X1Y2 X0Y2
+ X3Y3 X2Y3 X1Y3 X0Y3
+ 1 1
Step 1: two’s complement operands so high order bit is –2N-1. Must sign extend partial products and subtract the last one
Step 2: don’t want all those extra additions, so add a carefully chosen constant, remembering to subtract it at the end. Convert subtraction into add of (complement + 1).
Step 3: add the ones to the partial products and propagate the carries. All the sign extension bits go away!
Step 4: finish computing the constants…
Result: multiplying 2’s complement operands takes just about same amount of hardware as multiplying unsigned operands!
X3Y0 X2Y0 X1Y0 X0Y0
+ X3Y1 X2Y1 X1Y1 X0Y1
+ X3Y2 X2Y2 X1Y2 X0Y2
+ X3Y3 X2Y3 X1Y3 X0Y3
+ 1
- 1 1 1 1
X3Y0 X3Y0 X3Y0 X3Y0 X3Y0 X2Y0 X1Y0 X0Y0
+ 1
+ X3Y1 X3Y1 X3Y1 X3Y1 X2Y1 X1Y1 X0Y1
+ 1
+ X3Y2 X3Y2 X3Y2 X2Y2 X1Y2 X0Y2
+ 1
+ X3Y3 X3Y3 X2Y3 X1Y3 X0Y3
+ 1
+ 1
- 1 1 1 1
–B = ~B + 1

## Slide 20: 2’s Complement Multiplier
FA
FA
FA
FA
FA
HA
FA
HA
HA
FA
FA
FA
a3
a2
a1
a0
z0
z1
z2
z3
z4
z5
z6
z7
b3
b2
b1
b0
a3
a2
a1
a0
a3
a2
a1
a0
a3
a2
a1
a0
HA
1
1

## Slide 21: Increase Throughput With Pipelining
HA
FA
FA
FA
FA
HA
FA
HA
HA
FA
FA
FA
a3
a2
a1
a0
z0
z1
z2
z3
z4
z5
z6
z7
b3
b2
b1
b0
a3
a2
a1
a0
a3
a2
a1
a0
a3
a2
a1
a0
Before pipelining: Throughput = ~1/(2N) = (1/N)
After pipelining: Throughput = ~1/N = (1/N)
gotta break
that long
carry chain!

## Slide 22: “Carry-save” Pipelined Multiplier
Observation: Rather than propagating the carries to the next column, they can instead be forwarded onto the next column of the following row
FA
FA
HA
FA
FA
HA
FA
HA
FA
a3
a2
a1
a0
z0
z1
z2
z3
z4
z5
z6
z7
b3
b2
b1
b0
a3
a2
a1
a0
a3
a2
a1
a0
a3
a2
a1
a0
HA
HA
HA
HA
HA
FA
Latency = (N)
Throughput = (1)
Hardware = (N2)

## Slide 23: Reduce Area With Sequential Logic
Assume the multiplicand (A) has N bits and the multiplier (B) has M bits. If we only want to invest in a single N-bit adder, we can build a sequential circuit that processes a single partial product at a time and then cycle the circuit M times:
A
P
B
+
SN
NC
N
xN
N
N+1
SN-1…S0
Init: P0, load A&B
Repeat M times {
P  P + (BLSB==1 ? A : 0)
shift SN,P,B right one bit
}
Done: (N+M)-bit result in P,B
M bits
LSB
1
TPD = (1) for carry-save (see previous slide), but adds (N) cycles & (N) hardware
Latency = (N)
Throughput = (1/N)
Hardware = (N)
N+1 Sum bits and N saved carries
Carry-save

## Slide 24: Summary
Power dissipation can be controlled by dynamically varying TCLK, VDD or by selectively eliminating unnecessary transitions.
Functions with N inputs have minimum latency of O(log N) if output depends on all the inputs. But it can take some doing to find an implementation that achieves this bound.
Performing operations in “slices” is a good way to reduce hardware costs (but latency increases)
Pipelining can increase throughput (but latency increases)
Asymptotic analysis only gets you so far – factors of 10 matter in real life and typically N isn’t a parameter that’s changing within a given design.